31 July 2009

Candidate Standard 5100.9-2009

The Printer Working Group

Internet Printing Protocol (IPP)

Printer State Extensions v1.0

Status: Approved

Abstract:  This document defines the new IPP Printer attributes "printer-alert" and "printer-alert-description" plus extensions to the IPP Printer attribute "printer-state-reasons" (defined in RFC 2911) and to the IANA Printer MIB textual convention "PrtAlertCodeTC" (originally published in RFC 3805) as follows:

(a) A standard encoding of all of the machine-readable columnar objects in the 'prtAlertTable' defined in IETF Printer MIB v2 (RFC 3805) into substrings of values of the new IPP Printer "printer-alert" attribute defined in this document.

(b) A standard encoding of the localized 'prtAlertDescription' columnar object in the 'prtAlertTable' defined in IETF Printer MIB v2 (RFC 3805) into values of the new IPP Printer "printer-alert-description" attribute defined in this document.

(c) A standard mapping between the device errors and warnings in the 'PrtAlertCodeTC' textual convention defined in IANA Printer MIB and existing or new values (as needed) of the IPP Printer "printer-state-reasons" attribute defined in IPP/1.1.

(d) A standard mapping between the finishing subunit types in the 'FinDeviceTypeTC' textual convention defined in IANA Finisher MIB (originally published in RFC 3806) and new specific values of the 'PrtAlertCodeTC' textual convention defined in IANA Printer MIB and new values of the IPP Printer "printer-state-reasons" attribute defined in IPP/1.1, for high fidelity support of finishing alerts.

This document is a PWG Candidate Standard. For a definition of a “PWG Candidate Standard”, see

ftp://ftp.pwg.org/pub/pwg/general/process/pwg-process30.pdf

This document is available electronically at:

ftp://ftp.pwg.org/pub/pwg/candidates/cs-ippstate10-20090731-5100.9.pdf

Copyright © 2009, The Printer Working Group. All rights reserved.

This document may be copied and furnished to others, and derivative works that comment on, or otherwise explain it or assist in its implementation may be prepared, copied, published and distributed, in whole or in part, without restriction of any kind, provided that the above copyright notice, this paragraph and the title of the Document as referenced below are included on all such copies and derivative works.  However, this document itself may not be modified in any way, such as by removing the copyright notice or references to the Printer Working Group, a program of the IEEE-ISTO.

Title:  Internet Printing Protocol (IPP)/ Printer State Extensions v1.0

The IEEE-ISTO and the Printer Working Group DISCLAIM ANY AND ALL WARRANTIES, WHETHER EXPRESS OR IMPLIED INCLUDING (WITHOUT LIMITATION) ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

The Printer Working Group, a program of the IEEE-ISTO, reserves the right to make changes to the document without further notice.  The document may be updated, replaced or made obsolete by other documents at any time.

The IEEE-ISTO and the Printer Working Group, a program of the IEEE-ISTO take no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights.

The IEEE-ISTO and the Printer Working Group, a program of the IEEE-ISTO invite any interested party to bring to its attention any copyrights, patents, or patent applications, or other proprietary rights, which may cover technology that may be required to implement the contents of this document. The IEEE-ISTO and its programs shall not be responsible for identifying patents for which a license may be required by a document and/or IEEE-ISTO Industry Group Standard or for conducting inquiries into the legal validity or scope of those patents that are brought to its attention. Inquiries may be submitted to the IEEE-ISTO by e-mail at:

info@ieee-isto.org

The Printer Working Group acknowledges that the IEEE-ISTO (acting itself or through its designees) is, and shall at all times, be the sole entity that may authorize the use of certification marks, trademarks, or other special designations to indicate compliance with these materials.

Use of this document is wholly voluntary.  The existence of this document does not imply that there are no other ways to produce, test, measure, purchase, market, or provide other goods and services related to its scope.

About the IEEE-ISTO

The IEEE-ISTO is a not-for-profit corporation offering industry groups an innovative and flexible operational forum and support services. The IEEE Industry Standards and Technology Organization member organizations include printer manufacturers, print server developers, operating system providers, network operating systems providers, network connectivity vendors, and print management application developers. The IEEE-ISTO provides a forum not only to develop standards, but also to facilitate activities that support the implementation and acceptance of standards in the marketplace.  The organization is affiliated with the IEEE (http://www.ieee.org/) and the IEEE Standards Association (http://standards.ieee.org/ ).

For additional information regarding the IEEE-ISTO and its industry programs visit:             http://www.ieee-isto.org.

About the Printer Working Group

The Printer Working Group (or PWG) is a Program of the IEEE-ISTO. All references to the PWG in this document implicitly mean “The Printer Working Group, a Program of the IEEE ISTO.”  The PWG is chartered to make printers and the applications and operating systems supporting them work together better. In order to meet this objective, the PWG will document the results of their work as open standards that define print related protocols, interfaces, data models, procedures and conventions. Printer manufacturers and vendors of printer related software would benefit from the interoperability provided by voluntary conformance to these standards.

In general, a PWG standard is a specification that is stable, well understood, and is technically competent, has multiple, independent and interoperable implementations with substantial operational experience, and enjoys significant public support.

Contact information:

The Printer Working Group

c/o The IEEE Industry Standards and Technology Organization

445 Hoes Lane

Piscataway, NJ 08854

USA

IPP Web Page:

http://www.pwg.org/ipp

IPP Mailing List:

ipp@pwg.org

Instructions for subscribing to the IPP mailing list can be found at the following link:

http://www.pwg.org/mailhelp.html

Members of the PWG and interested parties are encouraged to join the PWG and IPP WG mailing lists in order to participate in discussions, clarifications and review of the IPP Working Group product.

Table of Contents

Internet Printing Protocol (IPP)	1

Printer State Extensions v1.0	1

Table of Contents	4

Table of Figures	5

List of Tables	5

1	Introduction	6

1.1	Scope	6

1.2	Problem Statement	6

2	Terminology	7

2.1	Conformance Terminology	7

2.2	Printing Terminology	7

3	Industry Standard Printing Model	8

3.1	Standard Model - ISO DPA	8

3.2	Print Device - Printer MIB	8

3.3	Print Service and Print Device - IPP	10

4	Requirements	12

4.1	Rationale for IPP PSX	12

4.2	Use Models for IPP PSX	14

4.2.1	Service Providers - Monitoring	14

4.2.2	System Administrators - Network Management	14

4.2.3	System Operators - Monitoring	14

4.3	Design Requirements for IPP PSX	15

5	IPP Printer Attributes	16

5.1	printer-state-reasons (1setOf type2 keyword)	16

5.1.1	Severity Suffixes Interoperability	16

5.1.2	Existing Printer State Reasons for Alert Codes	17

5.1.3	New Printer State Reasons for Alert Codes	20

5.1.4	New PrinterState Reasons for Finishing Subunits	22

5.2	printer-alert (1setOf octetString(MAX))	23

5.2.1	Keywords for Alert Objects	23

5.2.2	Printer Alert Encoding of Alert Objects	25

5.3	printer-alert-description (1setOf text(MAX))	27

5.3.1	Printer Alert Description Encoding	27

5.3.2	Example of Printer Alert Description	27

6	IANA Printer MIB Textual Conventions	28

6.1	PrtAlertCodeTC	28

6.1.1	New Alert Codes for Finishing Subunits	28

6.1.2	Conventions for Alert Code Numbering	40

7	Conformance Requirements	41

7.1	IPP Printer Conformance Requirements	41

7.2	IPP Client Conformance Requirements	41

7.3	Printer MIB Agent Conformance Requirements	42

7.4	Printer MIB Client Conformance Requirements	42

8	IANA Considerations	43

8.1	IPP Attributes and Keyword Values Registrations	43

8.2	IANA Printer MIB Alert Values Registrations	56

9	Internationalization Considerations	68

10	Security Considerations	68

11	Acknowledgements	68

12	References	69

12.1	Normative References	69

12.2	Informative References	70

13	Editors’ Addresses	71

14	Appendix A - Design Alternatives (Informative)	72

14.1	Printer Alert Encoding in Collection Attribute	72

14.1.1	Rationale for Rejection	72

14.2	Printer Alert Encoding in New Object	72

14.2.1	Rationale for Rejection	72

14.3	Printer Alert Encoding in Parallel Attributes	72

14.3.1	Rationale for Rejection	72

14.4	Printer Alert Encoding in State Message	73

14.4.1	Rationale for Rejection	73

14.5	Printer Alert Group Finishing Extensions	73

14.5.1	Rationale for Rejection	73

14.6	Printer Alert Subset for Finishing Subunits	73

14.6.1	Rationale for Rejection	73

Table of Figures

Figure 1 - Printer Block Diagram	9

Figure 2 - Simplified Printing Model	10

Figure 3 - Simplified Print Service and Print Device	11

Figure 4 - ABNF for IPP printer-alert	25

Figure 5 - Example of IPP printer-alert	26

Figure 6 - Example of IPP printer-alert-description	27

List of Tables

Table 5-1 - Existing Printer State Reasons for Alert Codes	17

Table 5-2 - New Printer State Reasons for Alert Codes	20

Table 5-3 - Keywords for Alert Objects	23

Table 6-1 - New Alert Codes for Finishing Subunits	28

Table 8-1 - IPP Attributes and Keyword Values for IANA	43

Table 8-2 - IANA Printer MIB Alert Values for IANA	56

# Introduction

## Scope

This document defines two new IPP Printer attributes "printer-alert" and "printer-alert-description" plus extensions to the IPP Printer attribute "printer-state-reasons" (defined in RFC 2911) and to the IANA Printer MIB textual convention "PrtAlertCodeTC" (originally published in RFC 3805) as follows:

- A standard encoding of all of the machine-readable columnar objects in the 'prtAlertTable' defined in IETF Printer MIB v2 (RFC 3805) into substrings of values of the new IPP Printer "printer-alert" attribute defined in this document.

- A standard encoding of the localized 'prtAlertDescription' columnar object in the 'prtAlertTable' defined in IETF Printer MIB v2 (RFC 3805) into values of the new IPP Printer "printer-alert-description" attribute defined in this document.

- A standard mapping between the device errors and warnings in the 'PrtAlertCodeTC' textual convention defined in IANA Printer MIB and existing or new values (as needed) of the IPP Printer "printer-state-reasons" attribute defined in IPP/1.1.

- A standard mapping between the finishing subunit types in the 'FinDeviceTypeTC' textual convention defined in IANA Finisher MIB (originally published in RFC 3806) and new specific values of the 'PrtAlertCodeTC' textual convention defined in IANA Printer MIB and new values of the IPP Printer "printer-state-reasons" attribute defined in IPP/1.1, for high fidelity support of finishing alerts.

## Problem Statement

When deploying printers in enterprise networks, customers often disable SNMPv1 (RFC 1157), based on local security policy - and secure SNMPv3 (RFC 3414) is not widely supported by current printers. Therefore, alternative support for secure queries for printer device alerts is required to manage, provision, and service these non-SNMP network printers. IPP/1.1 (RFC 2911) can be securely deployed in enterprise networks, using TLS/1.0 (RFC 2246) and HTTP/1.1 Upgrade (RFC 2817), so an IPP solution to this requirement is attractive.

The IPP "printer-state-reasons" attribute was defined in IPP/1.1 (RFC 2911), but the mapping of printer device alerts from the 'prtAlertCode' object defined in Printer MIB v1/v2 (RFC 1759/3805) was very sparse.

# Terminology

## Conformance Terminology

The key words "MUST", "MUST NOT", "REQUIRED", "SHOULD", "SHOULD NOT", "RECOMMENDED", "MAY", and "OPTIONAL" in this document are to be interpreted as defined in [RFC2119].

## Printing Terminology

Normative definitions and semantics of printing terms are imported from IETF Printer MIB v2 [RFC3805], IETF Finisher MIB [RFC3806], and IETF IPP/1.1 [RFC2911].

This document also defines the following protocol roles in order to specify unambiguous conformance requirements:

IPP Client - Initiator of outgoing IPP session requests and sender of outgoing IPP operation requests (HTTP/1.0 Client [RFC1957] / HTTP/1.1 Client [RFC2616]).

IPP Printer - Listener for incoming IPP session requests and receiver of incoming IPP operation requests (HTTP/1.0 Server [RFC1957] / HTTP/1.1 Server [RFC2616]).

Printer MIB Agent - Receiver of incoming SNMP operation requests (SNMPv1 Agent [RFC1157] / SNMPv3 Command Responder [RFC3411]).

Printer MIB Client - Sender of outgoing SNMP operation requests (SNMPv1 Manager [RFC1157] / SNMPv3 Command Generator [RFC3411]).

# Industry Standard Printing Model

## Standard Model - ISO DPA

The industry standard printing model was first defined during the development of ISO Document Printing Application (DPA) [ISO10175]. All subsequent open printing standards refer extensively to ISO DPA for the semantics of printing attributes.

WARNING: In ISO DPA, the abstract Printer object has two distinct 'realizations', to whit, Physical Printer (device) and Logical Printer (service). As a result, the term 'Printer' was used to mean a Physical Print Device in the IETF Printer MIB v1/v2 [RFC1759] [RFC3805] and later ambiguously used to mean _either_ a Logical Print Service or a Physical Print Device in IETF IPP/1.1 [RFC2911].

## Print Device - Printer MIB

The Print Device was first described in the IETF Host Resources MIB v1 [RFC1514] (September 1993) which defined the 'hrDevicePrinter' OID value for the 'hrDeviceType' element of the 'hrDeviceTable' and defined the 'hrPrinterTable' containing the 'hrPrinterStatus' (enumeration) and 'hrPrinterDetectedErrorState' (bit-mask) elements.

The industry standard Print Device model was later defined in section 2 of the IETF Printer MIB v1 [RFC1759] (March 1995) and is preserved without change in the IETF Printer MIB v2 [RFC3805] (June 2004). The block diagram is excerpted below.

Physical Connections

|

+-----------+

|           |

+-------------+ |

|  Interface  |-+

|    MIB-II   |

+-------------+

|

+-----------+

|           |

+-------------+ |    +-----------+

| Channel     |-+    | Operator  |

|             |      |  Console  |

+-------------+      +-----------+

|

+-----------+        +---------+

|           |        |         |

+-----------+       +-------------+ |    +-----------+ |

|  General  |       | Interpreter |-+    |  Alerts   |-+

|  Printer  |       |             |      |           |

+-----------+       +-------------+      +-----------+

|

+-------------------------------+

|        System Controller      |

|        HOST-RESOURCES-MIB     |

+-------------------------------+

+------+                    +--------+                  +--------+

|      |                    |        |                  |        |

+-------+ |    +-------+    +---------+ |    +-------+   +--------+ |

| Input |-+  +--------+|    |  Marker |-+  +--------+|   | Output |-+

|       |===>|        |+<==>|         |<==>|        |+==>|        |

+-------+    +--+  +--+     +---------+    +--+  +--+    +--------+

\            |  ||                         |  ||         \

\           |  ||                         |  ||          \

\          |  ||                         |  ||           \

+--------+  |  |+-------------------------|  ||         +---------+

|        |  |  +--------------------------+  ||         |         |

+----------+ |  |            Media Path          |+      +----------+ |

|  Media   |-+  +--------------------------------+       | Finisher |-+

|(optional)|                                             |(optional)|

+----------+                                             +----------+

Figure 1 - Printer Block Diagram

## Print Service and Print Device - IPP

A simplified printing model was defined in section 1.1 of IETF IPP/1.1 [RFC2911], based on ISO DPA [ISO10175]. The block diagram is excerpted below.

+--------------+

|  Application |

o         +. . . . . . . |

\|/        |   Spooler    |

/ \        +. . . . . . . |   +---------+

End-User     | Print Driver |---|  File   |

+-----------+ +-----+  +------+-------+   +----+----+

|  Browser  | | GUI |         |                |

+-----+-----+ +--+--+         |                |

|          |            |                |

|      +---+------------+---+            |

N   D   S   |      |      IPP Client    |------------+

O   I   E   |      +---------+----------+

T   R   C   |                |

I   E   U   |

F   C   R   -------------- Transport ------------------

I   T   I

C   O   T                    |         --+

A   R   Y           +--------+--------+  |

T   Y               |    IPP Server   |  |

I                   +--------+--------+  |

O                            |           |

N                   +-----------------+  | IPP Printer

|  Print Service  |  |

+-----------------+  |

|         --+

+-----------------+

| Output Device(s)|

+-----------------+

Figure 2 - Simplified Printing Model

A simplified Print Service model and Print Device model was defined in section 2.1 of IETF IPP/1.1 [RFC2911], based on the logical and physical 'realizations' of the Printer object originally defined in ISO DPA [ISO10175]. The term Printer was ambiguously used to mean _either_ a Logical Print Service or a Physical Print Device in IETF IPP/1.1 [RFC2911]. The block diagrams are excerpted below.

Legend:

##### indicates a Printer object which is

either embedded in an output device or is

hosted in a server.  The Printer object

might or might not be capable of queuing/spooling.

any   indicates any network protocol or direct

connect, including IPP

embedded printer:

output device

+---------------+

O   +--------+                         |  ###########  |

/|\  | client |------------IPP------------># Printer #  |

/ \  +--------+                         |  # Object  #  |

|  ###########  |

+---------------+

hosted printer:

+---------------+

O   +--------+        ###########      |               |

/|\  | client |--IPP--># Printer #-any->| output device |

/ \  +--------+        # Object  #      |               |

###########      +---------------+

+---------------+

fan out:                                 |               |

+-->| output device |

any/    |               |

O   +--------+      ###########   /     +---------------+

/|\  | client |-IPP-># Printer #--*

/ \  +--------+      # Object  #   \     +---------------+

########### any\    |               |

+-->| output device |

|               |

+---------------+

Figure 3 - Simplified Print Service and Print Device

# Requirements

Per the PWG Process, this section specifies the formal rationale for developing an IPP Printer State Extensions (PSX) specification, based on existing printing industry standards. This section also describes simple use models for IPP PSX environments.

## Rationale for IPP PSX

IETF and PWG standards for the printing industry define:

- A rationale for an abstract model of printing (to support alternate encodings and protocols) in section 3 of the IETF IPP Rationale [RFC2568].

- A set of design goals for status monitoring in a printing protocol in section 3.1.3 'Viewing the status and capabilities of a printer' (for End User), section 3.2.1 'Alerting' (for Operator), and section 3.3 'Administrator' (the bullet requirement to 'administrate billing or other charge-back mechanisms') of the IETF IPP Design Goals [RFC2567].

- An abstract model of a Print Service (i.e., ISO DPA Logical Printer) and a Print Device (i.e., ISO DPA Physical Printer) in section 2.1 of IETF IPP/1.1 [RFC2911].

- A partial set of Print Device alerts in the "printer-state-reasons" attribute in section 4.4.12 of IETF IPP/1.1 [RFC2911].

- An abstract model of a Print Device and contained Subunits in section 2.2 of the IETF Printer MIB v2 [RFC3805].

- A set of Print Device and Subunit types in the 'PrtAlertGroupTC' textual convention in IANA Printer MIB [IANAPRT], originally published in section 5 of the IETF Printer MIB v2 [RFC3805].

- A set of Print Device and Subunit alerts in the 'PrtAlertCodeTC' textual convention in IANA Printer MIB [IANAPRT], originally published in section 5 of the IETF Printer MIB v2 [RFC3805].

- An abstract model of Finishing Subunits integrated into the Printer Model (from [RFC3805]) in section 3 of the IETF Finisher MIB [RFC3806].

- A set of Finishing Subunit types in the 'FinDeviceTypeTC' textual convention in IANA Finisher MIB [IANAFIN], originally published in section 7 of the IETF Finisher MIB [RFC3806].

When deploying printers in enterprise networks, customers often disable SNMPv1 (RFC 1157), based on local security policy - and secure SNMPv3 (RFC 3414) is not widely supported by current printers.

Therefore an IPP PSX specification SHOULD:

a) Standardize non-SNMP alternative support for secure queries for network printer device alerts;

b)	Standardize capabilities to manage, provision, and service these non-SNMP network printers;

c)	Encourage adoption of modern IPP-based printing infrastructures.

The IPP "printer-state-reasons" attribute was defined in IPP/1.1 (RFC 2911), but the mapping of printer device alerts from the 'prtAlertCode' object defined in Printer MIB v1/v2 (RFC 1759/3805) was very sparse.

To support monitoring, maintenance, and administration of these network printers, this document defines:

(1) New enumerated values of the "PrtAlertCodeTC" textual convention for alerts for every Finishing Subunit type in the 'FinDeviceTypeTC' textual convention, for high fidelity alert mapping.

(2) New keyword values for the "printer-state-reasons" attribute to complete the mapping for every Print Device and Subunit alert in the 'PrtAlertCodeTC' textual convention.

(3) New keyword values for the new "printer-alert" attribute to encode all of the machine-readable columnar objects in 'prtAlertTable', for high fidelity alert mapping.

(4) A new "printer-alert-description" attribute to encode the localized 'prtAlertDescription' object in 'prtAlertTable', to complete the Printer MIB to IPP Printer mapping.

## Use Models for IPP PSX

### Service Providers - Monitoring

Outside service providers may lease and maintain network printers in remote customer enterprise networks in different administrative domains.

Note: Typically monitoring proxies within customer enterprise networks are required for scalability of this use model. However, the deployment of monitoring proxies and of security credentials is outside the scope of this document.

- To support reordering of supplies, outside service providers may read Device and Subunit alerts in "printer-state-reasons" from network printers that support IPP/1.1 (e.g., every day).

- To support preventive maintenance, outside service providers may read Device and Subunit alerts in "printer-state-reasons" from network printers that support IPP/1.1 (e.g., every hour).

- To support downtime guarantees, outside service providers may periodically read Device and Subunit alerts in "printer-state-reasons" from network printers that support IPP/1.1 (e.g., every 10 minutes).

### System Administrators - Network Management

Network system administrators configure and manage Print Devices in local enterprise networks.

- To support network management, network system administrators may subscribe to Print Device events from network printers that support IPP/1.1.

- To support preventive maintenance, network system administrators may read Device and Subunit alerts in "printer-state-reasons" from network printers that support IPP/1.1 (e.g., every hour).

- To support emergency maintenance, network system administrators may read Device and Subunit alerts in "printer-state-reasons", especially configuration changes and critical alerts, from network printers that support IPP/1.1 (e.g., every 10 minutes).

### System Operators - Monitoring

Network system operators monitor Print Devices and manage Print Jobs in local enterprise networks.

- To support Print Job management, network system operators may subscribe to Print Device and Print Job events from network printers that support IPP/1.1.

- To support Print Device monitoring, network system operators may read Device and Subunit alerts in "printer-state-reasons", especially for low or empty supplies, from network printers that support IPP/1.1 (e.g., every hour).

- To support Print Device availability, network system operators may read Device and Subunit alerts in "printer-state-reasons", especially for paper jams and other simple alerts, from network printers that support IPP/1.1 (e.g., every 10 minutes).

## Design Requirements for IPP PSX

(1) The IPP PSX design MUST follow the naming conventions defined in IETF IPP/1.1 [RFC2911], including keyword value case (lower) and hyphenation requirements.

(2) The IPP PSX design MUST define a complete mapping between Print Device and Subunit existing values of 'PrtAlertCodeTC' in IANA Printer MIB [IANAPRT] and existing values or new values (as needed) of "printer-state-reasons".

(3) The IPP PSX design MUST define Finishing Subunit-specific new values of 'PrtAlertCodeTC' for registration in IANA Printer MIB [IANAPRT] for every value of 'FinDeviceTypeTC' in IANA Finisher MIB [IANAFIN].

(4) The IPP PSX design MUST define a standard encoding for all of the machine-readable columnar objects defined in the 'prtAlertTable' in IETF Printer MIB v2 (RFC 3805) as substrings of values of a new "printer-alert" attribute.

(5) The IPP PSX design MUST define a standard encoding for the localized 'prtAlertDescription' columnar object defined in the 'prtAlertTable' in IETF Printer MIB v2 (RFC 3805) as text values of a new "printer-alert-description" attribute.

# IPP Printer Attributes

## printer-state-reasons (1setOf type2 keyword)

This section defines clarifications and extensions for the existing multi-valued IPP Printer "printer-state-reasons" attribute originally specified in IETF IPP/1.1 [RFC2911]. This IPP Printer attribute is REQUIRED for implementations that conform to this specification.  Specific values and mappings to/from the IETF Printer MIB v2 [RFC3805] are defined in detail below.

### Severity Suffixes Interoperability

The severity suffixes ('-report', '-error', and '-warning') for values of the existing IPP Printer "printer-state-reasons" attribute are defined in section 4.4.12 of [RFC2911].These values have NOT been IANA-registered because:

1) They are not valid for the attribute syntax ‘keyword’ defined in section 4.1.3 of [RFC2911].

2) They are structurally incompatibile with the IANA IPP Registry [IANAIPP] as defined in section 6 of [RFC2911].

#### Conformance

- For interoperability, IPP implementations that claim conformance to this specification SHOULD implement special-case parsing and validation for the severity suffixes for "printer-state-reasons" defined in [RFC2911].

### Existing Printer State Reasons for Alert Codes

The table below shows existing values of "printer-state-reasons" [RFC2911] and their mapping from existing values of 'PrtAlertCodeTC' [IANAPRT].

Deprecated Mappings: Existing values of "printer-state-reasons" in Table 5-1 that are enclosed in parentheses are DEPRECATED because they define non-unique mappings and SHOULD NOT be implemented. Instead, the new specific mappings defined in Table 5-2 SHOULD be implemented.

Table 5-1 - Existing Printer State Reasons for Alert Codes

PrtAlertCodeTC                          printer-state-reasons

-- RFC 1759 Generic codes

other(1)                                other

unknown(2)

coverOpen(3)                            cover-open

coverClosed(4)

interlockOpen(5)                        interlock-open

interlockClosed(6)

configurationChange(7)

jam(8)                                  media-jam

-- RFC 3805 Generic codes

subunitMissing(9)

subunitLifeAlmostOver(10)

subunitLifeOver(11)

subunitAlmostEmpty(12)

subunitEmpty(13)

subunitAlmostFull(14)

subunitFull(15)

subunitNearLimit(16)

subunitAtLimit(17)

subunitOpened(18)

subunitClosed(19)

subunitTurnedOn(20)

subunitTurnedOff(21)

subunitOffline(22)

subunitPowerSaver(23)

subunitWarmingUp(24)

subunitAdded(25)

subunitRemoved(26)

subunitResourceAdded(27)

subunitResourceRemoved(28)

subunitRecoverableFailure(29)

subunitUnrecoverableFailure(30)

subunitRecoverableStorageError(31)

subunitUnrecoverableStorageError(32)

subunitMotorFailure(33)

subunitMemoryExhausted(34)

subunitUnderTemperature(35)

subunitOverTemperature(36)

subunitTimingFailure(37)

subunitThermistorFailure(38)

-- General Printer Group

doorOpen(501)                           (door-open)

-- DEPRECATED -- use coverOpen(3)

doorClosed(502)

-- DEPRECATED -- use coverClosed(4)

powerUp(503)

powerDown(504)                          (shutdown)

printerNMSReset(505)

printerManualReset(506)

printerReadyToPrint(507)

-- Input Group

inputMediaTrayMissing(801)              input-tray-missing

inputMediaSizeChange(802)

inputMediaWeightChange(803)

inputMediaTypeChange(804)

inputMediaColorChange(805)

inputMediaFormPartsChange(806)

inputMediaSupplyLow(807)                media-low

inputMediaSupplyEmpty(808)              media-empty

inputMediaChangeRequest(809)            media-needed

inputManualInputRequest(810)

inputTrayPositionFailure(811)

inputTrayElevationFailure(812)

inputCannotFeedSizeSelected(813)

-- Output Group

outputMediaTrayMissing(901)             output-tray-missing

outputMediaTrayAlmostFull(902)          output-area-almost-full

outputMediaTrayFull(903)                output-area-full

outputMailboxSelectFailure(904)

-- Marker Group

markerFuserUnderTemperature(1001)       fuser-under-temp

markerFuserOverTemperature(1002)        fuser-over-temp

markerFuserTimingFailure(1003)

markerFuserThermistorFailure(1004)

markerAdjustingPrintQuality(1005)

-- Marker Supplies Group

markerTonerEmpty(1101)                  toner-empty

markerInkEmpty(1102)                    (marker-supply-empty)

markerPrintRibbonEmpty(1103)            (marker-supply-empty)

markerTonerAlmostEmpty(1104)            toner-low

markerInkAlmostEmpty(1105)              (marker-supply-low)

markerPrintRibbonAlmostEmpty(1106)      (marker-supply-low)

markerWasteTonerReceptacleAlmostFull(1107)

(marker-waste-almost-full)

markerWasteInkReceptacleAlmostFull(1108)

(marker-waste-almost-full)

markerWasteTonerReceptacleFull(1109)    (marker-waste-full)

markerWasteInkReceptacleFull(1110)      (marker-waste-full)

markerOpcLifeAlmostOver(1111)           opc-near-eol

markerOpcLifeOver(1112)                 opc-life-over

markerDeveloperAlmostEmpty(1113)        (marker-supply-low)

markerDeveloperEmpty(1114)              (marker-supply-empty)

markerTonerCartridgeMissing(1115)

-- Media Path Group

mediaPathMediaTrayMissing(1301)

mediaPathMediaTrayAlmostFull(1302)

mediaPathMediaTrayFull(1303)

mediaPathCannotDuplexMediaSelected(1304)

-- Interpreter Group

interpreterMemoryIncrease(1501)

interpreterMemoryDecrease(1502)

interpreterCartridgeAdded(1503)

interpreterCartridgeDeleted(1504)

interpreterResourceAdded(1505)

interpreterResourceDeleted(1506)

interpreterResourceUnavailable(1507)    interpreter-resource-unavailable

interpreterComplexPageEncountered(1509)

-- Alert Group

alertRemovalOfBinaryChangeEntry(1801)

-- A binary change alert has been removed

#### Conformance

- For interoperability, IPP implementations that claim conformance to this specification MUST implement the Table 5-1 standard mappings between existing values of "printer-state-reasons" [RFC2911] and existing values of 'PrtAlertCodeTC' [IANAPRT].

- For interoperability, IPP implementations that claim conformance to this specification SHOULD NOT implement the Table 5-1 deprecated mappings (enclosed in parentheses) between existing values of "printer-state-reasons" [RFC2911] and existing values of 'PrtAlertCodeTC' [IANAPRT]. Instead, the new specific mappings defined in Table 5-2 SHOULD be implemented.

### New Printer State Reasons for Alert Codes

The table below defines new values of "printer-state-reasons" [RFC2911] and their mapping from existing values of 'PrtAlertCodeTC' [IANAPRT].  Rows with a ‘----‘ value in “printer-state-reasons” indicate existing values “printer-state-reasons” that were originally defined in [RFC2911] (e.g., ‘jam’).  IPP implementations that claim conformance to this specification therefore support a complete and precise mapping of “printer-state-reasons” from original values of ‘PrtAlertCodeTC’ [IANAPRT] defined in [RFC 3805].

Table 5-2 - New Printer State Reasons for Alert Codes

PrtAlertCodeTC                          	printer-state-reasons

-- RFC 1759 Generic codes

other(1)                                	---

unknown(2)                              	unknown

coverOpen(3)                            	---

coverClosed(4)                          	cover-closed

interlockOpen(5)                        	---

interlockClosed(6)                      	interlock-closed

configurationChange(7)                  	configuration-change

jam(8)                                  	---

-- RFC 3805 Generic codes

subunitMissing(9)                       	subunit-missing

subunitLifeAlmostOver(10)               	subunit-life-almost-over

subunitLifeOver(11)                     	subunit-life-over

subunitAlmostEmpty(12)                  	subunit-almost-empty

subunitEmpty(13)                        	subunit-empty

subunitAlmostFull(14)                   	subunit-almost-full

subunitFull(15)                         	subunit-full

subunitNearLimit(16)                    	subunit-near-limit

subunitAtLimit(17)                      	subunit-at-limit

subunitOpened(18)                       	subunit-opened

subunitClosed(19)                       	subunit-closed

subunitTurnedOn(20)                     	subunit-turned-on

subunitTurnedOff(21)                    	subunit-turned-off

subunitOffline(22)                      	subunit-offline

subunitPowerSaver(23)                   	subunit-power-saver

subunitWarmingUp(24)                    	subunit-warming-up

subunitAdded(25)                        	subunit-added

subunitRemoved(26)                      	subunit-removed

subunitResourceAdded(27)                	subunit-resource-added

subunitResourceRemoved(28)              	subunit-resource-removed

subunitRecoverableFailure(29)           	subunit-recoverable-failure

subunitUnrecoverableFailure(30)         	subunit-unrecoverable-failure

subunitRecoverableStorageError(31)	subunit-recoverable-storage-error

subunitUnrecoverableStorageError(32)	subunit-unrecoverable-storage-error

subunitMotorFailure(33)                 	subunit-motor-failure

subunitMemoryExhausted(34)              	subunit-memory-exhausted

subunitUnderTemperature(35)             	subunit-under-temperature

subunitOverTemperature(36)              	subunit-over-temperature

subunitTimingFailure(37)                	subunit-timing-Failure

subunitThermistorFailure(38)            	subunit-thermistor-failure

-- General Printer Group

doorOpen(501)                           	---

-- DEPRECATED -- use coverOpen(3)

doorClosed(502)                         	cover-closed

-- DEPRECATED -- use coverClosed(4)

powerUp(503)                            	power-up

powerDown(504)                          	power-down

printerNMSReset(505)                    	printer-nms-reset

printerManualReset(506)                 	printer-manual-reset

printerReadyToPrint(507)                	printer-ready-to-print

-- Input Group

inputMediaTrayMissing(801)              	---

inputMediaSizeChange(802)               	input-media-size-change

inputMediaWeightChange(803)             	input-media-weight-change

inputMediaTypeChange(804)               	input-media-type-change

inputMediaColorChange(805)              	input-media-color-change

inputMediaFormPartsChange(806)          	input-media-form-parts-change

inputMediaSupplyLow(807)                	---

inputMediaSupplyEmpty(808)              	---

inputMediaChangeRequest(809)            	---

inputManualInputRequest(810)            	input-manual-input-request

inputTrayPositionFailure(811)           	input-tray-position-failure

inputTrayElevationFailure(812)          	input-tray-elevation-failure

inputCannotFeedSizeSelected(813)        	input-cannot-feed-size-selected

-- Output Group

outputMediaTrayMissing(901)             	---

outputMediaTrayAlmostFull(902)          	---

outputMediaTrayFull(903)                	---

outputMailboxSelectFailure(904)         	output-mailbox-select-failure

-- Marker Group

markerFuserUnderTemperature(1001)		---

markerFuserOverTemperature(1002)        	---

markerFuserTimingFailure(1003)          	marker-fuser-timing-failure

markerFuserThermistorFailure(1004)      	marker-fuser-thermistor-failure

markerAdjustingPrintQuality(1005)       	marker-adjusting-print-quality

-- Marker Supplies Group

markerTonerEmpty(1101)                  	---

markerInkEmpty(1102)                    	marker-ink-empty

markerPrintRibbonEmpty(1103)            	marker-print-ribbon-empty

markerTonerAlmostEmpty(1104)            	---

markerInkAlmostEmpty(1105)              	marker-ink-almost-empty

markerPrintRibbonAlmostEmpty(1106)      	marker-print-ribbon-almost-empty

markerWasteTonerReceptacleAlmostFull(1107)	marker-waste-toner-receptacle-almost-

full

markerWasteInkReceptacleAlmostFull(1108)	marker-waste-ink-receptacle-almost-full

markerWasteTonerReceptacleFull(1109)    	marker-waste-toner-receptacle-full

markerWasteInkReceptacleFull(1110)      	marker-waste-ink-receptacle-full

markerOpcLifeAlmostOver(1111)           	---

markerOpcLifeOver(1112)                 	---

markerDeveloperAlmostEmpty(1113)        	marker-developer-almost-empty

markerDeveloperEmpty(1114)              	marker-developer-empty

markerTonerCartridgeMissing(1115)       	marker-toner-cartridge-missing

-- Media Path Group

mediaPathMediaTrayMissing(1301)         	media-path-media-tray-missing

mediaPathMediaTrayAlmostFull(1302)	media-path-media-tray-almost-full

mediaPathMediaTrayFull(1303)            	media-path-media-tray-full

mediaPathCannotDuplexMediaSelected(1304) 	media-path-cannot-duplex-media-selected

-- Interpreter Group

interpreterMemoryIncrease(1501)         	interpreter-memory-increase

interpreterMemoryDecrease(1502)         	interpreter-memory-decrease

interpreterCartridgeAdded(1503)         	interpreter-cartridge-added

interpreterCartridgeDeleted(1504)       	interpreter-cartridge-deleted

interpreterResourceAdded(1505)          	interpreter-resource-added

interpreterResourceDeleted(1506)        	interpreter-resource-deleted

interpreterResourceUnavailable(1507)    	---

interpreterComplexPageEncountered(1509)	interpreter-complex-page-encountered

-- Alert Group

alertRemovalOfBinaryChangeEntry(1801)	alert-removal-of-binary-change-entry

-- A binary change alert has been removed

#### Conformance

- For interoperability, IPP implementations that claim conformance to this specification MUST implement the Table 5-2 standard mappings between new values of "printer-state-reasons" [RFC2911] and existing values of 'PrtAlertCodeTC' [IANAPRT].

### New PrinterState Reasons for Finishing Subunits

See the Table 6-1 'New Alert Codes for Finishing Subunits' in section 6.1.1  that shows new values of "printer-state-reasons" [RFC2911] and their mapping from new values of 'PrtAlertCodeTC' [IANAPRT] for Finishing Subunits.

#### Conformance

- For interoperability, IPP implementations that claim conformance to this specification MUST implement the Table 6-1 mapping standards between new values of "printer-state-reasons" [RFC2911] and new values of 'PrtAlertCodeTC' [IANAPRT] for Finishing Subunits.

## printer-alert (1setOf octetString(MAX))

This section defines the new multi-valued IPP Printer "printer-alert" attribute.  This IPP Printer attribute is REQUIRED for implementations that conform to this specification

### Keywords for Alert Objects

The table below defines keywords for "printer-alert" for all of the machine-readable columnar objects in 'prtAlertTable' [RFC3805]:

Note: The conformance levels in this table have been harmonized with:

- The bindings of the 'printerV2Alert' notification defined in IETF Printer MIB v2 [RFC3805];

- Section 9 'Event Notification Content' in IETF IPP Event Notifications and Subscriptions [RFC3995]; and

- DMTF/PWG CIM modelling of Printer MIB [WIMS-CIM].

Table 5-3 - Keywords for Alert Objects

Alert Object            	Datatype  	printer-alert tag   	Conformance

prtAlertCode                	String      	code                	REQUIRED

prtAlertIndex               	Integer     	index               	RECOMMENDED

prtAlertSeverityLevel 	String      	severity            	RECOMMENDED

prtAlertTrainingLevel  	String      	training            	OPTIONAL

prtAlertGroup               	String      	group               	RECOMMENDED

prtAlertGroupIndex     	Integer     	group-index         	RECOMMENDED

prtAlertLocation            	Integer    	location            	RECOMMENDED

prtAlertTime                	Integer     	time                	OPTIONAL

#### Conformance

- For interoperability, IPP implementations that claim conformance to this specification MUST implement the new REQUIRED IPP Printer "printer-alert" attribute.

- For interoperability, IPP implementations that claim conformance to this specification and implement the new "printer-alert" attribute MUST implement the Table 5-3 standard mappings between keywords in "printer-alert" and existing labels of 'prtAlertTable' objects [RFC3805].

- For interoperability, IPP implementations that claim conformance to this specification  MUST implement the Table 5-3 keywords defined as REQUIRED.

- For interoperability, IPP implementations that claim conformance to this specification SHOULD implement the Table 5-3 keywords defined as RECOMMENDED.

#### Rationale for Omission of prtAlertDescription

In this specification, a mapping of the human-readable, localized 'prtAlertDescription' object is NOT defined in "printer-alert" but rather in a separate new "printer-alert-description" attribute, for the following reasons:

- To define such a mapping, where only _part_ of the resulting "printer-alert" attribute is localized, would be technically impossible to specify in ABNF [RFC5234].

- To define such a mapping, without a fixed charset (because of localized content) would be technically impossible to specify in ABNF [RFC5234].

- To implement such a mapping, if the value of the IPP Printer "charset-configured" attribute was different from the value of prtLocalizationCharacterSet selected by prtGeneralCurrentLocalization, would require that the IPP implementation performed (potentially lossy) charset conversion.

- To implement such a mapping, if the value of the IPP Printer "natural-language-configured" attribute was different from the combined values of prtLocalizationLanguage and prtLocalizationCountry selected by prtGeneralCurrentLocalization, would require that the IPP implementation performed (potentially lossy) message translation.

### Printer Alert Encoding of Alert Objects

Values of the new IPP Printer "printer-alert" attribute MUST be encoded using a visible subset of the [US-ASCII] charset. Control codes (0x00 to 0x1F and 0x7F) MUST NOT be used. The ABNF [RFC5234] below defines the standard encoding in "printer-alert" for all of the machine-readable (non-localized) columnar objects in 'prtAlertTable' [RFC3805]:

printer-alert       = alert-code *[";" alert-element]

; set of alert elements encoded into one value

alert-code          = "code" "=" 1*ALPHA

; enumerated value as an alpha string (e.g., 'coverOpen')

; 'prtAlertCode' in IETF Printer MIB v2 [RFC3805] mapped to label

; in 'PrtAlertCodeTC' in IANA Printer MIB [IANAPRT]

alert-element       = alert-index /

alert-severity /

alert-training /

alert-group /

alert-group-index /

alert-location /

alert-time

alert-index         = "index" "=" 1*DIGIT

; integer value as a numeric string mapped directly mapped from

; 'prtAlertIndex' in [RFC1759] [RFC3805]

alert-severity      = "severity" "=" 1*ALPHA

; enumerated value as an alpha string (e.g., 'critical') mapped

; from 'prtAlertSeverityLevel' in [RFC1759] [RFC3805] to label

; in 'PrtAlertSeverityLevelTC' in IANA Printer MIB [IANAPRT]

alert-training      = "training" "=" 1*ALPHA

; enumerated value as an alpha string (e.g., 'fieldService') mapped

; from 'prtAlertTrainingLevel' in [RFC1759] [RFC3805] to label

; in 'PrtAlertTrainingLevelTC' in IANA Printer MIB [IANAPRT]

alert-group         = "group" "=" 1*ALPHA

; enumerated value as an alpha string (e.g., 'markerSupplies')

; mapped from 'prtAlertGroup' in [RFC1759] [RFC3805] to label

; in 'PrtAlertGroupTC' in IANA Printer MIB [IANAPRT]

alert-group-index   = "groupindex" "=" 1*DIGIT

; integer value as a numeric string mapped directly mapped from

; 'prtAlertGroupIndex' in [RFC1759] [RFC3805]

alert-location      = "location" "=" 1*DIGIT

; integer value as a numeric string mapped directly mapped from

; 'prtAlertLocation' in [RFC1759] [RFC3805]

alert-time          = "time" "=" 1*DIGIT

; integer value as a numeric string mapped directly mapped from

; 'prtAlertTime' in [RFC1759] [RFC3805]

Figure 4 - ABNF for IPP printer-alert

#### Conformance

- For interoperability, IPP implementations that claim conformance to this specification MUST implement the new REQUIRED IPP Printer "printer-alert" attribute.

- For interoperability, IPP implementations that claim conformance to this specification MUST implement the above standard encoding in "printer-alert" of machine-readable values of existing 'prtAlertTable' columnar objects [RFC3805].

#### Rationale for Encoding of Enumerated Values

In this specification, enumerated values of 'prtAlertTable' objects (e.g., 'prtAlertSeverityLevel') are mapped to corresponding enumeration labels in "printer-alert" for the following reasons:

- To define a strictly numeric mapping is (potentially) fragile and loses human-readability.

- To define an alphabetic (keyword) mapping is consistent with the IPP design preference for 'keyword' (section 4.1.3 of [RFC2911]) rather than 'enum' (section 4.1.4 of [RFC2911]) attribute syntaxes.

#### Example of Printer Alert

The following example shows all REQUIRED and RECOMMENDED and some OPTIONAL columnar objects from 'prtAlertTable' encoded into two corresponding values of the IPP Printer "printer-alert" attribute for two distinct (but closely related) alerts. Line breaks are shown for readability of this example, but MUST NOT be encoded into actual values of "printer-alert".

printer-alert[1] =

code=jam;index=22;severity=critical

;group=mediaPath;groupindex=4;location=6

printer-alert[2] =

code=coverOpen;index=23;severity=critical

;group=cover;groupindex=6;location=8

Figure 5 - Example of IPP printer-alert

## printer-alert-description (1setOf text(MAX))

This section defines the new multi-valued IPP Printer "printer-alert-description" attribute.. This IPP Printer attribute is REQUIRED for implementations that conform to this specification.

### Printer Alert Description Encoding

Each text value of "printer-alert-description" MUST be mapped directly from the corresponding human-readable, localized value of 'prtAlertDescription' as follows:

- Each value of 'prtAlertDescription' MUST be convered from the charset [RFC2978] [RFC3808] specified by 'prtLocalizationCharacterSet' and 'prtGeneralCurrentLocalization' to the charset specified by "charset-configured" (defaults to UTF-8 [RFC3629]) and then copied to a text value of "printer-alert-description".

- Each value of "printer-alert-description" MUST be tagged with the natural language [RFC4646] specified by 'prtLocalizationLanguage', 'prtLocalizationCountry', and 'prtGeneralCurrentLocalization'.

- Each value of "printer-alert-description" MUST be in the same order as the corresponding value of "printer-alert".

#### Conformance

- For interoperability, IPP implementations that claim conformance to this specification MUST implement the new REQUIRED IPP Printer "printer-alert-description" attribute.

- For interoperability, IPP implementations that claim conformance to this specification MUST implement the above standard encoding in "printer-alert-description" of human-readable, localized values of the 'prtAlertDescription' columnar object [RFC3805], including charset conversion and language tag copying.

### Example of Printer Alert Description

The following example shows two instances of the localized 'prtAlertDescription' columnar object from 'prtAlertTable' encoded into two corresponding values of the IPP Printer "printer-alert-description" attribute for two distinct (but closely related) alerts.

printer-alert-description[1] =

'Critical alert - jam in media path at location 6'

printer-alert-description[2] =

'Critical alert - cover open at location 8'

Figure 6 - Example of IPP printer-alert-description

# IANA Printer MIB Textual Conventions

## PrtAlertCodeTC

This section defines new values for the existing 'PrtAlertCodeTC' [IANAPRT] textual convention and also defines corresponding new values for the existing "printer-state-reasons" [RFC2911] attribute for registration with IANA. The REQUIRED finishing extensions to the the PrtAlertCodeTC textual convention defined in IANA Printer MIB are defined in detail below.

### New Alert Codes for Finishing Subunits

The table below shows new values of "printer-state-reasons" [RFC2911] and their mapping from new values of 'PrtAlertCodeTC' [IANAPRT] and their algorithmic mapping from existing values of 'FinDeviceTypeTC' [IANAFIN].

Note: See section 6.1.1.3 'Rationale for Stapler and Stitcher Devices' and section 6.1.2 'Conventions for Alert Code Numbering' for discussion of the missing 'stapler' in IANA Finisher MIB [IANAFIN].

Table 6-1 - New Alert Codes for Finishing Subunits

PrtAlertCodeTC	printer-state-reasons

-- FinDeviceTypeTC = stitcher(3) -> stapler

-- FinStitchingTypeTC = staple... (4,5,6,7, or 10)

staplerCoverOpen(30203)	stapler-cover-open

staplerCoverClosed(30204)	stapler-cover-closed

staplerInterlockOpen(30205)	stapler-interlock-open

staplerInterlockClosed(30206)	stapler-interlock-closed

staplerConfigurationChange(30207)	stapler-configuration-change

staplerJam(30208)	stapler-jam

staplerMissing(30209)	stapler-missing

staplerLifeAlmostOver(30210)	stapler-life-almost-over

staplerLifeOver(30211)	stapler-life-over

staplerAlmostEmpty(30212)	stapler-almost-empty

staplerEmpty(30213)	stapler-empty

staplerAlmostFull(30214)	stapler-almost-full

staplerFull(30215)	stapler-full

staplerNearLimit(30216)	stapler-near-limit

staplerAtLimit(30217)	stapler-at-limit

staplerOpened(30218)	stapler-opened

staplerClosed(30219)	stapler-closed

staplerTurnedOn(30220)	stapler-turned-on

staplerTurnedOff(30221)	stapler-turned-off

staplerOffline(30222)	stapler-offline

staplerPowerSaver(30223)	stapler-power-saver

staplerWarmingUp(30224)	stapler-warming-up

staplerAdded(30225)	stapler-added

staplerRemoved(30226)	stapler-removed

staplerResourceAdded(30227)	stapler-resource-added

staplerResourceRemoved(30228)	stapler-resource-removed

staplerRecoverableFailure(30229)	stapler-recoverable-failure

staplerUnrecoverableFailure(30230)	stapler-unrecoverable-failure

staplerRecoverableStorageError(30231)	stapler-recoverable-storage-error

staplerUnrecoverableStorageError(30232)	stapler-unrecoverable-storage-error

staplerMotorFailure(30233)	stapler-motor-failure

staplerMemoryExhausted(30234)	stapler-memory-exhausted

staplerUnderTemperature(30235)	stapler-under-temperature

staplerOverTemperature(30236)	stapler-over-temperature

staplerTimingFailure(30237)	stapler-timing-failure

staplerThermistorFailure(30238)	stapler-thermistor-failure

-- FinDeviceTypeTC = stitcher(3) -> stitcher

-- FinStitchingTypeTC = saddleStitch(8) or edgeStitch(9)

stitcherCoverOpen(30303)	stitcher-cover-open

stitcherCoverClosed(30304)	stitcher-cover-closed

stitcherInterlockOpen(30305)	stitcher-interlock-open

stitcherInterlockClosed(30306)	stitcher-interlock-closed

stitcherConfigurationChange(30307)	stitcher-configuration-change

stitcherJam(30308)	stitcher-jam

stitcherMissing(30309)	stitcher-missing

stitcherLifeAlmostOver(30310)	stitcher-life-almost-over

stitcherLifeOver(30311)	stitcher-life-over

stitcherAlmostEmpty(30312)	stitcher-almost-empty

stitcherEmpty(30313)	stitcher-empty

stitcherAlmostFull(30314)	stitcher-almost-full

stitcherFull(30315)	stitcher-full

stitcherNearLimit(30316)	stitcher-near-limit

stitcherAtLimit(30317)	stitcher-at-limit

stitcherOpened(30318)	stitcher-opened

stitcherClosed(30319)	stitcher-closed

stitcherTurnedOn(30320)	stitcher-turned-on

stitcherTurnedOff(30321)	stitcher-turned-off

stitcherOffline(30322)	stitcher-offline

stitcherPowerSaver(30323)	stitcher-power-saver

stitcherWarmingUp(30324)	stitcher-warming-up

stitcherAdded(30325)	stitcher-added

stitcherRemoved(30326)	stitcher-removed

stitcherResourceAdded(30327)	stitcher-resource-added

stitcherResourceRemoved(30328)	stitcher-resource-removed

stitcherRecoverableFailure(30329)	stitcher-recoverable-failure

stitcherUnrecoverableFailure(30330)	stitcher-unrecoverable-failure

stitcherRecoverableStorageError(30331)	stitcher-recoverable-storage-error

stitcherUnrecoverableStorageError(30332)	stitcher-unrecoverable-storage-error

stitcherMotorFailure(30333)	stitcher-motor-failure

stitcherMemoryExhausted(30334)	stitcher-memory-exhausted

stitcherUnderTemperature(30335)	stitcher-under-temperature

stitcherOverTemperature(30336)	stitcher-over-temperature

stitcherTimingFailure(30337)	stitcher-timing-failure

stitcherThermistorFailure(30338)	stitcher-thermistor-failure

-- FinDeviceTypeTC = folder(4)

folderCoverOpen(30403)	folder-cover-open

folderCoverClosed(30404)	folder-cover-closed

folderInterlockOpen(30405)	folder-interlock-open

folderInterlockClosed(30406)	folder-interlock-closed

folderConfigurationChange(30407)	folder-configuration-change

folderJam(30408)	folder-jam

folderMissing(30409)	folder-missing

folderLifeAlmostOver(30410)	folder-life-almost-over

folderLifeOver(30411)	folder-life-over

folderAlmostEmpty(30412)	folder-almost-empty

folderEmpty(30413)	folder-empty

folderAlmostFull(30414)	folder-almost-full

folderFull(30415)	folder-full

folderNearLimit(30416)	folder-near-limit

folderAtLimit(30417)	folder-at-limit

folderOpened(30418)	folder-opened

folderClosed(30419)	folder-closed

folderTurnedOn(30420)	folder-turned-on

folderTurnedOff(30421)	folder-turned-off

folderOffline(30422)	folder-offline

folderPowerSaver(30423)	folder-power-saver

folderWarmingUp(30424)	folder-warming-up

folderAdded(30425)	folder-added

folderRemoved(30426)	folder-removed

folderResourceAdded(30427)	folder-resource-added

folderResourceRemoved(30428)	folder-resource-removed

folderRecoverableFailure(30429)	folder-recoverable-failure

folderUnrecoverableFailure(30430)	folder-unrecoverable-failure

folderRecoverableStorageError(30431)	folder-recoverable-storage-error

folderUnrecoverableStorageError(30432)	folder-unrecoverable-storage-error

folderMotorFailure(30433)	folder-motor-failure

folderMemoryExhausted(30434)	folder-memory-exhausted

folderUnderTemperature(30435)	folder-under-temperature

folderOverTemperature(30436)	folder-over-temperature

folderTimingFailure(30437)	folder-timing-failure

folderThermistorFailure(30438)	folder-thermistor-failure

-- FinDeviceTypeTC = binder(5)

binderCoverOpen(30503)	binder-cover-open

binderCoverClosed(30504)	binder-cover-closed

binderInterlockOpen(30505)	binder-interlock-open

binderInterlockClosed(30506)	binder-interlock-closed

binderConfigurationChange(30507)	binder-configuration-change

binderJam(30508)	binder-jam

binderMissing(30509)	binder-missing

binderLifeAlmostOver(30510)	binder-life-almost-over

binderLifeOver(30511)	binder-life-over

binderAlmostEmpty(30512)	binder-almost-empty

binderEmpty(30513)	binder-empty

binderAlmostFull(30514)	binder-almost-full

binderFull(30515)	binder-full

binderNearLimit(30516)	binder-near-limit

binderAtLimit(30517)	binder-at-limit

binderOpened(30518)	binder-opened

binderClosed(30519)	binder-closed

binderTurnedOn(30520)	binder-turned-on

binderTurnedOff(30521)	binder-turned-off

binderOffline(30522)	binder-offline

binderPowerSaver(30523)	binder-power-saver

binderWarmingUp(30524)	binder-warming-up

binderAdded(30525)	binder-added

binderRemoved(30526)	binder-removed

binderResourceAdded(30527)	binder-resource-added

binderResourceRemoved(30528)	binder-resource-removed

binderRecoverableFailure(30529)	binder-recoverable-failure

binderUnrecoverableFailure(30530)	binder-unrecoverable-failure

binderRecoverableStorageError(30531)	binder-recoverable-storage-error

binderUnrecoverableStorageError(30532)	binder-unrecoverable-storage-error

binderMotorFailure(30533)	binder-motor-failure

binderMemoryExhausted(30534)	binder-memory-exhausted

binderUnderTemperature(30535)	binder-under-temperature

binderOverTemperature(30536)	binder-over-temperature

binderTimingFailure(30537)	binder-timing-failure

binderThermistorFailure(30538)	binder-thermistor-failure

-- FinDeviceTypeTC = trimmer(6)

trimmerCoverOpen(30603)	trimmer-cover-open

trimmerCoverClosed(30604)	trimmer-cover-closed

trimmerInterlockOpen(30605)	trimmer-interlock-open

trimmerInterlockClosed(30606)	trimmer-interlock-closed

trimmerConfigurationChange(30607)	trimmer-configuration-change

trimmerJam(30608)	trimmer-jam

trimmerMissing(30609)	trimmer-missing

trimmerLifeAlmostOver(30610)	trimmer-life-almost-over

trimmerLifeOver(30611)	trimmer-life-over

trimmerAlmostEmpty(30612)	trimmer-almost-empty

trimmerEmpty(30613)	trimmer-empty

trimmerAlmostFull(30614)	trimmer-almost-full

trimmerFull(30615)	trimmer-full

trimmerNearLimit(30616)	trimmer-near-limit

trimmerAtLimit(30617)	trimmer-at-limit

trimmerOpened(30618)	trimmer-opened

trimmerClosed(30619)	trimmer-closed

trimmerTurnedOn(30620)	trimmer-turned-on

trimmerTurnedOff(30621)	trimmer-turned-off

trimmerOffline(30622)	trimmer-offline

trimmerPowerSaver(30623)	trimmer-power-saver

trimmerWarmingUp(30624)	trimmer-warming-up

trimmerAdded(30625)	trimmer-added

trimmerRemoved(30626)	trimmer-removed

trimmerResourceAdded(30627)	trimmer-resource-added

trimmerResourceRemoved(30628)	trimmer-resource-removed

trimmerRecoverableFailure(30629)	trimmer-recoverable-failure

trimmerUnrecoverableFailure(30630)	trimmer-unrecoverable-failure

trimmerRecoverableStorageError(30631)	trimmer-recoverable-storage-error

trimmerUnrecoverableStorageError(30632)	trimmer-unrecoverable-storage-error

trimmerMotorFailure(30633)	trimmer-motor-failure

trimmerMemoryExhausted(30634)	trimmer-memory-exhausted

trimmerUnderTemperature(30635)	trimmer-under-temperature

trimmerOverTemperature(30636)	trimmer-over-temperature

trimmerTimingFailure(30637)	trimmer-timing-failure

trimmerThermistorFailure(30638)	trimmer-thermistor-failure

-- FinDeviceTypeTC = dieCutter(7)

dieCutterCoverOpen(30703)	die-cutter-cover-open

dieCutterCoverClosed(30704)	die-cutter-cover-closed

dieCutterInterlockOpen(30705)	die-cutter-interlock-open

dieCutterInterlockClosed(30706)	die-cutter-interlock-closed

dieCutterConfigurationChange(30707)	die-cutter-configuration-change

dieCutterJam(30708)	die-cutter-jam

dieCutterMissing(30709)	die-cutter-missing

dieCutterLifeAlmostOver(30710)	die-cutter-life-almost-over

dieCutterLifeOver(30711)	die-cutter-life-over

dieCutterAlmostEmpty(30712)	die-cutter-almost-empty

dieCutterEmpty(30713)	die-cutter-empty

dieCutterAlmostFull(30714)	die-cutter-almost-full

dieCutterFull(30715)	die-cutter-full

dieCutterNearLimit(30716)	die-cutter-near-limit

dieCutterAtLimit(30717)	die-cutter-at-limit

dieCutterOpened(30718)	die-cutter-opened

dieCutterClosed(30719)	die-cutter-closed

dieCutterTurnedOn(30720)	die-cutter-turned-on

dieCutterTurnedOff(30721)	die-cutter-turned-off

dieCutterOffline(30722)	die-cutter-offline

dieCutterPowerSaver(30723)	die-cutter-power-saver

dieCutterWarmingUp(30724)	die-cutter-warming-up

dieCutterAdded(30725)	die-cutter-added

dieCutterRemoved(30726)	die-cutter-removed

dieCutterResourceAdded(30727)	die-cutter-resource-added

dieCutterResourceRemoved(30728)	die-cutter-resource-removed

dieCutterRecoverableFailure(30729)	die-cutter-recoverable-failure

dieCutterUnrecoverableFailure(30730)	die-cutter-unrecoverable-failure

dieCutterRecoverableStorageError(30731)	die-cutter-recoverable-storage-error

dieCutterUnrecoverableStorageError(30732)	die-cutter-unrecoverable-storage-error

dieCutterMotorFailure(30733)	die-cutter-motor-failure

dieCutterMemoryExhausted(30734)	die-cutter-memory-exhausted

dieCutterUnderTemperature(30735)	die-cutter-under-temperature

dieCutterOverTemperature(30736)	die-cutter-over-temperature

dieCutterTimingFailure(30737)	die-cutter-timing-failure

dieCutterThermistorFailure(30738)	die-cutter-thermistor-failure

-- FinDeviceTypeTC = puncher(8)

puncherCoverOpen(30803)	puncher-cover-open

puncherCoverClosed(30804)	puncher-cover-closed

puncherInterlockOpen(30805)	puncher-interlock-open

puncherInterlockClosed(30806)	puncher-interlock-closed

puncherConfigurationChange(30807)	puncher-configuration-change

puncherJam(30808)	puncher-jam

puncherMissing(30809)	puncher-missing

puncherLifeAlmostOver(30810)	puncher-life-almost-over

puncherLifeOver(30811)	puncher-life-over

puncherAlmostEmpty(30812)	puncher-almost-empty

puncherEmpty(30813)	puncher-empty

puncherAlmostFull(30814)	puncher-almost-full

puncherFull(30815)	puncher-full

puncherNearLimit(30816)	puncher-near-limit

puncherAtLimit(30817)	puncher-at-limit

puncherOpened(30818)	puncher-opened

puncherClosed(30819)	puncher-closed

puncherTurnedOn(30820)	puncher-turned-on

puncherTurnedOff(30821)	puncher-turned-off

puncherOffline(30822)	puncher-offline

puncherPowerSaver(30823)	puncher-power-saver

puncherWarmingUp(30824)	puncher-warming-up

puncherAdded(30825)	puncher-added

puncherRemoved(30826)	puncher-removed

puncherResourceAdded(30827)	puncher-resource-added

puncherResourceRemoved(30828)	puncher-resource-removed

puncherRecoverableFailure(30829)	puncher-recoverable-failure

puncherUnrecoverableFailure(30830)	puncher-unrecoverable-failure

puncherRecoverableStorageError(30831)	puncher-recoverable-storage-error

puncherUnrecoverableStorageError(30832)	puncher-unrecoverable-storage-error

puncherMotorFailure(30833)	puncher-motor-failure

puncherMemoryExhausted(30834)	puncher-memory-exhausted

puncherUnderTemperature(30835)	puncher-under-temperature

puncherOverTemperature(30836)	puncher-over-temperature

puncherTimingFailure(30837)	puncher-timing-failure

puncherThermistorFailure(30838)	puncher-thermistor-failure

-- FinDeviceTypeTC = perforater(9)

perforaterCoverOpen(30903)	perforater-cover-open

perforaterCoverClosed(30904)	perforater-cover-closed

perforaterInterlockOpen(30905)	perforater-interlock-open

perforaterInterlockClosed(30906)	perforater-interlock-closed

perforaterConfigurationChange(30907)	perforater-configuration-change

perforaterJam(30908)	perforater-jam

perforaterMissing(30909)	perforater-missing

perforaterLifeAlmostOver(30910)	perforater-life-almost-over

perforaterLifeOver(30911)	perforater-life-over

perforaterAlmostEmpty(30912)	perforater-almost-empty

perforaterEmpty(30913)	perforater-empty

perforaterAlmostFull(30914)	perforater-almost-full

perforaterFull(30915)	perforater-full

perforaterNearLimit(30916)	perforater-near-limit

perforaterAtLimit(30917)	perforater-at-limit

perforaterOpened(30918)	perforater-opened

perforaterClosed(30919)	perforater-closed

perforaterTurnedOn(30920)	perforater-turned-on

perforaterTurnedOff(30921)	perforater-turned-off

perforaterOffline(30922)	perforater-offline

perforaterPowerSaver(30923)	perforater-power-saver

perforaterWarmingUp(30924)	perforater-warming-up

perforaterAdded(30925)	perforater-added

perforaterRemoved(30926)	perforater-removed

perforaterResourceAdded(30927)	perforater-resource-added

perforaterResourceRemoved(30928)	perforater-resource-removed

perforaterRecoverableFailure(30929)	perforater-recoverable-failure

perforaterUnrecoverableFailure(30930)	perforater-unrecoverable-failure

perforaterRecoverableStorageError(30931)	perforater-recoverable-storage-error

perforaterUnrecoverableStorageError(30932)	perforater-unrecoverable-storage-error

perforaterMotorFailure(30933)	perforater-motor-failure

perforaterMemoryExhausted(30934)	perforater-memory-exhausted

perforaterUnderTemperature(30935)	perforater-under-temperature

perforaterOverTemperature(30936)	perforater-over-temperature

perforaterTimingFailure(30937)	perforater-timing-failure

perforaterThermistorFailure(30938)	perforater-thermistor-failure

-- FinDeviceTypeTC = slitter(10)

slitterCoverOpen(31003)	slitter-cover-open

slitterCoverClosed(31004)	slitter-cover-closed

slitterInterlockOpen(31005)	slitter-interlock-open

slitterInterlockClosed(31006)	slitter-interlock-closed

slitterConfigurationChange(31007)	slitter-configuration-change

slitterJam(31008)	slitter-jam

slitterMissing(31009)	slitter-missing

slitterLifeAlmostOver(31010)	slitter-life-almost-over

slitterLifeOver(31011)	slitter-life-over

slitterAlmostEmpty(31012)	slitter-almost-empty

slitterEmpty(31013)	slitter-empty

slitterAlmostFull(31014)	slitter-almost-full

slitterFull(31015)	slitter-full

slitterNearLimit(31016)	slitter-near-limit

slitterAtLimit(31017)	slitter-at-limit

slitterOpened(31018)	slitter-opened

slitterClosed(31019)	slitter-closed

slitterTurnedOn(31020)	slitter-turned-on

slitterTurnedOff(31021)	slitter-turned-off

slitterOffline(31022)	slitter-offline

slitterPowerSaver(31023)	slitter-power-saver

slitterWarmingUp(31024)	slitter-warming-up

slitterAdded(31025)	slitter-added

slitterRemoved(31026)	slitter-removed

slitterResourceAdded(31027)	slitter-resource-added

slitterResourceRemoved(31028)	slitter-resource-removed

slitterRecoverableFailure(31029)	slitter-recoverable-failure

slitterUnrecoverableFailure(31030)	slitter-unrecoverable-failure

slitterRecoverableStorageError(31031)	slitter-recoverable-storage-error

slitterUnrecoverableStorageError(31032)	slitter-unrecoverable-storage-error

slitterMotorFailure(31033)	slitter-motor-failure

slitterMemoryExhausted(31034)	slitter-memory-exhausted

slitterUnderTemperature(31035)	slitter-under-temperature

slitterOverTemperature(31036)	slitter-over-temperature

slitterTimingFailure(31037)	slitter-timing-failure

slitterThermistorFailure(31038)	slitter-thermistor-failure

-- FinDeviceTypeTC = separationCutter(11)

separationCutterCoverOpen(31103)	separation-cutter-cover-open

separationCutterCoverClosed(31104)	separation-cutter-cover-closed

separationCutterInterlockOpen(31105)	separation-cutter-interlock-open

separationCutterInterlockClosed(31106)	separation-cutter-interlock-closed

separationCutterConfigurationChange(31107)	separation-cutter-configuration-change

separationCutterJam(31108)	separation-cutter-jam

separationCutterMissing(31109)	separation-cutter-missing

separationCutterLifeAlmostOver(31110)	separation-cutter-life-almost-over

separationCutterLifeOver(31111)	separation-cutter-life-over

separationCutterAlmostEmpty(31112)	separation-cutter-almost-empty

separationCutterEmpty(31113)	separation-cutter-empty

separationCutterAlmostFull(31114)	separation-cutter-almost-full

separationCutterFull(31115)	separation-cutter-full

separationCutterNearLimit(31116)	separation-cutter-near-limit

separationCutterAtLimit(31117)	separation-cutter-at-limit

separationCutterOpened(31118)	separation-cutter-opened

separationCutterClosed(31119)	separation-cutter-closed

separationCutterTurnedOn(31120)	separation-cutter-turned-on

separationCutterTurnedOff(31121)	separation-cutter-turned-off

separationCutterOffline(31122)	separation-cutter-offline

separationCutterPowerSaver(31123)	separation-cutter-power-saver

separationCutterWarmingUp(31124)	separation-cutter-warming-up

separationCutterAdded(31125)	separation-cutter-added

separationCutterRemoved(31126)	separation-cutter-removed

separationCutterResourceAdded(31127)	separation-cutter-resource-added

separationCutterResourceRemoved(31128)	separation-cutter-resource-removed

separationCutterRecoverableFailure(31129)	separation-cutter-recoverable-failure

separationCutterUnrecoverableFailure(31130)	separation-cutter-unrecoverable-failure

separationCutterRecoverableStorageError(31131)	separation-cutter-recoverable-storage-error

separationCutterUnrecoverableStorageError(31132)	separation-cutter-unrecoverable-storage-error

separationCutterMotorFailure(31133)	separation-cutter-motor-failure

separationCutterMemoryExhausted(31134)	separation-cutter-memory-exhausted

separationCutterUnderTemperature(31135)	separation-cutter-under-temperature

separationCutterOverTemperature(31136)	separation-cutter-over-temperature

separationCutterTimingFailure(31137)	separation-cutter-timing-failure

separationCutterThermistorFailure(31138)	separation-cutter-thermistor-failure

-- FinDeviceTypeTC = imprinter(12)

imprinterCoverOpen(31203)	imprinter-cover-open

imprinterCoverClosed(31204)	imprinter-cover-closed

imprinterInterlockOpen(31205)	imprinter-interlock-open

imprinterInterlockClosed(31206)	imprinter-interlock-closed

imprinterConfigurationChange(31207)	imprinter-configuration-change

imprinterJam(31208)	imprinter-jam

imprinterMissing(31209)	imprinter-missing

imprinterLifeAlmostOver(31210)	imprinter-life-almost-over

imprinterLifeOver(31211)	imprinter-life-over

imprinterAlmostEmpty(31212)	imprinter-almost-empty

imprinterEmpty(31213)	imprinter-empty

imprinterAlmostFull(31214)	imprinter-almost-full

imprinterFull(31215)	imprinter-full

imprinterNearLimit(31216)	imprinter-near-limit

imprinterAtLimit(31217)	imprinter-at-limit

imprinterOpened(31218)	imprinter-opened

imprinterClosed(31219)	imprinter-closed

imprinterTurnedOn(31220)	imprinter-turned-on

imprinterTurnedOff(31221)	imprinter-turned-off

imprinterOffline(31222)	imprinter-offline

imprinterPowerSaver(31223)	imprinter-power-saver

imprinterWarmingUp(31224)	imprinter-warming-up

imprinterAdded(31225)	imprinter-added

imprinterRemoved(31226)	imprinter-removed

imprinterResourceAdded(31227)	imprinter-resource-added

imprinterResourceRemoved(31228)	imprinter-resource-removed

imprinterRecoverableFailure(31229)	imprinter-recoverable-failure

imprinterUnrecoverableFailure(31230)	imprinter-unrecoverable-failure

imprinterRecoverableStorageError(31231)	imprinter-recoverable-storage-error

imprinterUnrecoverableStorageError(31232)	imprinter-unrecoverable-storage-error

imprinterMotorFailure(31233)	imprinter-motor-failure

imprinterMemoryExhausted(31234)	imprinter-memory-exhausted

imprinterUnderTemperature(31235)	imprinter-under-temperature

imprinterOverTemperature(31236)	imprinter-over-temperature

imprinterTimingFailure(31237)	imprinter-timing-failure

imprinterThermistorFailure(31238)	imprinter-thermistor-failure

-- FinDeviceTypeTC = wrapper(13)

wrapperCoverOpen(31303)	wrapper-cover-open

wrapperCoverClosed(31304)	wrapper-cover-closed

wrapperInterlockOpen(31305)	wrapper-interlock-open

wrapperInterlockClosed(31306)	wrapper-interlock-closed

wrapperConfigurationChange(31307)	wrapper-configuration-change

wrapperJam(31308)	wrapper-jam

wrapperMissing(31309)	wrapper-missing

wrapperLifeAlmostOver(31310)	wrapper-life-almost-over

wrapperLifeOver(31311)	wrapper-life-over

wrapperAlmostEmpty(31312)	wrapper-almost-empty

wrapperEmpty(31313)	wrapper-empty

wrapperAlmostFull(31314)	wrapper-almost-full

wrapperFull(31315)	wrapper-full

wrapperNearLimit(31316)	wrapper-near-limit

wrapperAtLimit(31317)	wrapper-at-limit

wrapperOpened(31318)	wrapper-opened

wrapperClosed(31319)	wrapper-closed

wrapperTurnedOn(31320)	wrapper-turned-on

wrapperTurnedOff(31321)	wrapper-turned-off

wrapperOffline(31322)	wrapper-offline

wrapperPowerSaver(31323)	wrapper-power-saver

wrapperWarmingUp(31324)	wrapper-warming-up

wrapperAdded(31325)	wrapper-added

wrapperRemoved(31326)	wrapper-removed

wrapperResourceAdded(31327)	wrapper-resource-added

wrapperResourceRemoved(31328)	wrapper-resource-removed

wrapperRecoverableFailure(31329)	wrapper-recoverable-failure

wrapperUnrecoverableFailure(31330)	wrapper-unrecoverable-failure

wrapperRecoverableStorageError(31331)	wrapper-recoverable-storage-error

wrapperUnrecoverableStorageError(31332)	wrapper-unrecoverable-storage-error

wrapperMotorFailure(31333)	wrapper-motor-failure

wrapperMemoryExhausted(31334)	wrapper-memory-exhausted

wrapperUnderTemperature(31335)	wrapper-under-temperature

wrapperOverTemperature(31336)	wrapper-over-temperature

wrapperTimingFailure(31337)	wrapper-timing-failure

wrapperThermistorFailure(31338)	wrapper-thermistor-failure

-- FinDeviceTypeTC = bander(14)

banderCoverOpen(31403)	bander-cover-open

banderCoverClosed(31404)	bander-cover-closed

banderInterlockOpen(31405)	bander-interlock-open

banderInterlockClosed(31406)	bander-interlock-closed

banderConfigurationChange(31407)	bander-configuration-change

banderJam(31408)	bander-jam

banderMissing(31409)	bander-missing

banderLifeAlmostOver(31410)	bander-life-almost-over

banderLifeOver(31411)	bander-life-over

banderAlmostEmpty(31412)	bander-almost-empty

banderEmpty(31413)	bander-empty

banderAlmostFull(31414)	bander-almost-full

banderFull(31415)	bander-full

banderNearLimit(31416)	bander-near-limit

banderAtLimit(31417)	bander-at-limit

banderOpened(31418)	bander-opened

banderClosed(31419)	bander-closed

banderTurnedOn(31420)	bander-turned-on

banderTurnedOff(31421)	bander-turned-off

banderOffline(31422)	bander-offline

banderPowerSaver(31423)	bander-power-saver

banderWarmingUp(31424)	bander-warming-up

banderAdded(31425)	bander-added

banderRemoved(31426)	bander-removed

banderResourceAdded(31427)	bander-resource-added

banderResourceRemoved(31428)	bander-resource-removed

banderRecoverableFailure(31429)	bander-recoverable-failure

banderUnrecoverableFailure(31430)	bander-unrecoverable-failure

banderRecoverableStorageError(31431)	bander-recoverable-storage-error

banderUnrecoverableStorageError(31432)	bander-unrecoverable-storage-error

banderMotorFailure(31433)	bander-motor-failure

banderMemoryExhausted(31434)	bander-memory-exhausted

banderUnderTemperature(31435)	bander-under-temperature

banderOverTemperature(31436)	bander-over-temperature

banderTimingFailure(31437)	bander-timing-failure

banderThermistorFailure(31438)	bander-thermistor-failure

-- FinDeviceTypeTC = makeEnvelope(15)

makeEnvelopeCoverOpen(31503)	make-envelope-cover-open

makeEnvelopeCoverClosed(31504)	make-envelope-cover-closed

makeEnvelopeInterlockOpen(31505)	make-envelope-interlock-open

makeEnvelopeInterlockClosed(31506)	make-envelope-interlock-closed

makeEnvelopeConfigurationChange(31507)	make-envelope-configuration-change

makeEnvelopeJam(31508)	make-envelope-jam

makeEnvelopeMissing(31509)	make-envelope-missing

makeEnvelopeLifeAlmostOver(31510)	make-envelope-life-almost-over

makeEnvelopeLifeOver(31511)	make-envelope-life-over

makeEnvelopeAlmostEmpty(31512)	make-envelope-almost-empty

makeEnvelopeEmpty(31513)	make-envelope-empty

makeEnvelopeAlmostFull(31514)	make-envelope-almost-full

makeEnvelopeFull(31515)	make-envelope-full

makeEnvelopeNearLimit(31516)	make-envelope-near-limit

makeEnvelopeAtLimit(31517)	make-envelope-at-limit

makeEnvelopeOpened(31518)	make-envelope-opened

makeEnvelopeClosed(31519)	make-envelope-closed

makeEnvelopeTurnedOn(31520)	make-envelope-turned-on

makeEnvelopeTurnedOff(31521)	make-envelope-turned-off

makeEnvelopeOffline(31522)	make-envelope-offline

makeEnvelopePowerSaver(31523)	make-envelope-power-saver

makeEnvelopeWarmingUp(31524)	make-envelope-warming-up

makeEnvelopeAdded(31525)	make-envelope-added

makeEnvelopeRemoved(31526)	make-envelope-removed

makeEnvelopeResourceAdded(31527)	make-envelope-resource-added

makeEnvelopeResourceRemoved(31528)	make-envelope-resource-removed

makeEnvelopeRecoverableFailure(31529)	make-envelope-recoverable-failure

makeEnvelopeUnrecoverableFailure(31530)	make-envelope-unrecoverable-failure

makeEnvelopeRecoverableStorageError(31531)	make-envelope-recoverable-storage-error

makeEnvelopeUnrecoverableStorageError(31532)	make-envelope-unrecoverable-storage-error

makeEnvelopeMotorFailure(31533)	make-envelope-motor-failure

makeEnvelopeMemoryExhausted(31534)	make-envelope-memory-exhausted

makeEnvelopeUnderTemperature(31535)	make-envelope-under-temperature

makeEnvelopeOverTemperature(31536)	make-envelope-over-temperature

makeEnvelopeTimingFailure(31537)	make-envelope-timing-failure

makeEnvelopeThermistorFailure(31538)	make-envelope-thermistor-failure

-- FinDeviceTypeTC = stacker(16)

stackerCoverOpen(31603)	stacker-cover-open

stackerCoverClosed(31604)	stacker-cover-closed

stackerInterlockOpen(31605)	stacker-interlock-open

stackerInterlockClosed(31606)	stacker-interlock-closed

stackerConfigurationChange(31607)	stacker-configuration-change

stackerJam(31608)	stacker-jam

stackerMissing(31609)	stacker-missing

stackerLifeAlmostOver(31610)	stacker-life-almost-over

stackerLifeOver(31611)	stacker-life-over

stackerAlmostEmpty(31612)	stacker-almost-empty

stackerEmpty(31613)	stacker-empty

stackerAlmostFull(31614)	stacker-almost-full

stackerFull(31615)	stacker-full

stackerNearLimit(31616)	stacker-near-limit

stackerAtLimit(31617)	stacker-at-limit

stackerOpened(31618)	stacker-opened

stackerClosed(31619)	stacker-closed

stackerTurnedOn(31620)	stacker-turned-on

stackerTurnedOff(31621)	stacker-turned-off

stackerOffline(31622)	stacker-offline

stackerPowerSaver(31623)	stacker-power-saver

stackerWarmingUp(31624)	stacker-warming-up

stackerAdded(31625)	stacker-added

stackerRemoved(31626)	stacker-removed

stackerResourceAdded(31627)	stacker-resource-added

stackerResourceRemoved(31628)	stacker-resource-removed

stackerRecoverableFailure(31629)	stacker-recoverable-failure

stackerUnrecoverableFailure(31630)	stacker-unrecoverable-failure

stackerRecoverableStorageError(31631)	stacker-recoverable-storage-error

stackerUnrecoverableStorageError(31632)	stacker-unrecoverable-storage-error

stackerMotorFailure(31633)	stacker-motor-failure

stackerMemoryExhausted(31634)	stacker-memory-exhausted

stackerUnderTemperature(31635)	stacker-under-temperature

stackerOverTemperature(31636)	stacker-over-temperature

stackerTimingFailure(31637)	stacker-timing-failure

stackerThermistorFailure(31638)	stacker-thermistor-failure

-- FinDeviceTypeTC = sheetRotator(17)

sheetRotatorCoverOpen(31703)	sheet-rotator-cover-open

sheetRotatorCoverClosed(31704)	sheet-rotator-cover-closed

sheetRotatorInterlockOpen(31705)	sheet-rotator-interlock-open

sheetRotatorInterlockClosed(31706)	sheet-rotator-interlock-closed

sheetRotatorConfigurationChange(31707)	sheet-rotator-configuration-change

sheetRotatorJam(31708)	sheet-rotator-jam

sheetRotatorMissing(31709)	sheet-rotator-missing

sheetRotatorLifeAlmostOver(31710)	sheet-rotator-life-almost-over

sheetRotatorLifeOver(31711)	sheet-rotator-life-over

sheetRotatorAlmostEmpty(31712)	sheet-rotator-almost-empty

sheetRotatorEmpty(31713)	sheet-rotator-empty

sheetRotatorAlmostFull(31714)	sheet-rotator-almost-full

sheetRotatorFull(31715)	sheet-rotator-full

sheetRotatorNearLimit(31716)	sheet-rotator-near-limit

sheetRotatorAtLimit(31717)	sheet-rotator-at-limit

sheetRotatorOpened(31718)	sheet-rotator-opened

sheetRotatorClosed(31719)	sheet-rotator-closed

sheetRotatorTurnedOn(31720)	sheet-rotator-turned-on

sheetRotatorTurnedOff(31721)	sheet-rotator-turned-off

sheetRotatorOffline(31722)	sheet-rotator-offline

sheetRotatorPowerSaver(31723)	sheet-rotator-power-saver

sheetRotatorWarmingUp(31724)	sheet-rotator-warming-up

sheetRotatorAdded(31725)	sheet-rotator-added

sheetRotatorRemoved(31726)	sheet-rotator-removed

sheetRotatorResourceAdded(31727)	sheet-rotator-resource-added

sheetRotatorResourceRemoved(31728)	sheet-rotator-resource-removed

sheetRotatorRecoverableFailure(31729)	sheet-rotator-recoverable-failure

sheetRotatorUnrecoverableFailure(31730)	sheet-rotator-unrecoverable-failure

sheetRotatorRecoverableStorageError(31731)	sheet-rotator-recoverable-storage-error

sheetRotatorUnrecoverableStorageError(31732)	sheet-rotator-unrecoverable-storage-error

sheetRotatorMotorFailure(31733)	sheet-rotator-motor-failure

sheetRotatorMemoryExhausted(31734)	sheet-rotator-memory-exhausted

sheetRotatorUnderTemperature(31735)	sheet-rotator-under-temperature

sheetRotatorOverTemperature(31736)	sheet-rotator-over-temperature

sheetRotatorTimingFailure(31737)	sheet-rotator-timing-failure

sheetRotatorThermistorFailure(31738)	sheet-rotator-thermistor-failure

-- FinDeviceTypeTC = inserter(18)

inserterCoverOpen(31803)	inserter-cover-open

inserterCoverClosed(31804)	inserter-cover-closed

inserterInterlockOpen(31805)	inserter-interlock-open

inserterInterlockClosed(31806)	inserter-interlock-closed

inserterConfigurationChange(31807)	inserter-configuration-change

inserterJam(31808)	inserter-jam

inserterMissing(31809)	inserter-missing

inserterLifeAlmostOver(31810)	inserter-life-almost-over

inserterLifeOver(31811)	inserter-life-over

inserterAlmostEmpty(31812)	inserter-almost-empty

inserterEmpty(31813)	inserter-empty

inserterAlmostFull(31814)	inserter-almost-full

inserterFull(31815)	inserter-full

inserterNearLimit(31816)	inserter-near-limit

inserterAtLimit(31817)	inserter-at-limit

inserterOpened(31818)	inserter-opened

inserterClosed(31819)	inserter-closed

inserterTurnedOn(31820)	inserter-turned-on

inserterTurnedOff(31821)	inserter-turned-off

inserterOffline(31822)	inserter-offline

inserterPowerSaver(31823)	inserter-power-saver

inserterWarmingUp(31824)	inserter-warming-up

inserterAdded(31825)	inserter-added

inserterRemoved(31826)	inserter-removed

inserterResourceAdded(31827)	inserter-resource-added

inserterResourceRemoved(31828)	inserter-resource-removed

inserterRecoverableFailure(31829)	inserter-recoverable-failure

inserterUnrecoverableFailure(31830)	inserter-unrecoverable-failure

inserterRecoverableStorageError(31831)	inserter-recoverable-storage-error

inserterUnrecoverableStorageError(31832)	inserter-unrecoverable-storage-error

inserterMotorFailure(31833)	inserter-motor-failure

inserterMemoryExhausted(31834)	inserter-memory-exhausted

inserterUnderTemperature(31835)	inserter-under-temperature

inserterOverTemperature(31836)	inserter-over-temperature

inserterTimingFailure(31837)	inserter-timing-failure

inserterThermistorFailure(31838)	inserter-thermistor-failure

#### Conformance

- For interoperability, IPP implementations that claim conformance to this specification MUST implement the Table 6-1 standard mappings between existing values of 'FinDeviceTypeTC' [IANAFIN] and new values of 'PrtAlertCodeTC' [IANAPRT] and new values of "printer-state-reasons" [RFC2911].

- For interoperability, IPP implementations that claim conformance to this specification MUST implement the Table 6-1 standard mappings between existing values of 'FinStitchingTypeTC' [IANAFIN] and new values of ' PrtAlertCodeTC' [IANAPRT] and new values of "printer-state-reasons" [RFC2911].

#### Rationale for New Finishing Alert Codes

In this specification, existing enumerated values of 'FinDeviceTypeTC' [IANAFIN] (e.g., 'binder(5)') are mapped algorithmically to new enumerated values of 'PrtAlertCodeTC' [IANAPRT] (e.g., 'binderJam(30508)for the following reasons:

- Unlike the base tables in IETF Printer MIB [RFC3805] (e.g., 'prtInputTable') which are mapped meaningfully to values of 'PrtAlertCodeTC' (e.g., 'inputMediaSizeChange(802)'), the base table in IETF Finisher MIB [RFC3805] ('finDeviceTable') is not currently mapped  to meaningful specific alerts.

- 'finDeviceTable' [RFC3806] entries are only distinguished by a non-index columnar object ('finDeviceType') which is NOT included in 'prtAlertTable' (and therefore NOT mapped to "printer-alert").

- Finishing alerts reported using the generic subunit alerts (e.g., 'subunitAlmostFull') are meaningless without a subsequent query of 'finDeviceTable' (impossible if SNMP is disabled).

#### Rationale for Separate Stapler and Stitcher Devices

In this specification the one value 'stitcher(3)' of 'FinDeviceTypeTC' [IANAFIN] is mapped algorithmically to _two_ new sets of enumerated values of 'PrtAlertCodeTC' [IANAPRT] (e.g., 'staplerJam(30208)' and 'stitcherJam(30308)'), based on values of 'FinStitchingTypeTC' (e.g., 'stapleTopLeft(4)' and 'saddleStitch(8)') in the 'stitchingType(30)' attribute in 'finDeviceAttributeTable'for the following reasons:

- Both 'staple' and 'stitch' finishing processes and devices are defined in section 2.2 'Process Specific Terminology' of IETF Finisher MIB [RFC3806].

- But, unlike all other finishing processes in IETF Finisher MIB [RFC3806], the 'stapler' and 'stitcher' device types were merged into a single 'stitcher(3)' value of 'FinDeviceTypeTC' in IANA Finisher MIB [IANAFIN].

- For the 'finDeviceType' non-index object in 'finDeviceTable' [RFC3806], the 'stapler' versus 'stitcher' finishing device types are only disambiguated via values of 'FinStitchingTypeTC' in IANA Finisher MIB [IANAFIN] for the 'stitchingType(30)' attribute in 'finDeviceAttributeTable' in the IETF Finisher MIB [RFC3806].

### Conventions for Alert Code Numbering

Printer MIB v1/v2 [RFC1759] [RFC3805] follows a convention that values of 'PrtAlertCodeTC' (e.g., 'inputMediaTrayMissing(801)') are defined in ranges found by multiplying the corresponding value of 'PrtAlertGroupTC' (e.g., 'input(8)') by 100 and skipping the even hundred (e.g., '800'). For example, 'input(8)' maps to a range of '801' to '899'.

But specific alert codes for Finishing Subunits also need the context of the value of 'FinDeviceTypeTC' [IANAFIN] in the 'finDeviceType' non-index object in the 'finDeviceTable' [RFC3806], because this object is NOT encoded in 'prtAlertTable' [RFC3805].

Therefore, this specification defines a new convention that specific alert code values for Finishing Subunits (e.g., 'slitterJam(31001)') MUST be mapped from existing values of 'FinDeviceTypeTC' [IANAFIN] (e.g., 'slitter(10') in ranges of '3nn01' to '3nn99', to avoid colliding with new alert groups that may be added to 'PrtAlertGroupTC' in the future.

This specification also defines a new convention specific alert code values for 'stapler' and 'stitcher' finishing. Device types are defined in two parallel ranges. See section 6.1.1.3 'Rationale for Stapler and 'Stitcher Devices' for more details.

# Conformance Requirements

## IPP Printer Conformance Requirements

To claim conformance to this specification, an IPP Printer implementation MUST support:

- The REQUIRED IPP Printer attribute printer-state-reasons including the mappings of existing values (section 5.1.2) and new values (sections 5.1.3 and 5.1.4) defined in this specification.

- The REQUIRED IPP Printer attribute printer-alert (section 5.2) defined in this specification.

- The REQUIRED IPP Printer attribute printer-alert-description (section 5.3) defined in this specification.

- The IDENTICAL set of REQUIRED IPP Printer attribute printer-alert.alert-code values as are supported in the corresponding prtAlertCode object defined in the IETF Printer MIB v2 [RFC3805] and/or the corresponding CodeName property defined in the the DMTF CIM_PrintAlertRecord class [CIMALERT].

- The conformance requirements for an IPP Object specified in section 5.2 of [RFC2911].

- The conformance requirements for IPP Internationalization Considerations (see section 9).

- The conformance requirements for IPP Security Considerations (see section 10) defined in this specification.

## IPP Client Conformance Requirements

To claim conformance to this specification, an IPP Client implementation MUST support:

- The REQUIRED IPP Printer attribute printer-state-reasons including the mappings of existing values (section 5.1.2) and new values (sections 5.1.3 and 5.1.4) defined in this specification.

- The REQUIRED IPP Printer attribute printer-alert (section 5.2) defined in this specification.

- The REQUIRED IPP Printer attribute printer-alert-description (section 5.3) defined in this specification.

- The IDENTICAL set of REQUIRED IPP Printer attribute printer-alert.alert-code values as are supported in the corresponding prtAlertCode object defined in the IETF Printer MIB v2 [RFC3805] and/or the corresponding CodeName property defined in the the DMTF CIM_PrintAlertRecord class [CIMALERT].

- The conformance requirements for an IPP Object specified in section 5.2 of [RFC2911].

- The conformance requirements for IPP Internationalization Considerations (see section 9).

- The conformance requirements for IPP Security Considerations (see section 10) defined in this specification.

## Printer MIB Agent Conformance Requirements

To claim conformance to this specification, a Printer MIB Agent implementation MUST support:

- The IDENTICAL set of prtAlertCode object values defined in section 6.1 of this specification and in the IETF Printer MIB v2 [RFC3805] as are supported in the corresponding IPP printer-state-reasons attribute defined in section 5.1 of this specification and in IPP/1.1 [RFC2911] and/or the corresponding CodeName property defined in the the DMTF CIM_PrintAlertRecord class [CIMALERT].

- All of the finishing prtAlertCode object values defined in section 6.1 of this specification that apply to the Printer MIB Agent implementation (i.e., for supported finishing device types).

## Printer MIB Client Conformance Requirements

To claim conformance to this specification, a Printer MIB Client implementation MUST support:

- The IDENTICAL set of prtAlertCode object values defined in section 6.1 of this specification and in the IETF Printer MIB v2 [RFC3805] as are supported in the corresponding IPP printer-state-reasons attribute defined in section 5.1 of this specification and in IPP/1.1 [RFC2911] and/or the corresponding CodeName property defined in the the DMTF CIM_PrintAlertRecord class [CIMALERT].

- All of the finishing prtAlertCode object values defined in section 6.1 of this specification that apply to the Printer MIB Client implementation (i.e., for supported finishing device types).

# IANA Considerations

## IPP Attributes and Keyword Values Registrations

This section contains the updates for IANA to add to the IANA IPP Registry [IANAIPP] according to the procedures defined in section 6 of [RFC2911] to cover the definitions in this document. The resulting registrations will be published in:

http://www.iana.org/assignments/ipp-registrations

Table 8-1 - IPP Attributes and Keyword Values for IANA

Attribute Name (attribute syntax)               Reference     Section

---------------------------------               ---------     -------

printer-alert (1setOf octetString(MAX))         [PWG5100.9]   5.2

printer-alert-description (1setOf text(MAX))    [PWG5100.9]   5.3

printer-state-reasons (1setOf type2 keyword)    [RFC2911]     4.4.12

alert-removal-of-binary-change-entry          [PWG5100.9]   5.1.3

configuration-change                          [PWG5100.9]   5.1.3

input-cannot-feed-size-selected               [PWG5100.9]   5.1.3

input-manual-input-request                    [PWG5100.9]   5.1.3

input-media-color-change                      [PWG5100.9]   5.1.3

input-media-form-parts-change                 [PWG5100.9]   5.1.3

input-media-size-change                       [PWG5100.9]   5.1.3

input-media-type-change                       [PWG5100.9]   5.1.3

input-media-weight-change                     [PWG5100.9]   5.1.3

input-tray-elevation-failure                  [PWG5100.9]   5.1.3

input-tray-position-failure                   [PWG5100.9]   5.1.3

interlock-closed                              [PWG5100.9]   5.1.3

interpreter-cartridge-added                   [PWG5100.9]   5.1.3

interpreter-cartridge-deleted                 [PWG5100.9]   5.1.3

interpreter-complex-page-encountered          [PWG5100.9]   5.1.3

interpreter-memory-decrease                   [PWG5100.9]   5.1.3

interpreter-memory-increase                   [PWG5100.9]   5.1.3

interpreter-resource-added                    [PWG5100.9]   5.1.3

interpreter-resource-deleted                  [PWG5100.9]   5.1.3

marker-adjusting-print-quality                [PWG5100.9]   5.1.3

marker-developer-almost-empty                 [PWG5100.9]   5.1.3

marker-developer-empty                        [PWG5100.9]   5.1.3

marker-fuser-thermistor-failure               [PWG5100.9]   5.1.3

marker-fuser-timing-failure                   [PWG5100.9]   5.1.3

marker-ink-almost-empty                       [PWG5100.9]   5.1.3

marker-ink-empty                              [PWG5100.9]   5.1.3

marker-print-ribbon-almost-empty              [PWG5100.9]   5.1.3

marker-print-ribbon-empty                     [PWG5100.9]   5.1.3

marker-toner-cartridge-missing                [PWG5100.9]   5.1.3

marker-waste-ink-receptacle-almost-full       [PWG5100.9]   5.1.3

marker-waste-ink-receptacle-full              [PWG5100.9]   5.1.3

marker-waste-toner-receptacle-almost-full     [PWG5100.9]   5.1.3

marker-waste-toner-receptacle-full            [PWG5100.9]   5.1.3

media-path-cannot-duplex-media-selected       [PWG5100.9]   5.1.3

media-path-media-tray-almost-full             [PWG5100.9]   5.1.3

media-path-media-tray-full                    [PWG5100.9]   5.1.3

media-path-media-tray-missing                 [PWG5100.9]   5.1.3

output-mailbox-select-failure                 [PWG5100.9]   5.1.3

power-down                                    [PWG5100.9]   5.1.3

power-up                                      [PWG5100.9]   5.1.3

printer-manual-reset                          [PWG5100.9]   5.1.3

printer-nms-reset                             [PWG5100.9]   5.1.3

printer-ready-to-print                        [PWG5100.9]   5.1.3

subunit-added                                 [PWG5100.9]   5.1.3

subunit-almost-empty                          [PWG5100.9]   5.1.3

subunit-almost-full                           [PWG5100.9]   5.1.3

subunit-at-limit                              [PWG5100.9]   5.1.3

subunit-closed                                [PWG5100.9]   5.1.3

subunit-empty                                 [PWG5100.9]   5.1.3

subunit-full                                  [PWG5100.9]   5.1.3

subunit-life-almost-over                      [PWG5100.9]   5.1.3

subunit-life-over                             [PWG5100.9]   5.1.3

subunit-memory-exhausted                      [PWG5100.9]   5.1.3

subunit-missing                               [PWG5100.9]   5.1.3

subunit-motor-failure                         [PWG5100.9]   5.1.3

subunit-near-limit                            [PWG5100.9]   5.1.3

subunit-offline                               [PWG5100.9]   5.1.3

subunit-opened                                [PWG5100.9]   5.1.3

subunit-over-temperature                      [PWG5100.9]   5.1.3

subunit-power-saver                           [PWG5100.9]   5.1.3

subunit-recoverable-failure                   [PWG5100.9]   5.1.3

subunit-recoverable-storage-error             [PWG5100.9]   5.1.3

subunit-removed                               [PWG5100.9]   5.1.3

subunit-resource-added                        [PWG5100.9]   5.1.3

subunit-resource-removed                      [PWG5100.9]   5.1.3

subunit-thermistor-failure                    [PWG5100.9]   5.1.3

subunit-timing-Failure                        [PWG5100.9]   5.1.3

subunit-turned-off                            [PWG5100.9]   5.1.3

subunit-turned-on                             [PWG5100.9]   5.1.3

subunit-under-temperature                     [PWG5100.9]   5.1.3

subunit-unrecoverable-failure                 [PWG5100.9]   5.1.3

subunit-unrecoverable-storage-error           [PWG5100.9]   5.1.3

subunit-warming-up                            [PWG5100.9]   5.1.3

unknown                                       [PWG5100.9]   5.1.3

bander-added                                  [PWG5100.9]   6.1.1

bander-almost-empty                           [PWG5100.9]   6.1.1

bander-almost-full                            [PWG5100.9]   6.1.1

bander-at-limit                               [PWG5100.9]   6.1.1

bander-closed                                 [PWG5100.9]   6.1.1

bander-configuration-change                   [PWG5100.9]   6.1.1

bander-cover-closed                           [PWG5100.9]   6.1.1

bander-cover-open                             [PWG5100.9]   6.1.1

bander-empty                                  [PWG5100.9]   6.1.1

bander-full                                   [PWG5100.9]   6.1.1

bander-interlock-closed                       [PWG5100.9]   6.1.1

bander-interlock-open                         [PWG5100.9]   6.1.1

bander-jam                                    [PWG5100.9]   6.1.1

bander-life-almost-over                       [PWG5100.9]   6.1.1

bander-life-over                              [PWG5100.9]   6.1.1

bander-memory-exhausted                       [PWG5100.9]   6.1.1

bander-missing                                [PWG5100.9]   6.1.1

bander-motor-failure                          [PWG5100.9]   6.1.1

bander-near-limit                             [PWG5100.9]   6.1.1

bander-offline                                [PWG5100.9]   6.1.1

bander-opened                                 [PWG5100.9]   6.1.1

bander-over-temperature                       [PWG5100.9]   6.1.1

bander-power-saver                            [PWG5100.9]   6.1.1

bander-recoverable-failure                    [PWG5100.9]   6.1.1

bander-recoverable-storage-error              [PWG5100.9]   6.1.1

bander-removed                                [PWG5100.9]   6.1.1

bander-resource-added                         [PWG5100.9]   6.1.1

bander-resource-removed                       [PWG5100.9]   6.1.1

bander-thermistor-failure                     [PWG5100.9]   6.1.1

bander-timing-failure                         [PWG5100.9]   6.1.1

bander-turned-off                             [PWG5100.9]   6.1.1

bander-turned-on                              [PWG5100.9]   6.1.1

bander-under-temperature                      [PWG5100.9]   6.1.1

bander-unrecoverable-failure                  [PWG5100.9]   6.1.1

bander-unrecoverable-storage-error            [PWG5100.9]   6.1.1

bander-warming-up                             [PWG5100.9]   6.1.1

binder-added                                  [PWG5100.9]   6.1.1

binder-almost-empty                           [PWG5100.9]   6.1.1

binder-almost-full                            [PWG5100.9]   6.1.1

binder-at-limit                               [PWG5100.9]   6.1.1

binder-closed                                 [PWG5100.9]   6.1.1

binder-configuration-change                   [PWG5100.9]   6.1.1

binder-cover-closed                           [PWG5100.9]   6.1.1

binder-cover-open                             [PWG5100.9]   6.1.1

binder-empty                                  [PWG5100.9]   6.1.1

binder-full                                   [PWG5100.9]   6.1.1

binder-interlock-closed                       [PWG5100.9]   6.1.1

binder-interlock-open                         [PWG5100.9]   6.1.1

binder-jam                                    [PWG5100.9]   6.1.1

binder-life-almost-over                       [PWG5100.9]   6.1.1

binder-life-over                              [PWG5100.9]   6.1.1

binder-memory-exhausted                       [PWG5100.9]   6.1.1

binder-missing                                [PWG5100.9]   6.1.1

binder-motor-failure                          [PWG5100.9]   6.1.1

binder-near-limit                             [PWG5100.9]   6.1.1

binder-offline                                [PWG5100.9]   6.1.1

binder-opened                                 [PWG5100.9]   6.1.1

binder-over-temperature                       [PWG5100.9]   6.1.1

binder-power-saver                            [PWG5100.9]   6.1.1

binder-recoverable-failure                    [PWG5100.9]   6.1.1

binder-recoverable-storage-error              [PWG5100.9]   6.1.1

binder-removed                                [PWG5100.9]   6.1.1

binder-resource-added                         [PWG5100.9]   6.1.1

binder-resource-removed                       [PWG5100.9]   6.1.1

binder-thermistor-failure                     [PWG5100.9]   6.1.1

binder-timing-failure                         [PWG5100.9]   6.1.1

binder-turned-off                             [PWG5100.9]   6.1.1

binder-turned-on                              [PWG5100.9]   6.1.1

binder-under-temperature                      [PWG5100.9]   6.1.1

binder-unrecoverable-failure                  [PWG5100.9]   6.1.1

binder-unrecoverable-storage-error            [PWG5100.9]   6.1.1

binder-warming-up                             [PWG5100.9]   6.1.1

die-cutter-added                              [PWG5100.9]   6.1.1

die-cutter-almost-empty                       [PWG5100.9]   6.1.1

die-cutter-almost-full                        [PWG5100.9]   6.1.1

die-cutter-at-limit                           [PWG5100.9]   6.1.1

die-cutter-closed                             [PWG5100.9]   6.1.1

die-cutter-configuration-change               [PWG5100.9]   6.1.1

die-cutter-cover-closed                       [PWG5100.9]   6.1.1

die-cutter-cover-open                         [PWG5100.9]   6.1.1

die-cutter-empty                              [PWG5100.9]   6.1.1

die-cutter-full                               [PWG5100.9]   6.1.1

die-cutter-interlock-closed                   [PWG5100.9]   6.1.1

die-cutter-interlock-open                     [PWG5100.9]   6.1.1

die-cutter-jam                                [PWG5100.9]   6.1.1

die-cutter-life-almost-over                   [PWG5100.9]   6.1.1

die-cutter-life-over                          [PWG5100.9]   6.1.1

die-cutter-memory-exhausted                   [PWG5100.9]   6.1.1

die-cutter-missing                            [PWG5100.9]   6.1.1

die-cutter-motor-failure                      [PWG5100.9]   6.1.1

die-cutter-near-limit                         [PWG5100.9]   6.1.1

die-cutter-offline                            [PWG5100.9]   6.1.1

die-cutter-opened                             [PWG5100.9]   6.1.1

die-cutter-over-temperature                   [PWG5100.9]   6.1.1

die-cutter-power-saver                        [PWG5100.9]   6.1.1

die-cutter-recoverable-failure                [PWG5100.9]   6.1.1

die-cutter-recoverable-storage-error          [PWG5100.9]   6.1.1

die-cutter-removed                            [PWG5100.9]   6.1.1

die-cutter-resource-added                     [PWG5100.9]   6.1.1

die-cutter-resource-removed                   [PWG5100.9]   6.1.1

die-cutter-thermistor-failure                 [PWG5100.9]   6.1.1

die-cutter-timing-failure                     [PWG5100.9]   6.1.1

die-cutter-turned-off                         [PWG5100.9]   6.1.1

die-cutter-turned-on                          [PWG5100.9]   6.1.1

die-cutter-under-temperature                  [PWG5100.9]   6.1.1

die-cutter-unrecoverable-failure              [PWG5100.9]   6.1.1

die-cutter-unrecoverable-storage-error        [PWG5100.9]   6.1.1

die-cutter-warming-up                         [PWG5100.9]   6.1.1

folder-added                                  [PWG5100.9]   6.1.1

folder-almost-empty                           [PWG5100.9]   6.1.1

folder-almost-full                            [PWG5100.9]   6.1.1

folder-at-limit                               [PWG5100.9]   6.1.1

folder-closed                                 [PWG5100.9]   6.1.1

folder-configuration-change                   [PWG5100.9]   6.1.1

folder-cover-closed                           [PWG5100.9]   6.1.1

folder-cover-open                             [PWG5100.9]   6.1.1

folder-empty                                  [PWG5100.9]   6.1.1

folder-full                                   [PWG5100.9]   6.1.1

folder-interlock-closed                       [PWG5100.9]   6.1.1

folder-interlock-open                         [PWG5100.9]   6.1.1

folder-jam                                    [PWG5100.9]   6.1.1

folder-life-almost-over                       [PWG5100.9]   6.1.1

folder-life-over                              [PWG5100.9]   6.1.1

folder-memory-exhausted                       [PWG5100.9]   6.1.1

folder-missing                                [PWG5100.9]   6.1.1

folder-motor-failure                          [PWG5100.9]   6.1.1

folder-near-limit                             [PWG5100.9]   6.1.1

folder-offline                                [PWG5100.9]   6.1.1

folder-opened                                 [PWG5100.9]   6.1.1

folder-over-temperature                       [PWG5100.9]   6.1.1

folder-power-saver                            [PWG5100.9]   6.1.1

folder-recoverable-failure                    [PWG5100.9]   6.1.1

folder-recoverable-storage-error              [PWG5100.9]   6.1.1

folder-removed                                [PWG5100.9]   6.1.1

folder-resource-added                         [PWG5100.9]   6.1.1

folder-resource-removed                       [PWG5100.9]   6.1.1

folder-thermistor-failure                     [PWG5100.9]   6.1.1

folder-timing-failure                         [PWG5100.9]   6.1.1

folder-turned-off                             [PWG5100.9]   6.1.1

folder-turned-on                              [PWG5100.9]   6.1.1

folder-under-temperature                      [PWG5100.9]   6.1.1

folder-unrecoverable-failure                  [PWG5100.9]   6.1.1

folder-unrecoverable-storage-error            [PWG5100.9]   6.1.1

folder-warming-up                             [PWG5100.9]   6.1.1

imprinter-added                               [PWG5100.9]   6.1.1

imprinter-almost-empty                        [PWG5100.9]   6.1.1

imprinter-almost-full                         [PWG5100.9]   6.1.1

imprinter-at-limit                            [PWG5100.9]   6.1.1

imprinter-closed                              [PWG5100.9]   6.1.1

imprinter-configuration-change                [PWG5100.9]   6.1.1

imprinter-cover-closed                        [PWG5100.9]   6.1.1

imprinter-cover-open                          [PWG5100.9]   6.1.1

imprinter-empty                               [PWG5100.9]   6.1.1

imprinter-full                                [PWG5100.9]   6.1.1

imprinter-interlock-closed                    [PWG5100.9]   6.1.1

imprinter-interlock-open                      [PWG5100.9]   6.1.1

imprinter-jam                                 [PWG5100.9]   6.1.1

imprinter-life-almost-over                    [PWG5100.9]   6.1.1

imprinter-life-over                           [PWG5100.9]   6.1.1

imprinter-memory-exhausted                    [PWG5100.9]   6.1.1

imprinter-missing                             [PWG5100.9]   6.1.1

imprinter-motor-failure                       [PWG5100.9]   6.1.1

imprinter-near-limit                          [PWG5100.9]   6.1.1

imprinter-offline                             [PWG5100.9]   6.1.1

imprinter-opened                              [PWG5100.9]   6.1.1

imprinter-over-temperature                    [PWG5100.9]   6.1.1

imprinter-power-saver                         [PWG5100.9]   6.1.1

imprinter-recoverable-failure                 [PWG5100.9]   6.1.1

imprinter-recoverable-storage-error           [PWG5100.9]   6.1.1

imprinter-removed                             [PWG5100.9]   6.1.1

imprinter-resource-added                      [PWG5100.9]   6.1.1

imprinter-resource-removed                    [PWG5100.9]   6.1.1

imprinter-thermistor-failure                  [PWG5100.9]   6.1.1

imprinter-timing-failure                      [PWG5100.9]   6.1.1

imprinter-turned-off                          [PWG5100.9]   6.1.1

imprinter-turned-on                           [PWG5100.9]   6.1.1

imprinter-under-temperature                   [PWG5100.9]   6.1.1

imprinter-unrecoverable-failure               [PWG5100.9]   6.1.1

imprinter-unrecoverable-storage-error         [PWG5100.9]   6.1.1

imprinter-warming-up                          [PWG5100.9]   6.1.1

inserter-added                                [PWG5100.9]   6.1.1

inserter-almost-empty                         [PWG5100.9]   6.1.1

inserter-almost-full                          [PWG5100.9]   6.1.1

inserter-at-limit                             [PWG5100.9]   6.1.1

inserter-closed                               [PWG5100.9]   6.1.1

inserter-configuration-change                 [PWG5100.9]   6.1.1

inserter-cover-closed                         [PWG5100.9]   6.1.1

inserter-cover-open                           [PWG5100.9]   6.1.1

inserter-empty                                [PWG5100.9]   6.1.1

inserter-full                                 [PWG5100.9]   6.1.1

inserter-interlock-closed                     [PWG5100.9]   6.1.1

inserter-interlock-open                       [PWG5100.9]   6.1.1

inserter-jam                                  [PWG5100.9]   6.1.1

inserter-life-almost-over                     [PWG5100.9]   6.1.1

inserter-life-over                            [PWG5100.9]   6.1.1

inserter-memory-exhausted                     [PWG5100.9]   6.1.1

inserter-missing                              [PWG5100.9]   6.1.1

inserter-motor-failure                        [PWG5100.9]   6.1.1

inserter-near-limit                           [PWG5100.9]   6.1.1

inserter-offline                              [PWG5100.9]   6.1.1

inserter-opened                               [PWG5100.9]   6.1.1

inserter-over-temperature                     [PWG5100.9]   6.1.1

inserter-power-saver                          [PWG5100.9]   6.1.1

inserter-recoverable-failure                  [PWG5100.9]   6.1.1

inserter-recoverable-storage-error            [PWG5100.9]   6.1.1

inserter-removed                              [PWG5100.9]   6.1.1

inserter-resource-added                       [PWG5100.9]   6.1.1

inserter-resource-removed                     [PWG5100.9]   6.1.1

inserter-thermistor-failure                   [PWG5100.9]   6.1.1

inserter-timing-failure                       [PWG5100.9]   6.1.1

inserter-turned-off                           [PWG5100.9]   6.1.1

inserter-turned-on                            [PWG5100.9]   6.1.1

inserter-under-temperature                    [PWG5100.9]   6.1.1

inserter-unrecoverable-failure                [PWG5100.9]   6.1.1

inserter-unrecoverable-storage-error          [PWG5100.9]   6.1.1

inserter-warming-up                           [PWG5100.9]   6.1.1

make-envelope-added                           [PWG5100.9]   6.1.1

make-envelope-almost-empty                    [PWG5100.9]   6.1.1

make-envelope-almost-full                     [PWG5100.9]   6.1.1

make-envelope-at-limit                        [PWG5100.9]   6.1.1

make-envelope-closed                          [PWG5100.9]   6.1.1

make-envelope-configuration-change            [PWG5100.9]   6.1.1

make-envelope-cover-closed                    [PWG5100.9]   6.1.1

make-envelope-cover-open                      [PWG5100.9]   6.1.1

make-envelope-empty                           [PWG5100.9]   6.1.1

make-envelope-full                            [PWG5100.9]   6.1.1

make-envelope-interlock-closed                [PWG5100.9]   6.1.1

make-envelope-interlock-open                  [PWG5100.9]   6.1.1

make-envelope-jam                             [PWG5100.9]   6.1.1

make-envelope-life-almost-over                [PWG5100.9]   6.1.1

make-envelope-life-over                       [PWG5100.9]   6.1.1

make-envelope-memory-exhausted                [PWG5100.9]   6.1.1

make-envelope-missing                         [PWG5100.9]   6.1.1

make-envelope-motor-failure                   [PWG5100.9]   6.1.1

make-envelope-near-limit                      [PWG5100.9]   6.1.1

make-envelope-offline                         [PWG5100.9]   6.1.1

make-envelope-opened                          [PWG5100.9]   6.1.1

make-envelope-over-temperature                [PWG5100.9]   6.1.1

make-envelope-power-saver                     [PWG5100.9]   6.1.1

make-envelope-recoverable-failure             [PWG5100.9]   6.1.1

make-envelope-recoverable-storage-error       [PWG5100.9]   6.1.1

make-envelope-removed                         [PWG5100.9]   6.1.1

make-envelope-resource-added                  [PWG5100.9]   6.1.1

make-envelope-resource-removed                [PWG5100.9]   6.1.1

make-envelope-thermistor-failure              [PWG5100.9]   6.1.1

make-envelope-timing-failure                  [PWG5100.9]   6.1.1

make-envelope-turned-off                      [PWG5100.9]   6.1.1

make-envelope-turned-on                       [PWG5100.9]   6.1.1

make-envelope-under-temperature               [PWG5100.9]   6.1.1

make-envelope-unrecoverable-failure           [PWG5100.9]   6.1.1

make-envelope-unrecoverable-storage-error     [PWG5100.9]   6.1.1

make-envelope-warming-up                      [PWG5100.9]   6.1.1

perforater-added                              [PWG5100.9]   6.1.1

perforater-almost-empty                       [PWG5100.9]   6.1.1

perforater-almost-full                        [PWG5100.9]   6.1.1

perforater-at-limit                           [PWG5100.9]   6.1.1

perforater-closed                             [PWG5100.9]   6.1.1

perforater-configuration-change               [PWG5100.9]   6.1.1

perforater-cover-closed                       [PWG5100.9]   6.1.1

perforater-cover-open                         [PWG5100.9]   6.1.1

perforater-empty                              [PWG5100.9]   6.1.1

perforater-full                               [PWG5100.9]   6.1.1

perforater-interlock-closed                   [PWG5100.9]   6.1.1

perforater-interlock-open                     [PWG5100.9]   6.1.1

perforater-jam                                [PWG5100.9]   6.1.1

perforater-life-almost-over                   [PWG5100.9]   6.1.1

perforater-life-over                          [PWG5100.9]   6.1.1

perforater-memory-exhausted                   [PWG5100.9]   6.1.1

perforater-missing                            [PWG5100.9]   6.1.1

perforater-motor-failure                      [PWG5100.9]   6.1.1

perforater-near-limit                         [PWG5100.9]   6.1.1

perforater-offline                            [PWG5100.9]   6.1.1

perforater-opened                             [PWG5100.9]   6.1.1

perforater-over-temperature                   [PWG5100.9]   6.1.1

perforater-power-saver                        [PWG5100.9]   6.1.1

perforater-recoverable-failure                [PWG5100.9]   6.1.1

perforater-recoverable-storage-error          [PWG5100.9]   6.1.1

perforater-removed                            [PWG5100.9]   6.1.1

perforater-resource-added                     [PWG5100.9]   6.1.1

perforater-resource-removed                   [PWG5100.9]   6.1.1

perforater-thermistor-failure                 [PWG5100.9]   6.1.1

perforater-timing-failure                     [PWG5100.9]   6.1.1

perforater-turned-off                         [PWG5100.9]   6.1.1

perforater-turned-on                          [PWG5100.9]   6.1.1

perforater-under-temperature                  [PWG5100.9]   6.1.1

perforater-unrecoverable-failure              [PWG5100.9]   6.1.1

perforater-unrecoverable-storage-error        [PWG5100.9]   6.1.1

perforater-warming-up                         [PWG5100.9]   6.1.1

puncher-added                                 [PWG5100.9]   6.1.1

puncher-almost-empty                          [PWG5100.9]   6.1.1

puncher-almost-full                           [PWG5100.9]   6.1.1

puncher-at-limit                              [PWG5100.9]   6.1.1

puncher-closed                                [PWG5100.9]   6.1.1

puncher-configuration-change                  [PWG5100.9]   6.1.1

puncher-cover-closed                          [PWG5100.9]   6.1.1

puncher-cover-open                            [PWG5100.9]   6.1.1

puncher-empty                                 [PWG5100.9]   6.1.1

puncher-full                                  [PWG5100.9]   6.1.1

puncher-interlock-closed                      [PWG5100.9]   6.1.1

puncher-interlock-open                        [PWG5100.9]   6.1.1

puncher-jam                                   [PWG5100.9]   6.1.1

puncher-life-almost-over                      [PWG5100.9]   6.1.1

puncher-life-over                             [PWG5100.9]   6.1.1

puncher-memory-exhausted                      [PWG5100.9]   6.1.1

puncher-missing                               [PWG5100.9]   6.1.1

puncher-motor-failure                         [PWG5100.9]   6.1.1

puncher-near-limit                            [PWG5100.9]   6.1.1

puncher-offline                               [PWG5100.9]   6.1.1

puncher-opened                                [PWG5100.9]   6.1.1

puncher-over-temperature                      [PWG5100.9]   6.1.1

puncher-power-saver                           [PWG5100.9]   6.1.1

puncher-recoverable-failure                   [PWG5100.9]   6.1.1

puncher-recoverable-storage-error             [PWG5100.9]   6.1.1

puncher-removed                               [PWG5100.9]   6.1.1

puncher-resource-added                        [PWG5100.9]   6.1.1

puncher-resource-removed                      [PWG5100.9]   6.1.1

puncher-thermistor-failure                    [PWG5100.9]   6.1.1

puncher-timing-failure                        [PWG5100.9]   6.1.1

puncher-turned-off                            [PWG5100.9]   6.1.1

puncher-turned-on                             [PWG5100.9]   6.1.1

puncher-under-temperature                     [PWG5100.9]   6.1.1

puncher-unrecoverable-failure                 [PWG5100.9]   6.1.1

puncher-unrecoverable-storage-error           [PWG5100.9]   6.1.1

puncher-warming-up                            [PWG5100.9]   6.1.1

separation-cutter-added                       [PWG5100.9]   6.1.1

separation-cutter-almost-empty                [PWG5100.9]   6.1.1

separation-cutter-almost-full                 [PWG5100.9]   6.1.1

separation-cutter-at-limit                    [PWG5100.9]   6.1.1

separation-cutter-closed                      [PWG5100.9]   6.1.1

separation-cutter-configuration-change        [PWG5100.9]   6.1.1

separation-cutter-cover-closed                [PWG5100.9]   6.1.1

separation-cutter-cover-open                  [PWG5100.9]   6.1.1

separation-cutter-empty                       [PWG5100.9]   6.1.1

separation-cutter-full                        [PWG5100.9]   6.1.1

separation-cutter-interlock-closed            [PWG5100.9]   6.1.1

separation-cutter-interlock-open              [PWG5100.9]   6.1.1

separation-cutter-jam                         [PWG5100.9]   6.1.1

separation-cutter-life-almost-over            [PWG5100.9]   6.1.1

separation-cutter-life-over                   [PWG5100.9]   6.1.1

separation-cutter-memory-exhausted            [PWG5100.9]   6.1.1

separation-cutter-missing                     [PWG5100.9]   6.1.1

separation-cutter-motor-failure               [PWG5100.9]   6.1.1

separation-cutter-near-limit                  [PWG5100.9]   6.1.1

separation-cutter-offline                     [PWG5100.9]   6.1.1

separation-cutter-opened                      [PWG5100.9]   6.1.1

separation-cutter-over-temperature            [PWG5100.9]   6.1.1

separation-cutter-power-saver                 [PWG5100.9]   6.1.1

separation-cutter-recoverable-failure         [PWG5100.9]   6.1.1

separation-cutter-recoverable-storage-error   [PWG5100.9]   6.1.1

separation-cutter-removed                     [PWG5100.9]   6.1.1

separation-cutter-resource-added              [PWG5100.9]   6.1.1

separation-cutter-resource-removed            [PWG5100.9]   6.1.1

separation-cutter-thermistor-failure          [PWG5100.9]   6.1.1

separation-cutter-timing-failure              [PWG5100.9]   6.1.1

separation-cutter-turned-off                  [PWG5100.9]   6.1.1

separation-cutter-turned-on                   [PWG5100.9]   6.1.1

separation-cutter-under-temperature           [PWG5100.9]   6.1.1

separation-cutter-unrecoverable-failure       [PWG5100.9]   6.1.1

separation-cutter-unrecoverable-storage-error [PWG5100.9]   6.1.1

separation-cutter-warming-up                  [PWG5100.9]   6.1.1

sheet-rotator-added                           [PWG5100.9]   6.1.1

sheet-rotator-almost-empty                    [PWG5100.9]   6.1.1

sheet-rotator-almost-full                     [PWG5100.9]   6.1.1

sheet-rotator-at-limit                        [PWG5100.9]   6.1.1

sheet-rotator-closed                          [PWG5100.9]   6.1.1

sheet-rotator-configuration-change            [PWG5100.9]   6.1.1

sheet-rotator-cover-closed                    [PWG5100.9]   6.1.1

sheet-rotator-cover-open                      [PWG5100.9]   6.1.1

sheet-rotator-empty                           [PWG5100.9]   6.1.1

sheet-rotator-full                            [PWG5100.9]   6.1.1

sheet-rotator-interlock-closed                [PWG5100.9]   6.1.1

sheet-rotator-interlock-open                  [PWG5100.9]   6.1.1

sheet-rotator-jam                             [PWG5100.9]   6.1.1

sheet-rotator-life-almost-over                [PWG5100.9]   6.1.1

sheet-rotator-life-over                       [PWG5100.9]   6.1.1

sheet-rotator-memory-exhausted                [PWG5100.9]   6.1.1

sheet-rotator-missing                         [PWG5100.9]   6.1.1

sheet-rotator-motor-failure                   [PWG5100.9]   6.1.1

sheet-rotator-near-limit                      [PWG5100.9]   6.1.1

sheet-rotator-offline                         [PWG5100.9]   6.1.1

sheet-rotator-opened                          [PWG5100.9]   6.1.1

sheet-rotator-over-temperature                [PWG5100.9]   6.1.1

sheet-rotator-power-saver                     [PWG5100.9]   6.1.1

sheet-rotator-recoverable-failure             [PWG5100.9]   6.1.1

sheet-rotator-recoverable-storage-error       [PWG5100.9]   6.1.1

sheet-rotator-removed                         [PWG5100.9]   6.1.1

sheet-rotator-resource-added                  [PWG5100.9]   6.1.1

sheet-rotator-resource-removed                [PWG5100.9]   6.1.1

sheet-rotator-thermistor-failure              [PWG5100.9]   6.1.1

sheet-rotator-timing-failure                  [PWG5100.9]   6.1.1

sheet-rotator-turned-off                      [PWG5100.9]   6.1.1

sheet-rotator-turned-on                       [PWG5100.9]   6.1.1

sheet-rotator-under-temperature               [PWG5100.9]   6.1.1

sheet-rotator-unrecoverable-failure           [PWG5100.9]   6.1.1

sheet-rotator-unrecoverable-storage-error     [PWG5100.9]   6.1.1

sheet-rotator-warming-up                      [PWG5100.9]   6.1.1

slitter-added                                 [PWG5100.9]   6.1.1

slitter-almost-empty                          [PWG5100.9]   6.1.1

slitter-almost-full                           [PWG5100.9]   6.1.1

slitter-at-limit                              [PWG5100.9]   6.1.1

slitter-closed                                [PWG5100.9]   6.1.1

slitter-configuration-change                  [PWG5100.9]   6.1.1

slitter-cover-closed                          [PWG5100.9]   6.1.1

slitter-cover-open                            [PWG5100.9]   6.1.1

slitter-empty                                 [PWG5100.9]   6.1.1

slitter-full                                  [PWG5100.9]   6.1.1

slitter-interlock-closed                      [PWG5100.9]   6.1.1

slitter-interlock-open                        [PWG5100.9]   6.1.1

slitter-jam                                   [PWG5100.9]   6.1.1

slitter-life-almost-over                      [PWG5100.9]   6.1.1

slitter-life-over                             [PWG5100.9]   6.1.1

slitter-memory-exhausted                      [PWG5100.9]   6.1.1

slitter-missing                               [PWG5100.9]   6.1.1

slitter-motor-failure                         [PWG5100.9]   6.1.1

slitter-near-limit                            [PWG5100.9]   6.1.1

slitter-offline                               [PWG5100.9]   6.1.1

slitter-opened                                [PWG5100.9]   6.1.1

slitter-over-temperature                      [PWG5100.9]   6.1.1

slitter-power-saver                           [PWG5100.9]   6.1.1

slitter-recoverable-failure                   [PWG5100.9]   6.1.1

slitter-recoverable-storage-error             [PWG5100.9]   6.1.1

slitter-removed                               [PWG5100.9]   6.1.1

slitter-resource-added                        [PWG5100.9]   6.1.1

slitter-resource-removed                      [PWG5100.9]   6.1.1

slitter-thermistor-failure                    [PWG5100.9]   6.1.1

slitter-timing-failure                        [PWG5100.9]   6.1.1

slitter-turned-off                            [PWG5100.9]   6.1.1

slitter-turned-on                             [PWG5100.9]   6.1.1

slitter-under-temperature                     [PWG5100.9]   6.1.1

slitter-unrecoverable-failure                 [PWG5100.9]   6.1.1

slitter-unrecoverable-storage-error           [PWG5100.9]   6.1.1

slitter-warming-up                            [PWG5100.9]   6.1.1

stacker-added                                 [PWG5100.9]   6.1.1

stacker-almost-empty                          [PWG5100.9]   6.1.1

stacker-almost-full                           [PWG5100.9]   6.1.1

stacker-at-limit                              [PWG5100.9]   6.1.1

stacker-closed                                [PWG5100.9]   6.1.1

stacker-configuration-change                  [PWG5100.9]   6.1.1

stacker-cover-closed                          [PWG5100.9]   6.1.1

stacker-cover-open                            [PWG5100.9]   6.1.1

stacker-empty                                 [PWG5100.9]   6.1.1

stacker-full                                  [PWG5100.9]   6.1.1

stacker-interlock-closed                      [PWG5100.9]   6.1.1

stacker-interlock-open                        [PWG5100.9]   6.1.1

stacker-jam                                   [PWG5100.9]   6.1.1

stacker-life-almost-over                      [PWG5100.9]   6.1.1

stacker-life-over                             [PWG5100.9]   6.1.1

stacker-memory-exhausted                      [PWG5100.9]   6.1.1

stacker-missing                               [PWG5100.9]   6.1.1

stacker-motor-failure                         [PWG5100.9]   6.1.1

stacker-near-limit                            [PWG5100.9]   6.1.1

stacker-offline                               [PWG5100.9]   6.1.1

stacker-opened                                [PWG5100.9]   6.1.1

stacker-over-temperature                      [PWG5100.9]   6.1.1

stacker-power-saver                           [PWG5100.9]   6.1.1

stacker-recoverable-failure                   [PWG5100.9]   6.1.1

stacker-recoverable-storage-error             [PWG5100.9]   6.1.1

stacker-removed                               [PWG5100.9]   6.1.1

stacker-resource-added                        [PWG5100.9]   6.1.1

stacker-resource-removed                      [PWG5100.9]   6.1.1

stacker-thermistor-failure                    [PWG5100.9]   6.1.1

stacker-timing-failure                        [PWG5100.9]   6.1.1

stacker-turned-off                            [PWG5100.9]   6.1.1

stacker-turned-on                             [PWG5100.9]   6.1.1

stacker-under-temperature                     [PWG5100.9]   6.1.1

stacker-unrecoverable-failure                 [PWG5100.9]   6.1.1

stacker-unrecoverable-storage-error           [PWG5100.9]   6.1.1

stacker-warming-up                            [PWG5100.9]   6.1.1

stapler-added                                 [PWG5100.9]   6.1.1

stapler-almost-empty                          [PWG5100.9]   6.1.1

stapler-almost-full                           [PWG5100.9]   6.1.1

stapler-at-limit                              [PWG5100.9]   6.1.1

stapler-closed                                [PWG5100.9]   6.1.1

stapler-configuration-change                  [PWG5100.9]   6.1.1

stapler-cover-closed                          [PWG5100.9]   6.1.1

stapler-cover-open                            [PWG5100.9]   6.1.1

stapler-empty                                 [PWG5100.9]   6.1.1

stapler-full                                  [PWG5100.9]   6.1.1

stapler-interlock-closed                      [PWG5100.9]   6.1.1

stapler-interlock-open                        [PWG5100.9]   6.1.1

stapler-jam                                   [PWG5100.9]   6.1.1

stapler-life-almost-over                      [PWG5100.9]   6.1.1

stapler-life-over                             [PWG5100.9]   6.1.1

stapler-memory-exhausted                      [PWG5100.9]   6.1.1

stapler-missing                               [PWG5100.9]   6.1.1

stapler-motor-failure                         [PWG5100.9]   6.1.1

stapler-near-limit                            [PWG5100.9]   6.1.1

stapler-offline                               [PWG5100.9]   6.1.1

stapler-opened                                [PWG5100.9]   6.1.1

stapler-over-temperature                      [PWG5100.9]   6.1.1

stapler-power-saver                           [PWG5100.9]   6.1.1

stapler-recoverable-failure                   [PWG5100.9]   6.1.1

stapler-recoverable-storage-error             [PWG5100.9]   6.1.1

stapler-removed                               [PWG5100.9]   6.1.1

stapler-resource-added                        [PWG5100.9]   6.1.1

stapler-resource-removed                      [PWG5100.9]   6.1.1

stapler-thermistor-failure                    [PWG5100.9]   6.1.1

stapler-timing-failure                        [PWG5100.9]   6.1.1

stapler-turned-off                            [PWG5100.9]   6.1.1

stapler-turned-on                             [PWG5100.9]   6.1.1

stapler-under-temperature                     [PWG5100.9]   6.1.1

stapler-unrecoverable-failure                 [PWG5100.9]   6.1.1

stapler-unrecoverable-storage-error           [PWG5100.9]   6.1.1

stapler-warming-up                            [PWG5100.9]   6.1.1

stitcher-added                                [PWG5100.9]   6.1.1

stitcher-almost-empty                         [PWG5100.9]   6.1.1

stitcher-almost-full                          [PWG5100.9]   6.1.1

stitcher-at-limit                             [PWG5100.9]   6.1.1

stitcher-closed                               [PWG5100.9]   6.1.1

stitcher-configuration-change                 [PWG5100.9]   6.1.1

stitcher-cover-closed                         [PWG5100.9]   6.1.1

stitcher-cover-open                           [PWG5100.9]   6.1.1

stitcher-empty                                [PWG5100.9]   6.1.1

stitcher-full                                 [PWG5100.9]   6.1.1

stitcher-interlock-closed                     [PWG5100.9]   6.1.1

stitcher-interlock-open                       [PWG5100.9]   6.1.1

stitcher-jam                                  [PWG5100.9]   6.1.1

stitcher-life-almost-over                     [PWG5100.9]   6.1.1

stitcher-life-over                            [PWG5100.9]   6.1.1

stitcher-memory-exhausted                     [PWG5100.9]   6.1.1

stitcher-missing                              [PWG5100.9]   6.1.1

stitcher-motor-failure                        [PWG5100.9]   6.1.1

stitcher-near-limit                           [PWG5100.9]   6.1.1

stitcher-offline                              [PWG5100.9]   6.1.1

stitcher-opened                               [PWG5100.9]   6.1.1

stitcher-over-temperature                     [PWG5100.9]   6.1.1

stitcher-power-saver                          [PWG5100.9]   6.1.1

stitcher-recoverable-failure                  [PWG5100.9]   6.1.1

stitcher-recoverable-storage-error            [PWG5100.9]   6.1.1

stitcher-removed                              [PWG5100.9]   6.1.1

stitcher-resource-added                       [PWG5100.9]   6.1.1

stitcher-resource-removed                     [PWG5100.9]   6.1.1

stitcher-thermistor-failure                   [PWG5100.9]   6.1.1

stitcher-timing-failure                       [PWG5100.9]   6.1.1

stitcher-turned-off                           [PWG5100.9]   6.1.1

stitcher-turned-on                            [PWG5100.9]   6.1.1

stitcher-under-temperature                    [PWG5100.9]   6.1.1

stitcher-unrecoverable-failure                [PWG5100.9]   6.1.1

stitcher-unrecoverable-storage-error          [PWG5100.9]   6.1.1

stitcher-warming-up                           [PWG5100.9]   6.1.1

trimmer-added                                 [PWG5100.9]   6.1.1

trimmer-almost-empty                          [PWG5100.9]   6.1.1

trimmer-almost-full                           [PWG5100.9]   6.1.1

trimmer-at-limit                              [PWG5100.9]   6.1.1

trimmer-closed                                [PWG5100.9]   6.1.1

trimmer-configuration-change                  [PWG5100.9]   6.1.1

trimmer-cover-closed                          [PWG5100.9]   6.1.1

trimmer-cover-open                            [PWG5100.9]   6.1.1

trimmer-empty                                 [PWG5100.9]   6.1.1

trimmer-full                                  [PWG5100.9]   6.1.1

trimmer-interlock-closed                      [PWG5100.9]   6.1.1

trimmer-interlock-open                        [PWG5100.9]   6.1.1

trimmer-jam                                   [PWG5100.9]   6.1.1

trimmer-life-almost-over                      [PWG5100.9]   6.1.1

trimmer-life-over                             [PWG5100.9]   6.1.1

trimmer-memory-exhausted                      [PWG5100.9]   6.1.1

trimmer-missing                               [PWG5100.9]   6.1.1

trimmer-motor-failure                         [PWG5100.9]   6.1.1

trimmer-near-limit                            [PWG5100.9]   6.1.1

trimmer-offline                               [PWG5100.9]   6.1.1

trimmer-opened                                [PWG5100.9]   6.1.1

trimmer-over-temperature                      [PWG5100.9]   6.1.1

trimmer-power-saver                           [PWG5100.9]   6.1.1

trimmer-recoverable-failure                   [PWG5100.9]   6.1.1

trimmer-recoverable-storage-error             [PWG5100.9]   6.1.1

trimmer-removed                               [PWG5100.9]   6.1.1

trimmer-resource-added                        [PWG5100.9]   6.1.1

trimmer-resource-removed                      [PWG5100.9]   6.1.1

trimmer-thermistor-failure                    [PWG5100.9]   6.1.1

trimmer-timing-failure                        [PWG5100.9]   6.1.1

trimmer-turned-off                            [PWG5100.9]   6.1.1

trimmer-turned-on                             [PWG5100.9]   6.1.1

trimmer-under-temperature                     [PWG5100.9]   6.1.1

trimmer-unrecoverable-failure                 [PWG5100.9]   6.1.1

trimmer-unrecoverable-storage-error           [PWG5100.9]   6.1.1

trimmer-warming-up                            [PWG5100.9]   6.1.1

wrapper-added                                 [PWG5100.9]   6.1.1

wrapper-almost-empty                          [PWG5100.9]   6.1.1

wrapper-almost-full                           [PWG5100.9]   6.1.1

wrapper-at-limit                              [PWG5100.9]   6.1.1

wrapper-closed                                [PWG5100.9]   6.1.1

wrapper-configuration-change                  [PWG5100.9]   6.1.1

wrapper-cover-closed                          [PWG5100.9]   6.1.1

wrapper-cover-open                            [PWG5100.9]   6.1.1

wrapper-empty                                 [PWG5100.9]   6.1.1

wrapper-full                                  [PWG5100.9]   6.1.1

wrapper-interlock-closed                      [PWG5100.9]   6.1.1

wrapper-interlock-open                        [PWG5100.9]   6.1.1

wrapper-jam                                   [PWG5100.9]   6.1.1

wrapper-life-almost-over                      [PWG5100.9]   6.1.1

wrapper-life-over                             [PWG5100.9]   6.1.1

wrapper-memory-exhausted                      [PWG5100.9]   6.1.1

wrapper-missing                               [PWG5100.9]   6.1.1

wrapper-motor-failure                         [PWG5100.9]   6.1.1

wrapper-near-limit                            [PWG5100.9]   6.1.1

wrapper-offline                               [PWG5100.9]   6.1.1

wrapper-opened                                [PWG5100.9]   6.1.1

wrapper-over-temperature                      [PWG5100.9]   6.1.1

wrapper-power-saver                           [PWG5100.9]   6.1.1

wrapper-recoverable-failure                   [PWG5100.9]   6.1.1

wrapper-recoverable-storage-error             [PWG5100.9]   6.1.1

wrapper-removed                               [PWG5100.9]   6.1.1

wrapper-resource-added                        [PWG5100.9]   6.1.1

wrapper-resource-removed                      [PWG5100.9]   6.1.1

wrapper-thermistor-failure                    [PWG5100.9]   6.1.1

wrapper-timing-failure                        [PWG5100.9]   6.1.1

wrapper-turned-off                            [PWG5100.9]   6.1.1

wrapper-turned-on                             [PWG5100.9]   6.1.1

wrapper-under-temperature                     [PWG5100.9]   6.1.1

wrapper-unrecoverable-failure                 [PWG5100.9]   6.1.1

wrapper-unrecoverable-storage-error           [PWG5100.9]   6.1.1

wrapper-warming-up                            [PWG5100.9]   6.1.1

## IANA Printer MIB Alert Values Registrations

This section contains the updates for IANA to add to the IANA Printer MIB according to the procedures defined in section 7 of [RFC3805] to cover the definitions in this document. The resulting registrations will be published in:

http://www.iana.org/assignments/ianaprinter-mib

IANA should first remove the comma on the last enumerated value in the 'PrtAlertCodeTC' textual convention and then insert the following new enumerated values and ASN.1 comments on usage:

Table 8-2 - IANA Printer MIB Alert Values for IANA

-- FinDeviceTypeTC = stitcher(3) -> stapler

-- FinStitchingTypeTC = staple... (4,5,6,7, or 10)

staplerCoverOpen(30203),

staplerCoverClosed(30204),

staplerInterlockOpen(30205),

staplerInterlockClosed(30206),

staplerConfigurationChange(30207),

staplerJam(30208),

staplerMissing(30209),

staplerLifeAlmostOver(30210),

staplerLifeOver(30211),

staplerAlmostEmpty(30212),

staplerEmpty(30213),

staplerAlmostFull(30214),

staplerFull(30215),

staplerNearLimit(30216),

staplerAtLimit(30217),

staplerOpened(30218),

staplerClosed(30219),

staplerTurnedOn(30220),

staplerTurnedOff(30221),

staplerOffline(30222),

staplerPowerSaver(30223),

staplerWarmingUp(30224),

staplerAdded(30225),

staplerRemoved(30226),

staplerResourceAdded(30227),

staplerResourceRemoved(30228),

staplerRecoverableFailure(30229),

staplerUnrecoverableFailure(30230),

staplerRecoverableStorageError(30231),

staplerUnrecoverableStorageError(30232),

staplerMotorFailure(30233),

staplerMemoryExhausted(30234),

staplerUnderTemperature(30235),

staplerOverTemperature(30236),

staplerTimingFailure(30237),

staplerThermistorFailure(30238),

-- FinDeviceTypeTC = stitcher(3) -> stitcher

-- FinStitchingTypeTC = saddleStitch(8) or edgeStitch(9)

stitcherCoverOpen(30303),

stitcherCoverClosed(30304),

stitcherInterlockOpen(30305),

stitcherInterlockClosed(30306),

stitcherConfigurationChange(30307),

stitcherJam(30308),

stitcherMissing(30309),

stitcherLifeAlmostOver(30310),

stitcherLifeOver(30311),

stitcherAlmostEmpty(30312),

stitcherEmpty(30313),

stitcherAlmostFull(30314),

stitcherFull(30315),

stitcherNearLimit(30316),

stitcherAtLimit(30317),

stitcherOpened(30318),

stitcherClosed(30319),

stitcherTurnedOn(30320),

stitcherTurnedOff(30321),

stitcherOffline(30322),

stitcherPowerSaver(30323),

stitcherWarmingUp(30324),

stitcherAdded(30325),

stitcherRemoved(30326),

stitcherResourceAdded(30327),

stitcherResourceRemoved(30328),

stitcherRecoverableFailure(30329),

stitcherUnrecoverableFailure(30330),

stitcherRecoverableStorageError(30331),

stitcherUnrecoverableStorageError(30332),

stitcherMotorFailure(30333),

stitcherMemoryExhausted(30334),

stitcherUnderTemperature(30335),

stitcherOverTemperature(30336),

stitcherTimingFailure(30337),

stitcherThermistorFailure(30338),

-- FinDeviceTypeTC = folder(4)

folderCoverOpen(30403),

folderCoverClosed(30404),

folderInterlockOpen(30405),

folderInterlockClosed(30406),

folderConfigurationChange(30407),

folderJam(30408),

folderMissing(30409),

folderLifeAlmostOver(30410),

folderLifeOver(30411),

folderAlmostEmpty(30412),

folderEmpty(30413),

folderAlmostFull(30414),

folderFull(30415),

folderNearLimit(30416),

folderAtLimit(30417),

folderOpened(30418),

folderClosed(30419),

folderTurnedOn(30420),

folderTurnedOff(30421),

folderOffline(30422),

folderPowerSaver(30423),

folderWarmingUp(30424),

folderAdded(30425),

folderRemoved(30426),

folderResourceAdded(30427),

folderResourceRemoved(30428),

folderRecoverableFailure(30429),

folderUnrecoverableFailure(30430),

folderRecoverableStorageError(30431),

folderUnrecoverableStorageError(30432),

folderMotorFailure(30433),

folderMemoryExhausted(30434),

folderUnderTemperature(30435),

folderOverTemperature(30436),

folderTimingFailure(30437),

folderThermistorFailure(30438),

-- FinDeviceTypeTC = binder(5)

binderCoverOpen(30503),

binderCoverClosed(30504),

binderInterlockOpen(30505),

binderInterlockClosed(30506),

binderConfigurationChange(30507),

binderJam(30508),

binderMissing(30509),

binderLifeAlmostOver(30510),

binderLifeOver(30511),

binderAlmostEmpty(30512),

binderEmpty(30513),

binderAlmostFull(30514),

binderFull(30515),

binderNearLimit(30516),

binderAtLimit(30517),

binderOpened(30518),

binderClosed(30519),

binderTurnedOn(30520),

binderTurnedOff(30521),

binderOffline(30522),

binderPowerSaver(30523),

binderWarmingUp(30524),

binderAdded(30525),

binderRemoved(30526),

binderResourceAdded(30527),

binderResourceRemoved(30528),

binderRecoverableFailure(30529),

binderUnrecoverableFailure(30530),

binderRecoverableStorageError(30531),

binderUnrecoverableStorageError(30532),

binderMotorFailure(30533),

binderMemoryExhausted(30534),

binderUnderTemperature(30535),

binderOverTemperature(30536),

binderTimingFailure(30537),

binderThermistorFailure(30538),

-- FinDeviceTypeTC = trimmer(6)

trimmerCoverOpen(30603),

trimmerCoverClosed(30604),

trimmerInterlockOpen(30605),

trimmerInterlockClosed(30606),

trimmerConfigurationChange(30607),

trimmerJam(30608),

trimmerMissing(30609),

trimmerLifeAlmostOver(30610),

trimmerLifeOver(30611),

trimmerAlmostEmpty(30612),

trimmerEmpty(30613),

trimmerAlmostFull(30614),

trimmerFull(30615),

trimmerNearLimit(30616),

trimmerAtLimit(30617),

trimmerOpened(30618),

trimmerClosed(30619),

trimmerTurnedOn(30620),

trimmerTurnedOff(30621),

trimmerOffline(30622),

trimmerPowerSaver(30623),

trimmerWarmingUp(30624),

trimmerAdded(30625),

trimmerRemoved(30626),

trimmerResourceAdded(30627),

trimmerResourceRemoved(30628),

trimmerRecoverableFailure(30629),

trimmerUnrecoverableFailure(30630),

trimmerRecoverableStorageError(30631),

trimmerUnrecoverableStorageError(30632),

trimmerMotorFailure(30633),

trimmerMemoryExhausted(30634),

trimmerUnderTemperature(30635),

trimmerOverTemperature(30636),

trimmerTimingFailure(30637),

trimmerThermistorFailure(30638),

-- FinDeviceTypeTC = dieCutter(7)

dieCutterCoverOpen(30703),

dieCutterCoverClosed(30704),

dieCutterInterlockOpen(30705),

dieCutterInterlockClosed(30706),

dieCutterConfigurationChange(30707),

dieCutterJam(30708),

dieCutterMissing(30709),

dieCutterLifeAlmostOver(30710),

dieCutterLifeOver(30711),

dieCutterAlmostEmpty(30712),

dieCutterEmpty(30713),

dieCutterAlmostFull(30714),

dieCutterFull(30715),

dieCutterNearLimit(30716),

dieCutterAtLimit(30717),

dieCutterOpened(30718),

dieCutterClosed(30719),

dieCutterTurnedOn(30720),

dieCutterTurnedOff(30721),

dieCutterOffline(30722),

dieCutterPowerSaver(30723),

dieCutterWarmingUp(30724),

dieCutterAdded(30725),

dieCutterRemoved(30726),

dieCutterResourceAdded(30727),

dieCutterResourceRemoved(30728),

dieCutterRecoverableFailure(30729),

dieCutterUnrecoverableFailure(30730),

dieCutterRecoverableStorageError(30731),

dieCutterUnrecoverableStorageError(30732),

dieCutterMotorFailure(30733),

dieCutterMemoryExhausted(30734),

dieCutterUnderTemperature(30735),

dieCutterOverTemperature(30736),

dieCutterTimingFailure(30737),

dieCutterThermistorFailure(30738),

-- FinDeviceTypeTC = puncher(8)

puncherCoverOpen(30803),

puncherCoverClosed(30804),

puncherInterlockOpen(30805),

puncherInterlockClosed(30806),

puncherConfigurationChange(30807),

puncherJam(30808),

puncherMissing(30809),

puncherLifeAlmostOver(30810),

puncherLifeOver(30811),

puncherAlmostEmpty(30812),

puncherEmpty(30813),

puncherAlmostFull(30814),

puncherFull(30815),

puncherNearLimit(30816),

puncherAtLimit(30817),

puncherOpened(30818),

puncherClosed(30819),

puncherTurnedOn(30820),

puncherTurnedOff(30821),

puncherOffline(30822),

puncherPowerSaver(30823),

puncherWarmingUp(30824),

puncherAdded(30825),

puncherRemoved(30826),

puncherResourceAdded(30827),

puncherResourceRemoved(30828),

puncherRecoverableFailure(30829),

puncherUnrecoverableFailure(30830),

puncherRecoverableStorageError(30831),

puncherUnrecoverableStorageError(30832),

puncherMotorFailure(30833),

puncherMemoryExhausted(30834),

puncherUnderTemperature(30835),

puncherOverTemperature(30836),

puncherTimingFailure(30837),

puncherThermistorFailure(30838),

-- FinDeviceTypeTC = perforater(9)

perforaterCoverOpen(30903),

perforaterCoverClosed(30904),

perforaterInterlockOpen(30905),

perforaterInterlockClosed(30906),

perforaterConfigurationChange(30907),

perforaterJam(30908),

perforaterMissing(30909),

perforaterLifeAlmostOver(30910),

perforaterLifeOver(30911),

perforaterAlmostEmpty(30912),

perforaterEmpty(30913),

perforaterAlmostFull(30914),

perforaterFull(30915),

perforaterNearLimit(30916),

perforaterAtLimit(30917),

perforaterOpened(30918),

perforaterClosed(30919),

perforaterTurnedOn(30920),

perforaterTurnedOff(30921),

perforaterOffline(30922),

perforaterPowerSaver(30923),

perforaterWarmingUp(30924),

perforaterAdded(30925),

perforaterRemoved(30926),

perforaterResourceAdded(30927),

perforaterResourceRemoved(30928),

perforaterRecoverableFailure(30929),

perforaterUnrecoverableFailure(30930),

perforaterRecoverableStorageError(30931),

perforaterUnrecoverableStorageError(30932),

perforaterMotorFailure(30933),

perforaterMemoryExhausted(30934),

perforaterUnderTemperature(30935),

perforaterOverTemperature(30936),

perforaterTimingFailure(30937),

perforaterThermistorFailure(30938),

-- FinDeviceTypeTC = slitter(10)

slitterCoverOpen(31003),

slitterCoverClosed(31004),

slitterInterlockOpen(31005),

slitterInterlockClosed(31006),

slitterConfigurationChange(31007),

slitterJam(31008),

slitterMissing(31009),

slitterLifeAlmostOver(31010),

slitterLifeOver(31011),

slitterAlmostEmpty(31012),

slitterEmpty(31013),

slitterAlmostFull(31014),

slitterFull(31015),

slitterNearLimit(31016),

slitterAtLimit(31017),

slitterOpened(31018),

slitterClosed(31019),

slitterTurnedOn(31020),

slitterTurnedOff(31021),

slitterOffline(31022),

slitterPowerSaver(31023),

slitterWarmingUp(31024),

slitterAdded(31025),

slitterRemoved(31026),

slitterResourceAdded(31027),

slitterResourceRemoved(31028),

slitterRecoverableFailure(31029),

slitterUnrecoverableFailure(31030),

slitterRecoverableStorageError(31031),

slitterUnrecoverableStorageError(31032),

slitterMotorFailure(31033),

slitterMemoryExhausted(31034),

slitterUnderTemperature(31035),

slitterOverTemperature(31036),

slitterTimingFailure(31037),

slitterThermistorFailure(31038),

-- FinDeviceTypeTC = separationCutter(11)

separationCutterCoverOpen(31103),

separationCutterCoverClosed(31104),

separationCutterInterlockOpen(31105),

separationCutterInterlockClosed(31106),

separationCutterConfigurationChange(31107),

separationCutterJam(31108),

separationCutterMissing(31109),

separationCutterLifeAlmostOver(31110),

separationCutterLifeOver(31111),

separationCutterAlmostEmpty(31112),

separationCutterEmpty(31113),

separationCutterAlmostFull(31114),

separationCutterFull(31115),

separationCutterNearLimit(31116),

separationCutterAtLimit(31117),

separationCutterOpened(31118),

separationCutterClosed(31119),

separationCutterTurnedOn(31120),

separationCutterTurnedOff(31121),

separationCutterOffline(31122),

separationCutterPowerSaver(31123),

separationCutterWarmingUp(31124),

separationCutterAdded(31125),

separationCutterRemoved(31126),

separationCutterResourceAdded(31127),

separationCutterResourceRemoved(31128),

separationCutterRecoverableFailure(31129),

separationCutterUnrecoverableFailure(31130),

separationCutterRecoverableStorageError(31131),

separationCutterUnrecoverableStorageError(31132),

separationCutterMotorFailure(31133),

separationCutterMemoryExhausted(31134),

separationCutterUnderTemperature(31135),

separationCutterOverTemperature(31136),

separationCutterTimingFailure(31137),

separationCutterThermistorFailure(31138),

-- FinDeviceTypeTC = imprinter(12)

imprinterCoverOpen(31203),

imprinterCoverClosed(31204),

imprinterInterlockOpen(31205),

imprinterInterlockClosed(31206),

imprinterConfigurationChange(31207),

imprinterJam(31208),

imprinterMissing(31209),

imprinterLifeAlmostOver(31210),

imprinterLifeOver(31211),

imprinterAlmostEmpty(31212),

imprinterEmpty(31213),

imprinterAlmostFull(31214),

imprinterFull(31215),

imprinterNearLimit(31216),

imprinterAtLimit(31217),

imprinterOpened(31218),

imprinterClosed(31219),

imprinterTurnedOn(31220),

imprinterTurnedOff(31221),

imprinterOffline(31222),

imprinterPowerSaver(31223),

imprinterWarmingUp(31224),

imprinterAdded(31225),

imprinterRemoved(31226),

imprinterResourceAdded(31227),

imprinterResourceRemoved(31228),

imprinterRecoverableFailure(31229),

imprinterUnrecoverableFailure(31230),

imprinterRecoverableStorageError(31231),

imprinterUnrecoverableStorageError(31232),

imprinterMotorFailure(31233),

imprinterMemoryExhausted(31234),

imprinterUnderTemperature(31235),

imprinterOverTemperature(31236),

imprinterTimingFailure(31237),

imprinterThermistorFailure(31238),

-- FinDeviceTypeTC = wrapper(13)

wrapperCoverOpen(31303),

wrapperCoverClosed(31304),

wrapperInterlockOpen(31305),

wrapperInterlockClosed(31306),

wrapperConfigurationChange(31307),

wrapperJam(31308),

wrapperMissing(31309),

wrapperLifeAlmostOver(31310),

wrapperLifeOver(31311),

wrapperAlmostEmpty(31312),

wrapperEmpty(31313),

wrapperAlmostFull(31314),

wrapperFull(31315),

wrapperNearLimit(31316),

wrapperAtLimit(31317),

wrapperOpened(31318),

wrapperClosed(31319),

wrapperTurnedOn(31320),

wrapperTurnedOff(31321),

wrapperOffline(31322),

wrapperPowerSaver(31323),

wrapperWarmingUp(31324),

wrapperAdded(31325),

wrapperRemoved(31326),

wrapperResourceAdded(31327),

wrapperResourceRemoved(31328),

wrapperRecoverableFailure(31329),

wrapperUnrecoverableFailure(31330),

wrapperRecoverableStorageError(31331),

wrapperUnrecoverableStorageError(31332),

wrapperMotorFailure(31333),

wrapperMemoryExhausted(31334),

wrapperUnderTemperature(31335),

wrapperOverTemperature(31336),

wrapperTimingFailure(31337),

wrapperThermistorFailure(31338),

-- FinDeviceTypeTC = bander(14)

banderCoverOpen(31403),

banderCoverClosed(31404),

banderInterlockOpen(31405),

banderInterlockClosed(31406),

banderConfigurationChange(31407),

banderJam(31408),

banderMissing(31409),

banderLifeAlmostOver(31410),

banderLifeOver(31411),

banderAlmostEmpty(31412),

banderEmpty(31413),

banderAlmostFull(31414),

banderFull(31415),

banderNearLimit(31416),

banderAtLimit(31417),

banderOpened(31418),

banderClosed(31419),

banderTurnedOn(31420),

banderTurnedOff(31421),

banderOffline(31422),

banderPowerSaver(31423),

banderWarmingUp(31424),

banderAdded(31425),

banderRemoved(31426),

banderResourceAdded(31427),

banderResourceRemoved(31428),

banderRecoverableFailure(31429),

banderUnrecoverableFailure(31430),

banderRecoverableStorageError(31431),

banderUnrecoverableStorageError(31432),

banderMotorFailure(31433),

banderMemoryExhausted(31434),

banderUnderTemperature(31435),

banderOverTemperature(31436),

banderTimingFailure(31437),

banderThermistorFailure(31438),

-- FinDeviceTypeTC = makeEnvelope(15)

makeEnvelopeCoverOpen(31503),

makeEnvelopeCoverClosed(31504),

makeEnvelopeInterlockOpen(31505),

makeEnvelopeInterlockClosed(31506),

makeEnvelopeConfigurationChange(31507),

makeEnvelopeJam(31508),

makeEnvelopeMissing(31509),

makeEnvelopeLifeAlmostOver(31510),

makeEnvelopeLifeOver(31511),

makeEnvelopeAlmostEmpty(31512),

makeEnvelopeEmpty(31513),

makeEnvelopeAlmostFull(31514),

makeEnvelopeFull(31515),

makeEnvelopeNearLimit(31516),

makeEnvelopeAtLimit(31517),

makeEnvelopeOpened(31518),

makeEnvelopeClosed(31519),

makeEnvelopeTurnedOn(31520),

makeEnvelopeTurnedOff(31521),

makeEnvelopeOffline(31522),

makeEnvelopePowerSaver(31523),

makeEnvelopeWarmingUp(31524),

makeEnvelopeAdded(31525),

makeEnvelopeRemoved(31526),

makeEnvelopeResourceAdded(31527),

makeEnvelopeResourceRemoved(31528),

makeEnvelopeRecoverableFailure(31529),

makeEnvelopeUnrecoverableFailure(31530),

makeEnvelopeRecoverableStorageError(31531),

makeEnvelopeUnrecoverableStorageError(31532),

makeEnvelopeMotorFailure(31533),

makeEnvelopeMemoryExhausted(31534),

makeEnvelopeUnderTemperature(31535),

makeEnvelopeOverTemperature(31536),

makeEnvelopeTimingFailure(31537),

makeEnvelopeThermistorFailure(31538),

-- FinDeviceTypeTC = stacker(16)

stackerCoverOpen(31603),

stackerCoverClosed(31604),

stackerInterlockOpen(31605),

stackerInterlockClosed(31606),

stackerConfigurationChange(31607),

stackerJam(31608),

stackerMissing(31609),

stackerLifeAlmostOver(31610),

stackerLifeOver(31611),

stackerAlmostEmpty(31612),

stackerEmpty(31613),

stackerAlmostFull(31614),

stackerFull(31615),

stackerNearLimit(31616),

stackerAtLimit(31617),

stackerOpened(31618),

stackerClosed(31619),

stackerTurnedOn(31620),

stackerTurnedOff(31621),

stackerOffline(31622),

stackerPowerSaver(31623),

stackerWarmingUp(31624),

stackerAdded(31625),

stackerRemoved(31626),

stackerResourceAdded(31627),

stackerResourceRemoved(31628),

stackerRecoverableFailure(31629),

stackerUnrecoverableFailure(31630),

stackerRecoverableStorageError(31631),

stackerUnrecoverableStorageError(31632),

stackerMotorFailure(31633),

stackerMemoryExhausted(31634),

stackerUnderTemperature(31635),

stackerOverTemperature(31636),

stackerTimingFailure(31637),

stackerThermistorFailure(31638),

-- FinDeviceTypeTC = sheetRotator(17)

sheetRotatorCoverOpen(31703),

sheetRotatorCoverClosed(31704),

sheetRotatorInterlockOpen(31705),

sheetRotatorInterlockClosed(31706),

sheetRotatorConfigurationChange(31707),

sheetRotatorJam(31708),

sheetRotatorMissing(31709),

sheetRotatorLifeAlmostOver(31710),

sheetRotatorLifeOver(31711),

sheetRotatorAlmostEmpty(31712),

sheetRotatorEmpty(31713),

sheetRotatorAlmostFull(31714),

sheetRotatorFull(31715),

sheetRotatorNearLimit(31716),

sheetRotatorAtLimit(31717),

sheetRotatorOpened(31718),

sheetRotatorClosed(31719),

sheetRotatorTurnedOn(31720),

sheetRotatorTurnedOff(31721),

sheetRotatorOffline(31722),

sheetRotatorPowerSaver(31723),

sheetRotatorWarmingUp(31724),

sheetRotatorAdded(31725),

sheetRotatorRemoved(31726),

sheetRotatorResourceAdded(31727),

sheetRotatorResourceRemoved(31728),

sheetRotatorRecoverableFailure(31729),

sheetRotatorUnrecoverableFailure(31730),

sheetRotatorRecoverableStorageError(31731),

sheetRotatorUnrecoverableStorageError(31732),

sheetRotatorMotorFailure(31733),

sheetRotatorMemoryExhausted(31734),

sheetRotatorUnderTemperature(31735),

sheetRotatorOverTemperature(31736),

sheetRotatorTimingFailure(31737),

sheetRotatorThermistorFailure(31738),

-- FinDeviceTypeTC = inserter(18)

inserterCoverOpen(31803),

inserterCoverClosed(31804),

inserterInterlockOpen(31805),

inserterInterlockClosed(31806),

inserterConfigurationChange(31807),

inserterJam(31808),

inserterMissing(31809),

inserterLifeAlmostOver(31810),

inserterLifeOver(31811),

inserterAlmostEmpty(31812),

inserterEmpty(31813),

inserterAlmostFull(31814),

inserterFull(31815),

inserterNearLimit(31816),

inserterAtLimit(31817),

inserterOpened(31818),

inserterClosed(31819),

inserterTurnedOn(31820),

inserterTurnedOff(31821),

inserterOffline(31822),

inserterPowerSaver(31823),

inserterWarmingUp(31824),

inserterAdded(31825),

inserterRemoved(31826),

inserterResourceAdded(31827),

inserterResourceRemoved(31828),

inserterRecoverableFailure(31829),

inserterUnrecoverableFailure(31830),

inserterRecoverableStorageError(31831),

inserterUnrecoverableStorageError(31832),

inserterMotorFailure(31833),

inserterMemoryExhausted(31834),

inserterUnderTemperature(31835),

inserterOverTemperature(31836),

inserterTimingFailure(31837),

inserterThermistorFailure(31838)

# Internationalization Considerations

In section 5, this document defines the new human-readable, localized "printer-alert-description" IPP Printer attribute using the existing 'text' syntax defined in section 4.1.1 of [RFC2911]. Values of this new attribute MUST copy their natural language tag [RFC4646] from the values of 'prtLocalizationLanguage', 'prtLocalizationCountry', and 'prtGeneralCurrentLocalization' [RFC3805]. Values of this new attribute MUST also be converted from the charset specified by the values of 'prtLocalizationCharacterSet' and 'prtGeneralCurrentLocalization' [RFC3805] to the charset specified by "charset-configured" (defaults to UTF-8 [RFC3629]).

In section 5, this document defines new keyword attribute values for "printer-state-reasons" [RFC2911] for Printer Subunits [RFC3805] and a new machine-readable attribute "printer-alert". Localization by the IPP Printer does NOT apply to these machine-readable attributes.

In section 6, this document defines new keyword attribute values for "printer-state-reasons" [RFC2911] for Finishing Subunits [RFC3806] and new corresponding enumerated attribute values for the 'PrtAlertCodeTC' textual convention [RFC3805] [IANAPRT]. Localization by the IPP Printer or SNMP Printer MIB Agent does NOT apply to these machine-readable attributes and values.

Therefore, this document conforms to 'IETF Policy on Character Sets and Languages' [RFC2277].

See section 7 'Internationalization Considerations' in [RFC2911] and section 8 'Internationalization Considerations' in [RFC3805]..

# Security Considerations

This document adds no new security considerations to the IETF Printer MIB v2 [RFC3805] or IETF IPP/1.1 [RFC2911].  In section 5, this document defines extensions to one existing REQUIRED IPP Printer Description attribute "printer-state-reasons" defined in [RFC2911]. This document also defines two new RECOMMENDED IPP Printer Description attributes "printer-alert" and "printer-alert-description". All three are IPP Printer Description attributes as defined in [RFC2911].

In section 6, this document defines extensions to one existing REQUIRED Printer MIB columnar object 'prtAlertCode' defined in [RFC3805] via extensions to one existing textual convention 'PrtAlertCodeTC' defined in [IANAPRT].

See section 8 ‘Security Considerations’ in [RFC2911] and section 9 'Security Considerations' in [RFC3805].

# Acknowledgements

The editors would like to acknowledge significant contributions to this document from Naoki Asada (Sharp)  who originally proposed the idea.

The editors would like to acknowledge comments on this document from Ron Bergman (formerly at Ricoh), Shah Bhatti (formerly at Samsung), Paul Danbold (Apple), Lee Farrell (Canon), Mike Fenelon (Microsoft), Rick Landau (Dell), Harry Lewis (InfoPrint Solutions), Stuart Rowley (formerly at Kyocera), Chris Story (Ricoh), Michael Sweet (Apple), Jerry Thrasher (Lexmark), Ted Tronson (Novell), Bill Wagner (TIC), Paul Tykodi (TCS), Pete Zehler (Xerox), and other IPP WG members.

# References

## Normative References

[CIMALERT] Landau, McDonald

CIM_PrintAlertRecord class, published in DMFT CIM Schema v2.20,

http://www.dmtf.org/standards/cim/cim_schema_v220/

[IANAFIN] Bergman, Lewis, McDonald.

IANA Finisher MIB, originally published in RFC 3806, June 2004,

http://www.iana.org/assignments/ianafinisher-mib

[IANAIPP] Hastings, McDonald.

IANA IPP Registry, established in RFC 2911, September 2000.

http://www.iana.org/assignments/ipp-registrations

[IANAPRT] Bergman, Lewis, McDonald.

IANA Printer MIB, originally published in RFC 3805, June 2004.

http://www.iana.org/assignments/ianaprinter-mib

[RFC2119] Bradner.

Key words for use in RFCs to Indicate Requirement Levels, RFC 2119,

March 1997.

[RFC2616] Fielding, Gettys, Mogul, Frystyk, Masinter, Leach,

Berners-Lee.  IETF HTTP/1.1, RFC 2616, June 1999.

[RFC2910] Herriot, Butler, Moore, Turner, Wenn.

IPP/1.1: Encoding and Transport, RFC 2910, September 2000.

(obsoletes [RFC2565])

[RFC2911] Hastings, Herriot, deBry, Isaacson, Powell.

IPP/1.1: Model and Semantics, RFC 2911, September 2000.

(obsoletes [RFC2566])

[RFC2978] Freed, Postel.

IANA Charset Registration Procedures, RFC 2978, October 2000.

[RFC3411] Harrington, Presuhn, Wijnen.

IETF Architecture for Describing SNMP Management Frameworks,

RFC 3411, December 2002.

[RFC3414] Blumenthal, Wijnen.

IETF User-based Security Model (USM) for SNMPv3, RFC 3414,

December 2002.

[RFC3629] Yergeau.

UTF-8, a transformation format of ISO 10646, RFC 3629

November 2003.

[RFC3805] Bergman, Lewis, McDonald.

IETF Printer MIB v2, RFC 3805, June 2004.

[RFC3806] Bergman, Lewis, McDonald.

IETF Printer Finishing MIB, RFC 3806, June 2004.

[RFC3808] McDonald.

IANA Charset MIB, RFC 3808, June 2004.

[RFC4646] Phillips, Davis.

Tags for Identifying Languages, RFC 4646, September 2006.

(obsoletes RFC 3066)

[RFC5234] Crocker, Overell.

Augmented BNF for Syntax Specifications, RFC 5234, January 2008.

[US-ASCII]

Coded Character Set -- 7-Bit American Standard Code for

Information Interchange, ANSI X3.4-1986.

## Informative References

[RFC1157] Case, Fedor, Schoffstall, Davin.

IETF Simple Network Management Protocol (SNMP), RFC 1157, May 1990.

[RFC1759] Smith, Wright, Hastings, Zilles, Gyllenskog.

IETF Printer MIB v1, RFC 1759, March 1995.

(obsoleted by [RFC3805])

[RFC1945] Berners-Lee, Fielding.

IETF HTTP/1.0, RFC 1945, May 1996.

(obsoleted by [RFC2616])

[RFC2277] Alvestrand.

IETF Policy on Character Sets and Languages, BCP 18 / RFC 2277,

January 1998.

[RFC2565] Herriot, Butler, Moore, Turner.

IPP/1.0: Encoding and Transport, RFC 2565, April 1999.

(obsoleted by [RFC2910])

[RFC2566] Hastings, Herriot, deBry, Isaacson, Powell.

IPP/1.0: Model and Semantics, RFC 2566, April 1999.

(obsoleted by [RFC2911])

[RFC2817] Khare, Lawrence.

IETF Upgrading to TLS Within HTTP/1.1, RFC 2817, May 2000.

[RFC3382] deBry, Hastings, Herriot, Ocke, Zehler.

IETF IPP 'collection' attribute syntax, RFC 3382, September 2002.

[RFC3995] Herriot, Hastings.

IETF IPP Event Notifications & Subscriptions, RFC 3995, March 2005.

[WIMS-CIM] IEEE-ISTO PWG WIMS WG - CIM Refresh Project

http://www.pwg.org/mailhelp.html - subscribe to WIMS mailing list

ftp://www.pwg.org/wims/cim - archive of WIMS-CIM planning papers

ftp://www.pwg.org/wims/wd - archive of WIMS-CIM working drafts

http://www.dmtf.org/standards/cim/cim_schema_v220/ - CIM_Printer,

CIM_PrintAlertRecord, etc. (complete Printer MIB mapping)

# Editors’ Addresses

Ira McDonald (High North)

Phone: +1-906-494-2434

Email: blueroofmusic@gmail.com

Craig Whittle (Sharp Labs America)

Phone: +1-360-817-8544

Email: cwhittle@sharplabs.com

Send comments to the PWG IPP Mailing List:

ipp@pwg.org  (subscribers only)

To subscribe, see the PWG web page:

http://www.pwg.org/mailhelp.html

# Appendix A - Design Alternatives (Informative)

This section provides durable documentation of the 'road not taken' on various design alternatives during the development of this document.

## Printer Alert Encoding in Collection Attribute

A note to the IPP WG mailing list on 19 July 2006 proposed an alternative to encode the columnar objects from 'prtAlertTable' in a new IPP Printer attribute using the 'collection' syntax defined in section 3 of [RFC3382].

### Rationale for Rejection

The IPP WG rejected this proposal because it would make support of this document dependent on support for the IPP 'collection' syntax (not widely supported in IPP/1.1 [RFC2911] [RFC2910] implementations and not known to be supported in any IPP/1.0 [RFC2566] [RFC2565] implementation).

## Printer Alert Encoding in New Object

A note to the IPP WG mailing list on 19 July 2006 proposed an alternative to encode the columnar objects from 'prtAlertTable' in a new first-class IPP object.

### Rationale for Rejection

The IPP WG rejected this proposal because it would NOT be compatible with any deployed IPP implementation (because it would require a new IPP request attribute group over-the-wire).

## Printer Alert Encoding in Parallel Attributes

A note to the IPP WG mailing list on 19 July 2006 proposed an alternative to encode the columnar objects from 'prtAlertTable' in an a set of ordered parallel IPP Printer attributes.

### Rationale for Rejection

The IPP WG rejected this proposal because it would NOT be robust (because ordering is NOT required by the '1setOf X' syntax defined in section 4.1.6 of [RFC2911]) and would NOT be compatible with vendor extensions.

## Printer Alert Encoding in State Message

The initial draft of this specification proposed an optimization (to avoid the definition of any new IPP Printer attributes) by overloading the existing IPP Printer attribute "printer-state-message" to encode columnar objects from 'prtAlertTable' in a structured string.

### Rationale for Rejection

The IPP WG rejected this proposal because it would have forced IPP Printer "printer-state-message" values to be locale-independent (illegal for the 'text' syntax defined in section 4.1.1 of [RFC2911]).

## Printer Alert Group Finishing Extensions

The initial draft of this specification proposed an optimization (to avoid the definition of many new Finishing Subunit-specific values of 'PrtAlertCodeTC' and IPP Printer attribute "printer-state-reasons") by defining one new value of 'PrtAlertGroupTC' for each value of of the IANA Finisher MIB 'FinDeviceTypeTC' (originally published in [RFC3806]) used in the non-index object 'finDeviceType' in 'finDeviceTable' and NOT included in 'prtAlertTable'.

### Rationale for Rejection

The IPP WG rejected this optimization because it would have made IPP Printer "printer-state-reasons" values ambiguous for all Finishing Subunits (because the generic 'subunit-xxx' alert values were used).

## Printer Alert Subset for Finishing Subunits

Previous versions of this document defined a subset of specific subunit alerts for each Finishing Subunit.

### Rationale for Rejection

Lively discussion during the review at the PWG Lexington face-to-face (27 October 2006) resulted in a consensus to expand to a complete set of specific subunit alerts for each Finishing Subunit.