## Slide 1: Imaging Device Security
Copyright © 2017 The Printer Working Group. All rights reserved.
The Printer Working Group
November 16, 2017
Virtual Face-to-Face
1

## Slide 2: Agenda
Copyright © 2017 The Printer Working Group. All rights reserved.
When | What
9:00 – 9:10 | Introductions, Agenda review
9:10 – 10:50 | Review results of Latest MFP TC Meeting
10:50 – 11:00 | Wrap Up / Next Steps
2

## Slide 3: Intellectual Property Policy
Copyright © 2017 The Printer Working Group. All rights reserved.
3
  “This meeting is conducted under the rules of the PWG IP policy”.
    Refer to the IP statements in the plenary slides

## Slide 4: Officers
Copyright © 2017 The Printer Working Group. All rights reserved.
4
Chair:
  Alan Sukert (Xerox)
Vice-Chair:
  Currently Vacant
Secretary:
  Alan Sukert (Xerox)
Document Editors:
  Ira McDonald (High North): HCD-TNC

## Slide 5: New HCD Protection Profile
Copyright © 2017 The Printer Working Group. All rights reserved.
5
The new Protection Profile for Hardcopy Devices (PP_HCD_V1.0) was published on September 11.
You can find it on NIAP’s web site … https://www.niap-ccevs.org/pp/PP_HCD_V1.0/
… and on IPA’s (including links to both the original and the Japanese translation) https://www.ipa.go.jp/security/publications/pp-jp/hcd.html
It is a US/Japan PP, not a “cPP” with broader international support.

## Slide 6: Summary of Oct 25, 2017 MFP Technical Committee Meetings
Copyright © 2017 The Printer Working Group. All rights reserved.
6
MFP TECHNICAL COMMITTEE MEETING AGENDA
Welcome, introductions, logistics, agenda review…
TC administrivia
Requirements issues
Implementation issues
Plans and processes for updating and maintaining the HCD PP
Summary and next steps

## Slide 7: Requirements issues: RSA key establishment in TLS
Copyright © 2017 The Printer Working Group. All rights reserved.
7
Labgram #106 was issued, put “on hold” after lab meeting
NIST is revising 800-56A/B/C, perhaps by mid 2018
NIAP may or may not align with NIST; not decided yet
Recommend that TOEs be able to disable RSA key exchange ciphersuites in evaluated configuration

## Slide 8: Requirements issues: Password policies
Copyright © 2017 The Printer Working Group. All rights reserved.
8
FIA_PMG_EXT specifies password length/composition requirements
  Requires capability to compose using upper case, lower case, numeric, and specials
  It may be updated to require passwords to include all four types
SP 800-171, SP 800-53, and CNSSI 1253, have more stringent requirements
  Including password lifetime, re-use
  These are not required for CC evaluation
On the other hand, new SP 800-63 tosses out composition, lifetime, re-use
Password policies could be different for normal versus admin users
  Admins are more trusted, but admin access is more critical
  We are looking at other PPs (e.g., GPOS, Mobile Devices) for precedents

## Slide 9: Requirements issues: Audit log servers
Copyright © 2017 The Printer Working Group. All rights reserved.
9
Does FAU_STG_EXT.1 require the use of syslog protocol?
Network Devices interpretation #1 said that syslog is not required
It was accepted by NIAP, but the TD is now archived
It should apply to the HCD PP
A TRRT will be submitted

## Slide 10: Requirements issues: NDcPP and FDEcPP updates and TDs
Copyright © 2017 The Printer Working Group. All rights reserved.
10
NDcPP and FDEcPP have been updated since their predecessors were used as the basis for some parts of the HCD PP
In particular, TLS requirements were separated into TLS server and TLS client SFRs, and X.509 requirements have been added
Technical Decisions have also been issued for NDcPP, FDEcPP, and other NIAP PPs / cPPs, that may apply to HCDs
The HCD TC will review these and propose changes to the HCD as appropriate

## Slide 11: Requirements issues: Key Transport (FCS_COP.1(i)) AAs
Copyright © 2017 The Printer Working Group. All rights reserved.
11
There are no assurance activities associated with FCS_COP.1(i)
They have been added to the FDEcPP
The TC will propose to adopt/adapt those assurance activities

## Slide 12: Requirements issues: Wi-Fi support
Copyright © 2017 The Printer Working Group. All rights reserved.
12
HCDs support WiFi, but it is not part of HCD PP v1.0
The WLAN EP for Mobile Devices covers this, so we may adopt/adapt requirements from that (as an option for HCDs)

## Slide 13: Requirements issues: Other protocols
Copyright © 2017 The Printer Working Group. All rights reserved.
13
HCDs in customer environments use protocols that are not covered by the PP.
To evaluate using these protocols, they must be encapsulated, but that may not be representative of how customers use them
We are looking at
  SNMPv3: There is a TD on this topic for NDcPP v1.0
  S/MIME: It is covered in the Email Client PP
  Kerberos: Maybe it would be covered in a directory server PP (not currently in development)
  SMBv3: Not sure

## Slide 14: Implementation issues: Requirements embedded in AAs
Copyright © 2017 The Printer Working Group. All rights reserved.
14
Some of the assurance activities impose security functional requirements that are not present in the associated SFR
The TC will identify these and propose changes to consolidate those requirements in the SFR

## Slide 15: Implementation issues: Inconsistencies in KMD instructions
Copyright © 2017 The Printer Working Group. All rights reserved.
15
There are some inconsistencies between the KMD instructions in the HCD PP annex and KMD-related assurance activities
The TC will identify these and propose changes to make them consistent

## Slide 16: Implementation issues: Use of 3rd-party entropy sources
Copyright © 2017 The Printer Working Group. All rights reserved.
16
There were some questions about how to describe entropy from 3rd party sources
  Vendors cannot describe details that are unavailable to them or that would infringe on 3rd party intellectual property
NIAP has a policy on that topic

## Slide 17: Implementation issues: Key destruction testing
Copyright © 2017 The Printer Working Group. All rights reserved.
17
Key destruction testing by before-after comparison of memory dumps can be onerous
Alternative testing methods can be proposed to NIAP for consideration
There is a more information in a key destruction template on github

## Slide 18: Implementation issues: Use of TPMs in the HCD TOE
Copyright © 2017 The Printer Working Group. All rights reserved.
18
Some vendors use TPMs in their products
How can TPM crypto functions be evaluated?
It was suggested that the DSC cPP (under development) would need to be used
However, it’s not clear if the DSC cPP has that purpose…

## Slide 19: Plans and processes for updating/maintaining the HCD PP Internationalized crypto
Copyright © 2017 The Printer Working Group. All rights reserved.
19
Current SFRs and Assurance Activities for cryptographic functions in HCD PP cannot be evaluated in all nations (in particular, Korea)
The crypto WG is developing a catalog of crypto functions that we may adopt/adapt

## Slide 20: Plans and processes for updating/maintaining the HCD PP EAL claims
Copyright © 2017 The Printer Working Group. All rights reserved.
20
The HCD PP itself is certified (by JISEC) but it does not claim conformance to EAL1
The PP does not claim conformance to EAL1 but mentions that it contains the SARs necessary for conforming STs to claim EAL1
We may be able to fix this in a revised PP
However, this does not solve other EAL-related problems (EU customers if they require either EAL2+ or cPP)

## Slide 21: Plans and processes for updating/maintaining the HCD PP Versioning
Copyright © 2017 The Printer Working Group. All rights reserved.
21
An update to HCD_PP_V1.0 that fixes problems, incorporates existing TDs and errata, but which does not add new requirements, would be V1.1
If new requirements are added, it must be V2.0.

## Slide 22: Plans and processes for updating/maintaining the HCD PP Who does what?
Copyright © 2017 The Printer Working Group. All rights reserved.
22
US/JP/KR schemes are resource-limited and cannot lead the effort to update the HCD PP
The HCD TC will lead the effort and, where possible, submit fully-formed proposals for US and JP approval

## Slide 23: Plans and processes for updating/maintaining the HCD PP iTC formation and cPP development
Copyright © 2017 The Printer Working Group. All rights reserved.
23
We will update the HCD PP as a bi-lateral (US/JP) PP, not a cPP
There is sufficient interest from at least two schemes to start the iTC formation process, perhaps 6~12 months from now

## Slide 24: Wrap Up/ Next Steps
Copyright © 2017 The Printer Working Group. All rights reserved.
24
Some volunteer assignments have been made to work these issues
If you are interested in working on these or other issues, please contact Brian Smithson brian.smithson@ricoh-usa.com or Alan Sukert Alan.Sukert@xerox.com

## Slide 25: Wrap Up/ Next Steps HCD PP Version 1.1 Potential Topics
Copyright © 2017 The Printer Working Group. All rights reserved.
25
Existing Technical Decisions against HCD PP Version 1.0
Current Errata
RSA Key Agreement – when NIST enforces NIST SP 800-131A
Audit Log Server Requirements
Updated requirements from NDcPP and FDEcPP
Updated requirements from Technical Decions other than for HCD PP
Assurance Activities (AAs) for Key Transport SFR (FCS_COP.1(i))
Additional requirements that show up in Assurance Activities
Inconsistencies between Key Management Description (KMD) description and KMD AAs
3rd Party Entropy Sources
Key Destruction SFR
TPMs used in the TOE
EAL Claim for HCD PP

## Slide 26: Wrap Up/ Next Steps HCD PP Version 2.0 Potential Topics
Copyright © 2017 The Printer Working Group. All rights reserved.
26
Password Policies
Password Policy Applicability (normal vs. admin users)
Wi-Fi Support
SNMPv3 Support
Kerberos Support
S/MIME Support
SMBv3 Support
Internationally-friendly crypto requirements that don’t rely on FIPS