Comparison of IPP Notification Delivery Methods

From:	Tom Hastings

Date	10/27/1999

File:	ipp-notification-delivery-method-table.doc

In the following list of requirements, if the opposite of the requirement is not clear, the opposite is indicated after an arrow (->), suggesting the other end of the range.

The value in the box means:

3 = meets requirement well,

2 = meets requirement somewhat,

1 = doesn't meet requirement very well,

0 = doesn't meet the requirement at all, if the opposite is indicated, it behaves as the opposite (CON).

? = I wasn't sure.

shaded number indicates for a variant the deltas from a previous method.

Abbreviations:  NS = Notification Source;  NR = Notification Recipient;  UR = Ultimate Recipient

| Requirement - PRO -> CON | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Variant of: |  |  |  | 3 | 3,4 | 3 | 3 | 7 | 7 |  |  | 11 |  | 13 |
|  | poll | in-band | http | SNMP | UDP |
| Fits notification model [ipp-not] | 0 | 3 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 3 | 3 | 3 | 3 | 3 |
| Fits current IPP Model [ipp-mod]; changes existing operations | 3 | 0 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 0 | 3 | 3 | 3 | 3 |
| Likely to go through firewalls | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1 | 0 | 0 | 0 | 0 |
| Fewer connections left open -> one per pending job | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 3 | 3 | 3 | 3 |
| Fewer connection setups to send/receive a notification | 3 | 3 | 2 | 2 | 2 | 2 | 2 | 0 | 2 | 3 | 3 | 3 | 3 | 3 |
| Reduces network traffic, events can be batched into one Notification | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 0 | 0 | 0 | 0 |
| Works with HTTP servers -> multiple responses needed | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 0 | 3 | 3 | 3 | 3 | 3 |
| Don't miss events after subscribing | 0 | 3 | 3 | 0 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 |
| Per-Job and Per-Printer Subscription; Per-Job only | 0 | 0 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 |
| End users and operators -> end users only or operators only | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 1 | 1 | 1 | 1 |
| Good for all events -> not good for page level or complete only | 3 | 2 | 3 | 3 | 3 | 3 | 3 | 0 | 3 | 3 | 3 | 3 | 3 | 3 |
| Good when only job complete event wanted | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 3 | 3 | 3 | 3 |
| Human Consumable and Machine Consumable | 0 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 0 | 0 | 0 | 0 |
| No limit to size of content | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 1 | 1 | 1 | 1 |
| Same owner on different workstations can get notification from selective subscriptions | 3 | 3 | 0 | 3 | 3 | 0 | 0 | 0 | 0 | 3 | 3 | 3 | 3 | 3 |
| Easy for NS to implement | 0 | 2 | 1 | 1 | 1 | 3 | 0 | 0 | 0 | 1 | 3 | 3 | 3 | 3 |
| Easy for NS cleanup when subscriptions no longer wanted | 3 | 3 | 2 | 2 | 2 | 3 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 3 |
| Anyone can be NR -> only subscriber can be NR | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 3 | 3 | 3 | 3 |
| Any NR can cancel subscription -> only owner can | 3 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 3 | 0 | 0 | 0 | 0 |
| Transport is reliable | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 1 | 3 | 1 | 3 |
| Transport widely deployed | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 1 | 3 | 3 |
| Transport is fast | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 |
| NR already deployed (2 = easy to deploy) | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 3 | 1 | 0 | 0 |
| NR already does further filtering | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 2 | 2 | 2 |
| NR already has interface to UR | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 3 | 3 | 3 | 3 |
| Easy to implement NR | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1 | 2 | 2 | 2 | 2 |
| NR can receive from multiple NS | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 3 | 3 | 3 | 3 |
| UR doesn't need Internet connection | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| UR always reachable | ? | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 1 |
| Server in middle can easily pass thru client subscriptions | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 3 | 3 | 3 | 3 |
| Can use 'application/ipp' -> needs new MIME type | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 0 | 0 | 0 | 0 | 0 |
| No new port is needed -> new default port is needed | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 0 | 3 | 3 | 3 | 3 |
| Likely to be accepted by IETF | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 2 | 3 | 3 | 1 | 1 |
| Totals: | 60 | 52 | 50 | 50 | 53 | 52 | 49 | 47 | 49 | 72 | 71 | 70 | 66 | 68 |

| Requirement - PRO -> CON | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Variant of: | 13 | 14 |  | 17 | 17 | 17 |  | 21 |  | 23 | 24 | 25 | 1-3 |  |
|  | TCP | email | IM | paging | configured paging |  | esc |
| Fits notification model [ipp-not] | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 0 | 0 | 0 | 0 | 0 |  |
| Fits current IPP Model [ipp-mod]; changes existing operations | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 |  |
| Likely to go through firewalls | 0 | 0 | 2 | 3 | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 2 |  |
| Fewer connections left open -> one per pending job | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 |  |
| Fewer connection setups to send/receive a notification | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 |  |
| Reduces network traffic, events can be batched into one Notification | 0 | 0 | 0? | 0? | 0? | 0? | 0 | 0 | 0 | 0 | 0 | 0 | 2 |  |
| Works with HTTP servers -> multiple responses needed | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 |  |
| Don't miss events after subscribing | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 0 |  |
| Per-Job and Per-Printer Subscription; not both | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 0 | 0 | 0 | 0 | 3 |  |
| End users and operators -> operators only | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 0 | 0 | 0 | 0 | 0 |  |
| Good for all events -> not good for page level or complete only | 3 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 |  |
| Good when only job complete event wanted | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 |  |
| Human Consumable and Machine Consumable | 0 | 0 | 3 | 0 | 3 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| No limit to size of content | 1 | 1 | 3 | 3 | 3 | 3 | 1 | 0 | 0 | 0 | 0 | 0 | 3 |  |
| Same owner on different workstations can get notification from selective subscriptions | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 |  |
| Easy for NS to implement | 3 | 3 | 3 | 2 | 1 | 1 | 3 | 3 | 3 | 3 | 3 | 3 | 0 |  |
| Easy for NS cleanup when subscriptions no longer wanted | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 |  |
| Anyone can be NR -> only subscriber can be NR | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 0 |  |
| Any NR can cancel subscription -> only owner can | 0 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 |  |
| Transport is reliable | 3 | 3 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 3 |  |
| Transport widely deployed | 3 | 3 | 3 | 3 | 3 | 3 | 2 | 2 | 3 | 3 | 3 | 3 | 3 |  |
| Transport is fast | 3 | 3 | 0 | 0 | 0 | 0 | 2 | 2 | 3 | 3 | 3 | 3 | 3 |  |
| NR already deployed (2 = easy to deploy) | 0 | 0 | 3 | 3 | 3 | 3 | 2 | 3 | 3 | 3 | 3 | 3 | 1 |  |
| NR already does further filtering | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 2? | 2? | 2? | 2? | 0 |  |
| NR already has interface to UR | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 1 |  |
| Easy to implement NR | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 2 |  |
| NR can receive from multiple NS | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 2 |  |
| UR doesn't need Internet connection | 0 | 0 | 2 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 0 |  |
| UR always reachable | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 3 | ? |  |
| Server in middle can easily pass thru client subscriptions | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 |  |
| Can use 'application/ipp' -> needs new MIME type | 0 | 0 | 3 | 2 | 3 | 3 | 2 | 2? | 2? | 2? | 2? | 2? | 3 |  |
| No new port is needed -> new default port is needed | 0 | 0 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 |  |
| Likely to be accepted by IETF | 3 | 3 | 3 | 3 | 3 | 3 | 1 | 2 | 2 | 2 | 2 | 2 | 2 |  |
| Totals: | 69 | 72 | 83 | 79 | 81 | 81 | 76 | 77 | 68 | 68 | 68 | 68 | 63 |  |