PWG-DRAFT  - 15 ISSUES are numbered and highlighted like this	Carl Kugler

ipp-ops-admin-990625.txt	IBM Corporation

T. Hastings

Xerox Corporation

June 25, 1999

Internet Printing Protocol/1.0 & 1.1: Additional Administrative Operations

Status of this Memo

This document is a PWG-Draft.  It is intended for registration following the registration procedures of IPP/1.0 [RFC2566] and IPP/1.1 [ipp-mod].  This version includes the comments discussed at the IPP telecon, on 6/23/1999.

Abstract

This document specifies eight additional OPTIONAL administrative operations for use with the Internet Printing Protocol/1.0 (IPP) [RFC2565, RFC2566] and IPP/1.1 [ipp-mod, ipp-pro].  These operations are 4 Printer object operations that operators/administrators may perform on a Printer object:

Set-Printer-Attributes

Enable-Printer

Disable-Printer

Shutdown-Printer

and 4 Job object operations that end-users may perform on their jobs and operators/administrators may perform on any job:

Set-Job-Attributes

Reprocess-Job

Cancel-Current-Job  (though the target is the Printer object)

Space-Current-Job  (though the target is the Printer object)

In addition, two operation attributes:  "job-message-from-operator" and "printer-message-from-operator" are included to set the corresponding Job and Printer Description attributes.

Finally, a new 'client-error-attributes-not-settable' is defined for use with the two Set operations.

The full set of IPP documents includes:

Design Goals for an Internet Printing Protocol [RFC2567]

Rationale for the Structure and Model and Protocol for the Internet Printing Protocol [RFC2568]

Internet Printing Protocol/1.1: Model and Semantics (this document)

Internet Printing Protocol/1.1: Encoding and Transport [IPP-PRO]

Internet Printing Protocol/1.1: Implementer's Guide [IPP-IIG]

Mapping between LPD and IPP Protocols [RFC2569]

The "Design Goals for an Internet Printing Protocol" document takes a broad look at distributed printing functionality, and it enumerates real-life scenarios that help to clarify the features that need to be included in a printing protocol for the Internet.  It identifies requirements for three types of users: end users, operators, and administrators.  It calls out a subset of end user requirements that are satisfied in IPP/1.0.  A few OPTIONAL operator operations have been added to IPP/1.1.

The "Rationale for the Structure and Model and Protocol for the Internet Printing Protocol" document describes IPP from a high level view, defines a roadmap for the various documents that form the suite of IPP specification documents, and gives background and rationale for the IETF working group's major decisions.

The "Internet Printing Protocol/1.1: Encoding and Transport" document is a formal mapping of the abstract operations and attributes defined in the model document onto HTTP/1.1 [RFC2616].  It defines the encoding rules for a new Internet MIME media type called "application/ipp".  This document also defines the rules for transporting over HTTP a message body whose Content-Type is "application/ipp".  This document defines a new scheme named 'ipp' for identifying IPP printers and jobs.

The "Internet Printing Protocol/1.1: Implementer's Guide" document gives insight and advice to implementers of IPP clients and IPP objects.  It is intended to help them understand IPP/1.1 and some of the considerations that may assist them in the design of their client and/or IPP object implementations.  For example, a typical order of processing requests is given, including error checking.  Motivation for some of the specification decisions is also included.

The "Mapping between LPD and IPP Protocols" document gives some advice to implementers of gateways between IPP and LPD (Line Printer Daemon) implementations.

Table of Contents

1.	Introduction	4

2.	New Operation attributes	4

2.1	New operation attribute:  "printer-message-from-operator" (text(127))	4

2.2	New operation attribute:  "job-message-from-operator" (text(127))	5

3.	New status code: 'client-error-attributes-not-settable'	6

4.	Summary of Administrative operations and Operation-Id Assignments	6

4.1	Printer Operations	7

4.1.1	Set-Printer-Attributes Operation	7

4.1.2	Disable-Printer Operation	11

4.1.3	Enable-Printer Operation	11

4.1.4	Shutdown-Printer Operation	12

4.2	Job Operations	13

4.2.1	Set-Job-Attributes	14

4.2.2	Reprocess-Job Operation	17

4.2.3	Cancel-Current-Job Operation	17

4.2.4	Space-Current-Job operation	19

# Introduction

The Internet Printing Protocol (IPP) is an application level protocol that can be used for distributed printing using Internet tools and technologies.  IPP version 1.1 (IPP/1.1) focuses only on end user functionality with a few administrative operations included.  This document defines additional OPTIONAL end user and administrative operations used to control Jobs and Printers. This document is a registration proposal for an extension to IPP/1.0 and IPP/1.1 following the registration procedures in those documents.

# New Operation attributes

This section defines the new "printer-message-from-operation" and "job-message-from-operator" operation attributes that set the corresponding Printer and Job Description attributes.

## New operation attribute:  "printer-message-from-operator" (text(127))

Type of registration:  attribute

Proposed keyword name of this attribute:  "printer-message-from-operator"

Types of attribute (Operation, Job Template, Job Description, Printer Description):  Operation

Operations to be used with if the attribute is an operation attribute:  See below

Object (Job, Printer, etc. if bound to an object):   Printer (already in IPP/1.0 and IPP/1.1)

Attribute syntax(es) (include 1setOf and range as in Section 4.2):  text(127)

Specification of this attribute (follow the style of IPP Model Section 4.2):

"printer-message-from-operator" (text(127))

The client OPTIONALLY supplies this attribute.  The Printer object SHOULD supports this operation attribute if it supports the corresponding Printer Description attribute.  The value of this attribute is a message from the operator about the Printer object on which the operator has just performed an operation.  If supported, the Printer copies the value to the Printer's "printer-message-from-operator" Printer Description attribute (see [ipp-mod] section 4.4.25).  If the client omits this attribute, the Printer either removes the attribute from the Printer or sets the attribute to the zero-length string, depending on implementation.

This operation attribute is defined for use with the following operator operations on the Printer object:

Pause-Printer - see [ipp-mod] section 3.2.7

Resume-Printer - see [ipp-mod] section 3.2.8

Purge-Jobs - see [ipp-mod] section 3.2.9

Disable-Printer - see section 4.1.2

Enable-Printer - see section 4.1.3

Shutdown-Printer - see section 4.1.4

The "printer-message-from-operator" operation attribute MUST NOT be supported as an operation attribute for the Set-Printer-Attributes operation.  If the operator wants to set the Printer's "printer-message-from-operator" Printer Description attribute when issuing the Set-Printer-Attributes operation, the client supplies the "printer-message-from-operator" with its new value as one of the Printer Description attributes in Group 2 in the request.  Otherwise the Printer leaves the value of the Printer's "printer-message-from-operator" Printer Description attribute unchanged by not explicitly setting the attribute.

## New operation attribute:  "job-message-from-operator" (text(127))

Type of registration:  attribute

Proposed keyword name of this attribute:  "job-message-from-operator"

Types of attribute (Operation, Job Template, Job Description, Printer Description):  Operation

Operations to be used with if the attribute is an operation attribute:  See below

Object (Job, Printer, etc. if bound to an object):   Job (already in IPP/1.0 and IPP/1.1)

Attribute syntax(es) (include 1setOf and range as in Section 4.2):  text(127)

Specification of this attribute (follow the style of IPP Model Section 4.2):

"job-message-from-operator" (text(127))

The client OPTIONALLY supplies this attribute.  The Printer object SHOULD supports this operation attribute if it supports the corresponding Job Description attribute.  The value of this attribute is a message from the operator about the Job object on which the operator has just performed an operation.  If supported, the Printer copies the value to the Job's "job-message-from-operator" Job Description attribute (see [ipp-mod] section 4.3.16).  If the client omits this attribute, the Printer either removes the attribute from the Job object or sets the attribute to the zero-length string, depending on implementation.

This operation attribute is defined for use with the following operator operations on the Job object:

Cancel-Job - see [ipp-mod] section 3.2.4

Hold-Job - see [ipp-mod] section 3.3.5

Release-Job - see [ipp-mod] section 3.3.6

Restart-Job - see [ipp-mod] section 3.3.7

Reprocess-Job - see section 4.2.2

Cancel-Current-Job - see section 4.2.3

Space-Current-Job - see section 4.2.4

The "job-message-from-operator" operation attribute MUST NOT be supported as an operation attribute for the Set-Job-Attributes operation.  If the operator wants to set the Job's "job-message-from-operator" Job Description attribute when issuing the Set-Job-Attributes operation, the client supplies the "job-message-from-operator" with its new value as one of the Job Description attributes in Group 2 in the request.  Otherwise the Printer leaves the value of the Job's "job-message-from-operator" Job Description attribute unchanged by not explicitly setting the attribute.

# New status code: 'client-error-attributes-not-settable'

Type of registration:  status code

Keyword symbolic name of this status code value:  'client-error-attributes-not-settable'

Numeric value (to be assigned by the IPP Designated Expert in consultation with IANA):

Operations that this status code may be used with:  Set-Printer-Attributes, Set-Job-Attributes

Specification of this status code (follow the style of IPP Model Section 13 APPENDIX B:  Status Codes and Suggested Status Code Messages):

#### 13.1.4.20 client-error-attributes-not-settable (0x0413)

In a Set-Printer-Attributes or Set-Job-Attributes request, if the Printer object does not support one or more attributes as settable, and the client supplied the "ipp-attributes-fidelity" operation attribute with the 'true' value, the Printer object MUST return this status code.  The Printer object MUST also return in the Unsupported Attributes Group all the attributes and/or values supplied by the client that are not settable.  See [ipp-mod] section 3.1.7.  For example, if the request indicates 'job-state', all implementations MUST reject the request.  As another example, if the request indicates an attribute that is supported, but not settable by this implementation, such as, say, "printer-name", the implementation rejects the request.  If the "ipp-attribute-fidelity" attribute is 'false', the Printer MUST ignore attributes that are not settable, rather than reject the request and return this status code.

# Summary of Administrative operations and Operation-Id Assignments

The Administrative operations are summarized in the following table:

| Operation Name | Operation-Id | Brief description |
| --- | --- | --- |
| Set-Printer-Attributes | 0x?? | Sets attribute values of the Printer object |
| Enable-Printer | 0x?? | Allows the Printer to accept create job operations |
| Disable-Printer | 0x?? | Prevents the Printer from accepting create job operations |
| Shutdown-Printer | 0x?? | Shuts the Printer down in several ways |
| Set-Job-Attributes | 0x?? | Sets attribute values of the Job object |
| Reprocess-Job | 0x?? | Creates a copy of a completed job with a new Job ID and processes it |
| Cancel-Current-Job | 0x?? | Cancels the current job on the Printer |
| Space-Current-Job ISSUE 1: better name? | 0x?? | Skips or repeats some number of impressions for current job on the Printer |

All of the operations in this registration proposal specification are OPTIONAL for an IPP object to support.  Unless the specification of an OPTIONAL operation requires support of another OPTIONAL operation, conforming implementations may support any combination of these operations.

## Printer Operations

All Printer operations are directed at Printer objects.  A client MUST always supply the "printer-uri" operation attribute in order to identify the correct target of the operation.  These descriptions assume all of the common semantics of IPP/1.1 Model and Semantics [ipp-mod].

### Set-Printer-Attributes Operation

Type of registration:  operation

Proposed name of this operation:  Set-Printer-Attributes

Object Target:  Printer

Specification of this operation:

This OPTIONAL operation allows a client to set the values of the attributes of a Printer object.   In the request, the client supplies the set of Printer attribute names and values that are to be set.  In the response, the Printer object returns success or rejects the request with indications of which attribute or attributes could not be set.

How the Printer object validates the client-supplied attributes in the Set-Printer-Attributes request is implementation-dependent, since there are no corresponding Printer attributes that specify the allowed values that may be set on the Printer object.

The Printer MUST accept this operation in any state, i.e., for any of the values of the Printer object's "printer-state" attribute.

For Printer attributes that are supported, some MUST be settable, some SHOULD be settable, some MAY be settable, and some MUST NOT be settable as indicated in the following table:

| IPP Printer Attributes | Settable? |
| --- | --- |
| all Job Template Default attributes ("xxx-default" [ipp-mod] section 4.2 and extensions) | SHOULD if attribute supported |
| all Job Template Supported attributes ("xxx-supported" [ipp-mod] section 4.2 and extensions) | SHOULD if attribute supported |
| all Job Template Ready attributes ("xxx-ready" [ipp-mod] section 4.2 and extensions) | SHOULD if attribute supported |
| printer-uri-supported | SHOULD |
| uri-security-supported | SHOULD |
| uri-authentication-supported | SHOULD |
| printer-name | MAY |
| printer-location | SHOULD if attribute supported |
| printer-info | SHOULD if attribute supported |
| printer-driver-installer | SHOULD if attribute supported |
| printer-make-and-model | MAY |
| printer-more-info-manufacturer | MAY |
| printer-state | MUST NOT |
| printer-state-reasons | MUST NOT |
| printer-state-message | MUST NOT if attribute supported |
| ipp-versions-supported | MAY |
| operations-supported | SHOULD |
| ipp-multiple-document-jobs-supported | MUST NOT if attribute supported |
| charset-configured | SHOULD |
| charset-supported | MAY |
| natural-language-configured | SHOULD |
| generated-natural-language-supported | MAY |
| document-format-default | SHOULD |
| document-format-supported | SHOULD |
| printer-is-accepting-jobs | MUST NOT - see Enable-Printer/Disable-Printer |
| queued-job-count | MUST NOT |
| printer-message-from-operator | MUST NOT - see "printer-message-from-operator" operation attribute ISSUE 2: Better to set explicitly in Set-Printer-Attributes? If yes, change to "MUST if attribute supported". Operation attribute in the other admin operations only. |
| color-supported | MAY if attribute supported |
| reference-uri-schemes-supported | MAY if attribute supported |
| pdl-override-supported | MUST NOT |
| printer-up-time | MUST NOT |
| printer-current-time | MAY if attribute supported |
| multiple-operation-time-out | SHOULD if attribute supported |
| compression-supported | MAY |
| job-k-octets-supported | SHOULD if attribute supported |
| job-impressions-supported | SHOULD if attribute supported |
| job-media-sheets-supported | SHOULD if attribute supported |
| pages-per-minute | MAY if attribute supported |
| pages-per-minute-color | MAY if attribute supported |

Access Rights: The authenticated user (see [ipp-mod] section 8.3) performing this operation must be an operator or administrator of the Printer object (see [ipp-mod] sections 1 and 8.5).  Otherwise, the IPP Printer MUST reject the operation and return:  'client-error-forbidden', 'client-error-not-authenticated', or 'client-error-not-authorized' as appropriate.

Most Printer attributes will require administrator privileges to set, such as "xxx-supported", while some will require operator privileges only, such as "media-ready" and "printer-message-from-operator".  Which attributes require which privileges depends on implementation and MAY depend on site policy.

#### Set-Printer-Attributes Request

The following sets of attributes are part of the Set-Printer-Attributes Request:

Group 1: Operation Attributes

Natural Language and Character Set:

The "attributes-charset" and "attributes-natural-language" attributes as described in [ipp-mod] section 3.1.4.1.

Target:

The "printer-uri" (uri) operation attribute which is the target for this operation as described in [ipp-mod] section 3.1.5.

Requesting User Name:

The "requesting-user-name" (name(MAX)) attribute SHOULD be supplied by the client as described in [ipp-mod] section 8.3.

"ipp-attribute-fidelity" (boolean):

The client OPTIONALLY supplies this attribute.  The Printer object MUST support this attribute.  This operation attribute is used to specify whether or not the sets are to be atomic.  If 'false', or not present, Printer sets what it can and returns the unset attribute/value pairs in the Unsupported Attributes group.  If 'true', either all supplied attributes MUST be set or the operation MUST be rejected.  All Printer objects MUST support both types of setting.

"document-format" (mimeMediaType):

The client SHOULD supply this attribute.  The Printer object MUST support this attribute.  This attribute is useful for a client to select the interpreter to which the attribute modification should be applied.  See [ipp-mod] section 3.2.5.1 "Get-Printer-Attributes Request".

If the Printer object does not distinguish between different sets of supported values for each different document format when validating jobs in the create and Validate-Job operations, it MUST NOT distinguish between different document formats in the Set-Printer-Attributes operation.  If the Printer object does distinguish between different sets of supported values for each different document format specified by the client, this specialization applies only to the same Printer attributes as the Get-Printer-Attributes operation (see [ipp-mod] section 3.2.5.1).

If the client omits this "document-format" operation attribute, the Printer object MUST respond as if the attribute had been supplied with the value of the Printer object's "document-format-default" attribute.  It is recommended that the client always supply a value for "document-format", since the Printer object's "document-format-default" may be 'application/octet-stream', in which case the set attributes and values are for the union of the document formats that the Printer can automatically sense.  For more details, see the description of the 'mimeMediaType' attribute syntax in [ipp-mod] section 4.1.9.

If the client supplies a value for the "document-format" Operation attribute that is not supported by the Printer, i.e., is not among the values of the Printer object's "document-format-supported" attribute, the Printer object MUST reject the operation and return the 'client-error-document-format-not-supported' status code.

Group 2: Printer Attributes

The client MUST supply a set of Printer attributes as defined in [ipp-mod] section 4.2 Job Template Attributes ("xxx-default", "xxx-supported", and "xxx-ready" attributes) and section 4.4 Printer Description Attributes.  Each Printer attribute supplied in Group 2 replaces the value(s) of the corresponding Printer attribute on the target Printer object.  If a Printer object attribute had not been configured yet and so had the 'no-value' out-of-band value (see [ipp-mod] 4.1), the supplied value(s) replace the 'no-value' value.  For attributes that can have multiple values (1setOf), all values supplied by the client replace all values of the corresponding Printer object attribute.

#### Set-Printer-Attributes Response

The Printer object returns the following sets of attributes as part of the Get-Printer-Attributes Response:

Group 1: Operation Attributes

Status Message:

In addition to the REQUIRED status code returned in every response, the response OPTIONALLY includes a "status-message" (text(255)) and/or a "detailed-status-message" (text(MAX)) operation attribute as described in [ipp-mod] sections 13 and 3.1.6.

Natural Language and Character Set:

The "attributes-charset" and "attributes-natural-language" attributes as described in [ipp-mod] section 3.1.4.2.

Group 2: Unsupported Attributes

See [ipp-mod] section 3.1.7 for details on returning Unsupported Attributes.

In the case of attributes that are supported, but are not settable by the implementation (see table above), the Printer object returns the client-supplied attribute(s) with a substituted value of 'not-settable'.  This value's syntax type is "out-of-band" and its encoding is defined by special rules for "out-of-band" values in the "Encoding and Transport" document [IPP-PRO].  Its value indicates that the attribute is not settable.  Group 2 is returned independent of the value for the "ipp-attribute-fidelity" attribute supplied by the client.

ISSUE 3:  Should we add a Group 3: Printer Object Attributes which returns the previous values for any attributes set?

### Disable-Printer Operation

Type of registration:  operation

Proposed name of this operation:  Disable-Printer

Object Target:  Printer

Specification of this operation:

This OPTIONAL operation allows a client to stop the Printer object from accepting jobs, i.e., cause the Printer to reject subsequent create job operations (Print-Job, Print-URI, and Create-Job operation) and return the 'server-error-not-accepting-jobs' status code.  The Printer still accepts all other operations.  All previously submitted Jobs and currently processing Jobs continue unaffected.  The Printer sets the value of its "printer-is-accepting-jobs" read-only Printer Description attribute to 'false' (see [ipp-mod] section 4.4.20), no matter what the previous value was.  This operation has no immediate effect on the Printer's "printer-state" and "printer-state-reasons" attributes.

Note:  Use the Enable-Printer operation (section 4.1.3) to enable a Printer to accept Jobs again.

If the Disable-Printer operation is supported, then the Enable-Printer operation MUST be supported, and vice-versa.

Note:  Use the Enable-Printer and Disable-Printer operations to allow or prevent input to a Printer.  Use the Pause-Printer and Resume-Printer operations to prevent or allow output from the Printer.

Whether or not the Disable-Printer operation stops jobs that are submitted using job submission protocols other than IPP, depends on implementation, i.e., on whether the IPP protocol is being used as a universal management protocol or just to manage IPP jobs, respectively.

Access Rights: The authenticated user (see [ipp-mod] section 8.3) performing this operation must be an operator or administrator of the Printer object (see [ipp-mod] Sections 1 and 8.5).  Otherwise, the IPP Printer MUST reject the operation and return:  'client-error-forbidden', 'client-error-not-authenticated', or 'client-error-not-authorized' as appropriate.

The Disable-Printer Request and Disable-Printer Response have the same attribute groups and attributes as the Pause-Printer operation (see [ipp-mod] sections 3.2.7.1 and 3.2.7.2), including the new "printer-message-from-operator" operation attribute (see section 2.1).

### Enable-Printer Operation

Type of registration:  operation

Proposed name of this operation:  Enable-Printer

Object Target:  Printer

Specification of this operation:

This OPTIONAL operation allows a client to start the Printer object accepting jobs, i.e., cause the Printer to accept subsequent create job operations (Print-Job, Print-URI, and Create-Job operation).  The Printer still accepts all other operations.  All previously submitted Jobs and currently processing Jobs continue unaffected.  The Printer sets the value of its "printer-is-accepting-jobs" read-only Printer Description attribute to 'true' (see [ipp-mod] section 4.4.20), no matter what the previous value was.  This operation has no immediate effect on the Printer's "printer-state" and "printer-state-reasons" attributes.

Note:  Use the Disable-Printer operation (section 4.1.2) to stop a Printer from accepting Jobs.

If the Enable-Printer operation is supported, then the Disable-Printer operation MUST be supported, and vice-versa.

Note:  Use the Enable-Printer and Disable-Printer operations to allow or prevent input to a Printer.  Use the Pause-Printer and Resume-Printer operations to prevent or allow output from the Printer.

Whether or not the Enable-Printer operation allows acceptance of  jobs that are submitted using job submission protocols other than IPP, depends on implementation, i.e., on whether the IPP protocol is being used as a universal management protocol or just to manage IPP jobs, respectively.

Access Rights: The authenticated user (see [ipp-mod] section 8.3) performing this operation must be an operator or administrator of the Printer object (see [ipp-mod] Sections 1 and 8.5).  Otherwise, the IPP Printer MUST reject the operation and return:  'client-error-forbidden', 'client-error-not-authenticated', or 'client-error-not-authorized' as appropriate.

The Enable-Printer Request and Enable-Printer Response have the same attribute groups and attributes as the Pause-Printer operation (see [ipp-mod] sections 3.2.7.1 and 3.2.7.2), including the new "printer-message-from-operator" operation attribute (see section 2.1).

### Shutdown-Printer Operation

Type of registration:  operation

Proposed name of this operation:  Enable-Printer

Object Target:  Printer

Specification of this operation:

This OPTIONAL operation allows a client to shut down a Printer, i.e., stop processing jobs and terminating all communications with the Printer.  The Printer adds the 'shutdown' value (see [ipp-mod] section 4.4.11) to its "printer-state-reasons" Printer Description attribute immediately.  The Printer is disabled immediately (see the Disable-Printer operation in section 4.1.2).  The "when" operation attribute specifies how much processing occurs before the shutdown takes place.  All other requests continue to be accepted until the printer is shutdown.

Whether or not the Shutdown-Printer operation affects jobs that were submitted to the device using job submission protocols other than IPP, depends on implementation, i.e., on whether the IPP protocol is being used as a universal management protocol or just to manage IPP jobs, respectively.

The Printer object MUST accept this operation in any state and transition the Printer object to the 'idle' state.

Access Rights: The authenticated user (see [ipp-mod] section 8.3) performing this operation must be an operator or administrator of the Printer object (see [ipp-mod] sections 1 and 8.5).  Otherwise, the IPP object MUST reject the operation and return: client-error-forbidden, client-error-not-authenticated, and client-error-not-authorized as appropriate.

The Shutdown-Printer Request and Shutdown-Printer Response have the same attribute groups and attributes as the Pause-Printer operation (see [ipp-mod] sections 3.2.7.1 and 3.2.7.2), including the new "printer-message-from-operator" operation attribute (see section 2.1), and with the addition of the following Group 1 operation attributes in the request:

"when" (type2 keyword)

The client OPTIONALLY supplies this attribute.  The Printer object MUST support this attribute, if it supports this operation.  The value of this attribute indicates when to shutdown the printer.  If the client omits this attribute, the Printer assumes the 'after-current' value.

Standard keyword values are:

'now' - cancel the currently printing job(s) and shut down the Printer.  Jobs in the 'held' and 'pending' state remain in those states.

'after-current' - shutdown the Printer after the current job finishes printing.  Jobs in the 'held' and 'pending' state remain in those states.

'after-all' - shutdown the Printer after all 'pending' jobs finish printing.  Jobs in the 'held' state remain in the 'held' state.

"non-process-run-out" (boolean)

The client OPTIONALLY supplies this attribute.  The Printer object OPTIONALLY supports this attribute.  This attribute indicates whether or not the printer is to perform "non-process run-out", i.e., move the last printed sheet to the stacker, before shutting down.

ISSUE 4:  What behavior if the client omits this attributes?

ISSUE 5:  What behavior if the implementation does not support this attribute?

"synchronize" (boolean)

The client OPTIONALLY supplies this attribute.  The Printer object OPTIONALLY supports this attribute.  This attribute indicates whether or not the printer is to synchronize the checkpoint data for the current job with the pages that have actually printed.  If this attribute is supported, then a value of 'true' implies that the Printer will be able to resume the job at the point of synchronization when the Printer is restarted.

ISSUE 6:  Is the current job automatically restarted when the Printer is restarted?  Or does some client have to issue a Restart-Job operation?

## Job Operations

All Job operations are directed at Job objects.  A client MUST always supply some means of identifying the Job object in order to identify the correct target of the operation.  That job identification MAY either be a single Job URI or a combination of a Printer URI with a Job ID.  The IPP object implementation MUST support both forms of identification for every job.

### Set-Job-Attributes

Type of registration:  operation

Proposed name of this operation:  Set-Job-Attributes

Object Target:  Job

Specification of this operation:

This OPTIONAL operation allows a client to set the values of the attributes of a Job object.   In the request, the client supplies the set of Job attribute names and values that are to be set.  In the response, the IPP object returns success or rejects the request with indications of which attribute or attributes could not be set.

This operation is almost identical to the Set-Printer-Attributes operation (see section 4.1.1).  The only differences are that the operation is directed at a Job object rather than a Printer object, there is no "document-format" operation attribute used when setting a Job object, and the validation is the same as the create job operations, i.e., depend on the "xxx-supported" Printer Description attributes.

The validation of the Set-Job-Attributes request is performed as if the job had been submitted originally with the new values.  If such a create job operation would have been accepted, then the Set-Job-Attributes MUST be accepted.  If such a create job operation would have been rejected, then the Set-Job-Attributes MUST be rejected and the Job MUST be unchanged.

The IPP object MUST accept or reject the request based on the job's current state and transition the job to the indicated new state as follows:

| Current "job-state" | New "job-state" | IPP object's response status code and action: |
| --- | --- | --- |
| 'pending' | 'pending' | 'successful-ok' |
| 'pending' | 'pending-held' | 'successful-ok' - needed resources are not ready |
| 'pending-held' | 'pending-held' | 'successful-ok' |
| 'pending-held' | 'pending' | 'successful-ok' - needed resources are ready |
| 'processing' | 'processing' | 'successful-ok' or 'client-error-not-possible' depending on the attributes being set, whether the job has started marking media, and/or implementation |
| 'processing-stopped' | 'processing-stopped' | 'successful-ok' or 'client-error-not-possible' depending on the attributes being set, whether the job has started marking media, and/or implementation |
| 'completed' | 'completed' | 'client-error-not-possible' |
| 'canceled' | 'canceled' | 'client-error-not-possible' |
| 'aborted' | 'aborted' | 'client-error-not-possible' |

For Job attributes that are supported, some MUST be settable, some SHOULD be settable, some MAY be settable, and some MUST NOT be settable as indicated in the following table:

| IPP Job Attributes | Settable? |
| --- | --- |
| all Job Template Job attributes ("xxx" [ipp-mod] section 4.2 and extensions) | SHOULD if attribute supported |
| job-uri | MUST NOT |
| job-id | MUST NOT |
| job-printer-uri | MUST NOT |
| job-more-info | MUST NOT if attribute supported |
| job-name | MUST - also set in create operation |
| job-originating-user-name | MUST NOT - set in create operation |
| job-state | MUST NOT |
| job-state-reasons | MUST NOT |
| job-state-message | MUST NOT if attribute supported |
| number-of-documents | MUST NOT |
| output-device-assigned | MUST NOT |
| time-at-creation | MUST NOT |
| time-at-processing | MUST NOT |
| time-at-completed | MUST NOT |
| job-printer-up-time | MUST NOT |
| date-time-at-creation | MUST NOT if attribute supported |
| date-time-at-processing | MUST NOT if attribute supported |
| date-time-at-completed | MUST NOT if attribute supported |
| number-of-intervening-jobs | MUST NOT if attribute supported |
| job-message-from-operator | MUST if attribute supported and if operator |
| job-k-octets | MUST NOT if attribute supported |
| job-impressions | MAY if attribute supported - see Rule 1 |
| job-media-sheets | MAY if attribute supported - see Rule 1 |
| job-k-octets-processed | MUST NOT if attribute supported |
| job-impressions-completed | MUST NOT if attribute supported |
| job-media-sheets-completed | MUST NOT if attribute supported |
| attributes-charset | MUST NOT - set in create operation |
| attributes-natural-language | MUST NOT - set in create operation |

Rule 1 - However, an implementation MAY refuse to allow this Job Description attribute to be set, if it has determined a more reliable value from the document content.

Whether or not the Set-Job-Attributes operation affects jobs that are submitted using job submission protocols other than IPP, depends on implementation, i.e., on whether the IPP protocol is being used as a universal management protocol or just to manage IPP jobs, respectively.

Access Rights: The authenticated user (see [ipp-mod] section 8.3) performing this operation must either be the job owner or an operator or administrator of the Printer object (see [ipp-mod] sections 1 and 8.5).  Otherwise, the IPP object MUST reject the operation and return: 'client-error-forbidden', 'client-error-not-authenticated', or 'client-error-not-authorized' as appropriate.

#### Set-Job-Attributes Request

The following sets of attributes are part of the Set-Printer-Attributes Request:

Group 1: Operation Attributes

Natural Language and Character Set:

The "attributes-charset" and "attributes-natural-language" attributes as described in [ipp-mod] section 3.1.4.1.

Target:

The "printer-uri" (uri) operation attribute which is the target for this operation as described in [ipp-mod] section 3.1.5.

Requesting User Name:

The "requesting-user-name" (name(MAX)) attribute SHOULD be supplied by the client as described in [ipp-mod] section 8.3.

"ipp-attribute-fidelity" (boolean):

The client OPTIONALLY supplies this attribute.  The Printer object MUST support this attribute if it supports this operation.  This operation attribute is used to specify whether or not the sets are to be atomic.  If 'false', or not present, Printer sets what it can and returns the unset attribute/value pairs in the Unsupported Attributes group.  If 'true', either all supplied attributes MUST be set or the operation MUST be rejected.  All Printer objects MUST support both types of setting.  See [ipp-mod] section 15 for a full description of "ipp-attribute-fidelity" and its relationship to other attributes, especially the Printer object's "pdl-override-supported" attribute.

Group 2: Printer Attributes

The client MUST supply a set of Job attributes as defined in [ipp-mod] section 4.2 Job Template Attributes ("xxx" attributes) and section 4.3 Job Description Attributes.  Each Job attribute supplied in Group 2 replaces the value(s) of the corresponding Job attribute on the target Job object.  For attributes that can have multiple values (1setOf), all values supplied by the client replace all values of the corresponding Printer object attribute.

#### Set-Job-Attributes Response

The Printer object returns the following sets of attributes as part of the Get-Job-Attributes Response:

Group 1: Operation Attributes

Status Message:

In addition to the REQUIRED status code returned in every response, the response OPTIONALLY includes a "status-message" (text(255)) and/or a "detailed-status-message" (text(MAX)) operation attribute as described in [ipp-mod] sections 13 and 3.1.6.

Natural Language and Character Set:

The "attributes-charset" and "attributes-natural-language" attributes as described in [ipp-mod] section 3.1.4.2.

Group 2: Unsupported Attributes

See [ipp-mod] section 3.1.7 for details on returning Unsupported Attributes.

The attributes returned are the same as for the create operation with the same new attribute values.  However, in the case of attributes that are supported, but are not settable by the implementation (see table above), the Printer object returns the client-supplied attribute(s) with a substituted value of 'not-settable'.  This value's syntax type is "out-of-band" and its encoding is defined by special rules for "out-of-band" values in the "Encoding and Transport" document [IPP-PRO].  Its value indicates that the attribute is not settable.

Group 2 is returned independent of the value for the "ipp-attribute-fidelity" attribute supplied by the client.  However, if "ipp-attribute-fidelity" is 'true', the 'client-error-attributes-not-settable' status code is returned.  If "ipp-attribute-fidelity" is 'false', the 'successful-ok-ignored-or-substituted-attributes' status code is returned.

ISSUE 7:  Should we add a Group 3: Printer Object Attributes which returns the previous values for any attributes set?

### Reprocess-Job Operation

This OPTIONAL operation allows a client to re-process a copy of a job that is retained in the queue after processing has completed (see [ipp-mod] section 4.3.7.2).  This operation is the same as the Restart-Job operation (see [ipp-mod] section 3.3.7), except that the Printer creates a new job that is a copy of the identified job and the identified job is unchanged.  The new job is assigned new values to the "job-uri" and "job-id" attributes.  The identified job moves to the Job History after a suitable period, independent of whether one or more Reprocess-Job operations have been performed on it.

If the Set-Job-Attributes operation is supported, then the "job-hold-until" operation attribute MUST be supported with at least the 'indefinite' value, so that a client can modify the new job before it is scheduled for processing using the Set-Job-Attributes operation.  After modifying the job, the client can release the job for processing, by using the Release-Job operation specifying the newly assigned "job-uri" or "job-id" for the new job.

### Cancel-Current-Job Operation

This OPTIONAL operation allows a client to cancel the current job on the target Printer.  Since a Job might already be marking by the time a Cancel-Current-Job is received, some media sheet pages might be printed before the job is actually terminated.

If there are no jobs in the 'processing' or 'processing-stopped' states, the Printer rejects the request and returns the 'client-error-not-possible' status code.  Otherwise, the Printer MUST perform the Cancel-Current-Job request, as if the client had supplied the "job-uri" or the "job-id" of the current job in a Cancel-Job operation.  If more than one job is in the 'processing' or 'processing-stopped' states, the one that is marking is canceled and the others are unaffected.

Warning:  On a shared printer, there is a race condition.  Between the time that a user issues this operation and its acceptance, the current job might change to a different job.  If the user is authenticated to cancel the new job, the wrong job is canceled.

Access Rights: The authenticated user (see [ipp-mod] section 8.3) performing this operation must either be the job owner of the current job or an operator or administrator of the Printer object (see [ipp-mod] sections 1 and 8.5).  Otherwise, the IPP object MUST reject the operation and return: 'client-error-forbidden', 'client-error-not-authenticated', or 'client-error-not-authorized' as appropriate.

The Cancel-Current-Job Request and Cancel-Current-Job Response have the same attribute groups and attributes as the Pause-Printer operation (see [ipp-mod] sections 3.2.7.1 and 3.2.7.2), including the new "job-message-from-operator" operation attribute (see [ipp-mod] section 2.2), with the addition of the following Group 1 Operation attribute in the request:

"non-process-run-out" (boolean):

The client OPTIONALLY supplies this Operation attribute.  The IPP object OPTIONALLY supports this operation attribute, if it is able to perform a non-process-run-out, i.e., remove the last few printed sheets of a job that is finished printing on a continuous-forms printer.  Normally, on such a printer, the last sheets of a job remain in the printer and are forced out by the next job, thereby saving time when printing one job after another.  However, when shutting done the Printer is it desirable to remove the end of the last job.

ISSUE 8:  What behavior if the client omits this attributes?

ISSUE 9:  What behavior if the implementation does not support this attribute?

ISSUE 10:  Why is this automatic on a continuous form printer?  When would an operator want to shutdown the Printer and NOT run out the last sheets.  It would be simpler to require process-run-out when shutting down (for continuous and cut sheet printers).

"synchronize" (boolean):

The client OPTIONALLY supplies this Operation attribute.  The IPP object OPTIONALLY supports this operation attribute, if it is able to synchronize the data, i.e., synchronize the checkpoint data for the current job with the pages that have actually printed.  If this attribute is supported, a value of 'true' causes the Printer to resume the job at the point of synchronization when the Printer is restarted.

ISSUE 11:  Should we define a Restart-Printer operation?

ISSUE 12:  What behavior if the client omits this attributes?

ISSUE 13:  What behavior if the implementation does not support this attribute?

ISSUE 14:  What does this attribute mean when the "when" attribute is 'after-current' or 'after-all'?  Or should this be a new value for "when", i.e., 'after-synchronization' so it is only used when shutting down the Printer in the middle of the current job?

### Space-Current-Job operation

This OPTIONAL operation allows a client to repeat or skip a specified number of impressions for the current job on the target Printer.  This operation is typically supported in a continuous forms implementation for synchronizing the web after forms run out or media change.

If there are no jobs in the 'processing' or 'processing-stopped' states, the Printer rejects the request and returns the 'client-error-not-possible' status code.  Otherwise, the Printer repeats or skips the indicated number of impressions specified by the "back-space" or "forward-space" operation attribute, respectively.

Warning:  On a shared printer, there is a race condition.  Between the time that a user issues this operation and its acceptance, the current job might change to a different job.  If the user is authenticated to space the new job, the wrong job is spaced.

Access Rights: The authenticated user (see [ipp-mod] section 8.3) performing this operation must either be the job owner of the current job or an operator or administrator of the Printer object (see [ipp-mod] sections 1 and 8.5).  Otherwise, the IPP object MUST reject the operation and return: 'client-error-forbidden', 'client-error-not-authenticated', or 'client-error-not-authorized' as appropriate.

The Space-Current-Job Request and Space-Current-Job Response have the same attribute groups and attributes as the Pause-Printer operation (see [ipp-mod] sections 3.2.7.1 and 3.2.7.2), including the new "job-message-from-operator" operation attribute (see [ipp-mod] section 2.2), with the addition of the following Group 1 Operation attribute in the request:

"back-space" (integer(1:MAX)):

The client OPTIONALLY supplies this Operation attribute.  The IPP object OPTIONALLY supports this operation attribute, if it is able to repeat impressions.

If the client supplies a value that specifies more impressions than the job has performed, the job is positioned at the beginning without any indication.

"forward-space" (integer(1:MAX)):

The client OPTIONALLY supplies this Operation attribute.  The IPP object OPTIONALLY supports this operation attribute, if it is able to skip impressions.

If the client supplies a value that specifies more impressions than remain in the job, the job is positioned at the end without any indication.

"non-process-run-out" (boolean):

The client OPTIONALLY supplies this Operation attribute.  The IPP object OPTIONALLY supports this operation attribute, if it is able to perform a non-process-run-out, i.e., remove the last few printed sheets of a job that is finished printing on a continuous-forms printer.  Normally, on such a printer, the last sheets of a job remain in the printer and are forced out by the next job, thereby saving time when printing one job after another.  However, when backspacing or advance the Printer is it desirable to be able to specify whether or not to force out the most recently printed sheets.  ISSUE 15:  Correct?