Property Table of JMP Attributes

From:  Tom Hastings;  Date:  5/8/97;  File:  attr-tab.doc

Col	Description

Head

#	enum value for jmAttributeTypeIndex, e.g., JmAttributeTypeIndexTC

I/O	Integer vs. OCTET STRING:

I = Integer32(-2..2147483647)

O = OCTET STRING(SIZE(0..63))

I/O = Integer OR OCTET STRING

I+O = Integer AND OCTET STRING

TC	Integer is a textual-convention in this or the Printer MIB

M	Conformance requirements for an agent:

M = Mandatory

<blank> = Conditionally Mandatory

>1	MULTI-ROW (more than one row allowed):

>1 = MULTI-ROW

<blank> = one one row allowed for this attribute

S	Accessible through Job State Table (and the Attributes Table)

<blank> = only in the Attributes table

L	linked with the Printer MIB, such that the Printer MIB must be implemented for

this attribute to provide a meaningful value to the application.  Printer MIB

textual-conventions are not flagged as linked.

M/A	Application program usage:

M = Monitoring application will use

A = Accounting (or system utilization) application will use

MA = both a Monitoring and an Accounting application will use.

S/D	STATIC vs. DYNAMIC:

S = STATIC (doesn't usually change, ModifyJob operation may change)

D = DYNAMIC (expected to change during the life time of the job)

S/P/D/A	When is the STATIC or DYNAMIC attribute value first assigned:

S = submission time

P = start of processing

D = during processing and/or printing

C = completion

a = any time.

states = job state(s) in which the attribute value is of interest:

H = held

Pen = Pending

Pro = Processing

Pri = Printing

N = needsAttention

Can = canceled

Com = completed

a = all states.

| # | Attribute | I/O | TC | M | >1 | L | S | M/A | S/D | S/P/D/A | states |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | other | I/O |
| MA |
| a | a |
| 2 | unknown | I/O |
| MA |
| a | a |
|  | Job State attributes |
| 3 | jobState | I | TC | M |
|  | S | MA | D | a | a |
| 4 | jobStateAssociatedValue | I |
| L | S | MA | D | a | a |
| 5 | jobStateReasons1 | I | TC |
|  | MA | D | a | a |
| 6 | jobStateReasons2 | I | TC |
|  | M | D | a | a |
| 7 | jobStateReasons3 | I | TC |
|  | M | D | a | a |
| 8 | jobStateReasons4 | I | TC |
|  | M | D | a | a |
| 9 | numberOfInterveningJobs | I |
| M |
|  | S | M | D | S | Pen |
| 10 | deviceAlertCode | I | TC | M |
| L | S | M | D | D | N |
| 11 | processingMessage | O |
|  | >1 |
|  | M | D | D | Pro Pri |
|  | Job Identification attributes |
| 12 | serverAssignedJobName | O |
| MA | S | S | a |
| 13 | jobName | O |
| MA | S | S | a |
| 14 | jobServiceTypes | I | TC |
|  | MA | S | S | a |
| 15 | jobOwner | O |
| MA | S | S | a |
| 16 | jobAccountName | O |
| A | S | S | a |
| 17 | jobSourceChannelIndex | I |
| L |
| M | S | S | a |
| 18 | jobSourcePlatformType | I | TC |
|  | MA | S | S | a |
| 19 | submittingServerName | O |
| MA | S | S | a |
| 20 | submittingApplicationName | O |
| MA | S | S | a |
| 21 | deviceNameRequested | O |
| MA | S | S | a |
| 22 | queueNameRequested | O |
| MA | S | S | a |
| 23 | physicalDeviceIndex | I |
|  | >1 | L |
| MA | S | P | a |
| 24 | physicalDeviceName | O |
|  | >1 |
|  | MA | S | P | a |
| 25 | numberOfDocuments | I |
| MA | S | S | a |
| 26 | fileName | O |
|  | >1 |
|  | MA | S | S | a |
| 27 | documentName | O |
|  | >1 |
|  | MA | S | S | a |
| 28 | jobComment | O |
| M | S | S | a |
| 29 | documentFormatIndex | I |
|  | >1 | L |
| MA | S | S P D | a |
| 30 | documentFormatType | I | TC |
| >1 |
|  | MA | S | S P D | a |
|  | Job Parameter attributes |
| 31 | jobPriority | I |
| MA | S | S | a |
| 32 | jobProcessAfterDateAndTime | O |
| MA | S | S | H Pen |
| 33 | jobHoldUntil | I |
| MA | S | S | H Pen |
| 34 | outputBinIndex | I |
| M | >1 | L | S | M | S | C | Can Com |
| 35 | outputBinName | O |
|  | >1 |
|  | M | S | C | Can Com |
| 36 | sides | I |
|  | >1 |
|  | MA | S | S P D | a |
| 37 | finishing | I | TC |
| >1 |
|  | MA | S | S P D | a |
|  | Image Quality attributes (requested and used) |
| 38 | printQualityRequested | I | TC |
| >1 |
|  | M | S | S | a |
| 39 | printQualityUsed | I | TC |
| >1 |
|  | A | S | D | Com |
| 40 | tonerEcomonyRequested | I | TC |
| >1 |
|  | M | S | S | a |
| 41 | tonerEcomonyUsed | I | TC |
| >1 |
|  | A | S | D | Com |
| 42 | tonerDensityRequested | I |
|  | >1 |
|  | M | S | S | a |
| 43 | tonerDensityUsed | I |
|  | >1 |
|  | A | S | D | Com |
|  | Job Progress attributes (requested and consumed) |
| 44 | jobCopiesRequested | I |
| M | S | S P | a |
| 45 | jobCopiesCompleted | I |
| MA | D | D | Pri Can Com |
| 46 | documentCopiesRequested | I |
| M | S | S P D | a |
| 47 | documentCopiesCompleted | I |
| MA | D | D | Pri Can Com |
| 48 | jobKOctetsRequested | I |
| M |
|  | S | M | S | S P | a |
| 49 | jobKOctetsTransferred | I |
| M | D | S | Pen |
| 50 | jobKOctetsCompleted | I |
| M |
|  | S | MA | D | D | Pri Can Com |
|  | Impression attributes (requested and consumed) |
| 51 | impressionsSpooled | I |
| M | D | S | Pen |
| 52 | impressionsSentToDevice | I |
| M | D | S | Pen |
| 53 | impressionsInterpreted | I |
| M | D | D | Pro |
| 54 | impressionsRequested | I |
| M |
|  | S | M | S | S | a |
| 55 | impressionsCompleted | I |
| M |
|  | S | MA | D | D | Pri Can Com |
| 56 | impressionsCompletedCurrentCopy | I |
| M | D | D | Pri Can Com |
|  | Page attributes (requested and consumed) |
| 57 | pagesRequested | I |
| M | S | S P D | a |
| 58 | pagesCompleted | I |
| MA | D | D | Pri Can Com |
| 59 | pagesCompletedCurrentCopy | I |
| M | D | D | Pri Can Com |
|  | Sheet attributes (requested and consumed) |
| 60 | sheetsRequested | I |
| M | S | S P D | a |
| 61 | sheetsCompleted | I |
| MA | D | D | Pri Can Com |
| 62 | sheetsCompletedCurrentCopy | I |
| M | D | D | Pri Can Com |
|  | Resource attributes (requested and consumed) |
| 63 | mediumRequestedType | I | TC |
| >1 |
|  | M | S | S P D | a |
| 64 | mediumRequestedName | O |
|  | >1 |
|  | M | S | S P D | a |
| 65 | mediumConsumedName | I+O |
|  | >1 |
|  | MA | D | D | Pri Can Com |
| 66 | colorantRequestedIndex | I |
|  | >1 | L |
| M | S | S P D | a |
| 67 | colorantRequestedName | O |
|  | >1 |
|  | M | S | S P D | a |
| 68 | colorantConsumedIndex | I+O |
|  | >1 | L |
| MA | S | D | Pri Can Com |
| 69 | colorantConsumedName | O |
|  | >1 |
|  | MA | D | D | Pri Can Com |
|  | Time attributes (set by server or device) |
| 70 | jobSubmissionToServerDateAndTime | O |
| MA | S | S | a |
| 71 | jobSubmissionToDeviceDateAndTime | O |
| MA | S | S | a |
| 72 | jobSubmissionToDeviceTimeStamp | I |
| MA | S | S | a |
| 73 | jobStartedBeingHeldTimeStamp | I |
|  | S | M | S | S | a |
| 74 | jobStartedProcessingDateAndTime | O |
| MA | S | P | a |
| 75 | jobStartedProcessingTimeStamp | I |
| MA | S | P | a |
| 76 | jobCompletedDateAndTime | O |
| MA | S | C | Can? Com |
| 77 | jobCompletedTimeStamp | I |
| MA | S | C | Can? Com |
| 78 | jobProcessingCPUTime | I |
| MA | D | D | a |