Table of Aspect Ratio Modes

Rick Landau, Dell

v0.1 20061201

Incoming images and displays exist in a number of different aspect ratios, including but not limited to:

- 4:3

- 5:4

- 16:9

- 16:10

To display a logical image of one aspect ratio on a physical display of another aspect ratio, the video processing may use one or more of several functions.

- 1:1 or "postage stamp" mapping: display the logical image pixel-for-pixel on the physical display; the image may be centered within the display.

- shrink/expand preserving the aspect ratio: change the size of the logical image to fit some dimension of the physical display.  Note that 1:1 is simply this function with no scaling.

- stretch/distort, scale anamorphically not preserving the aspect ratio: scale vertical and horizontal dimensions differently to fit some dimensions of the physical display.

- crop: remove some pixels of the logical image to fit some dimension of the physical display.

- pad: add black pixels to the edges of the logical image to fit some dimension of the physical display.

We attempted to analyze all the known aspect ratio modes using combinations of these functions.

| Aspect Ratio Mode uses Functions | shrink / expand, preserving aspect ratio | stretch / distort, changing aspect ratio | crop | pad |
| --- | --- | --- | --- | --- |
| 4:3 window | no scaling, display image at 100% |  |  | pad H and V if needed to center image |
| 1.33 | 4:3 image, fill 4:3 display |  |  |  |
| letterbox | fit image H to display H |  |  | pad to center V |
| widescreen |  | stretch/distort 4:3 image onto 16:9 display in both V and H |  |  |
| 1.78 | 16:9 image onto 16:9 display V and H |  |  |  |
| crop | 16:9 image onto 4:3 display, fit V |  | H now wider than display, crop to retain center |  |
| 1.85 | remove letterboxing, fit non-blank V to display V |  | H now wider than display, crop to retain center |  |
| 4:3 fill |  | stretch/distort any image onto 4:3 display |  |  |
| 2.35:1 | remove letterboxing, fit non-blank V to display V |  | H now wider than display, crop to retain center |  |
| normal | image "best fit" to display, H or V whichever is less |  |  | pad H or V as needed to center |
| full |  | stretch/distort any image onto any display |  |  |
| zoom | user-selected magnification factor |  | display acts as movable window on large virtual image, cropping H and V |  |
| cinema |  | same as "widescreen" |  |  |
| v-zoom |  | same as "full" |  |  |
| stadium | fit image V onto display V | nonlinearly stretch edges of image H, outside center 50% approx., to fill display H |  |  |